# Poles, Ducts, and Rights of Way (PDR) Microduct

### Description

PDR microduct technology is an alternative solution to the current innerduct technology.   Microduct is a smaller version of innerduct that must be placed inside an innerduct.  Available duct capacity is increased since up to four (4) microducts can be placed within a 1¼-inch innerduct.

#### Terms and Conditions

You will be required to have an Interconnection Agreement with CenturyLink prior to a submitting a request for microduct.  If the Interconnection Agreement does not include the rate elements for microduct, the Interconnection Agreement must be amended prior to submitting a PDR microduct request. The process for obtaining an Interconnection Agreement or amending an existing agreement is located at www.qwest.com/wholesale/clecs/clec_index.html.

The availability of microduct can be categorized into the following scenarios:

- In cities where CenturyLink has deployed microduct technology, you may lease available vacant microduct.

- In cities where CenturyLink has deployed microduct technology and existing microducts are occupied, you have the option to ask CenturyLink to place microduct along the desired route or you can choose to place microduct if it meets CenturyLink specifications (see below).

- In cities where CenturyLink has deployed microduct technology and CenturyLink has not yet placed microduct, you have the option to ask CenturyLink to place microduct along the desired route or you can choose to place microduct if it meets CenturyLink specifications (see below).

- In cities where CenturyLink has not deployed microduct and you wish to use this technology, you must lease an innerduct.  In these locations you will be required to furnish and place the microduct.   At the conclusion of the lease, you and CenturyLink will make a joint decision whether or not you will be required to remove your microduct from the innerduct.  If you choose to leave the microduct and it does not meet CenturyLink current standards, you will be charged for the removal costs.

CenturyLink microduct specifications are as follows:

- A standard 12/10-millimeter (outside/inside diameter) microduct.  Microduct color-coding must be consistent with the Suggested Optical Cable Code (SOCC) as contained in Telcordia’s standard document SR2014.

- If the innerduct is 1¼-inch in diameter, a maximum of four (4) microducts must be placed in the innerduct.

- If the innerduct is one (1) inch in diameter, a maximum of three (3) microducts must be placed in the innerduct.

- CenturyLink must retain one (1) microduct for maintenance.

- Microducts not occupied by you will vest to CenturyLink.

- Microduct can never be directly buried.

- Placement must be in an approved innerduct that is suited for the environment.

Unless otherwise stated above, the duct/conduit/innerduct terms and conditions as described in Section 10.8 of the SGAT for the relevant state also apply to microduct.

Rate Elements

You will be charged, if applicable, the non-recurring charges for Innerduct Inquiry, Field Verification, Planner Verification, Manhole Verification, Manhole Make-Ready, Make Ready and/or Poles/Ducts/ROW Transfer of Responsibility Fees as reflected in Exhibit A.

Microduct Occupancy Fee.  This recurring charge is billed annually per microduct, per foot.

Ordering

The PDR microduct process is the same as the existing duct/innerduct process.  See the Preordering and Ordering sections in the General PDR PCAT for the process with the following exceptions:

- The Attachment 2 form will indicate the recurring charge for microduct if this technology was requested and available.  Click here to view the Attachment 2 form.