To: 	 	Bill Difference Distribution Group

# From:		Jana Charles

Date:		June 1, 2012

Subject:	BOS Version 52 Differences List - Initial

Following is the BOS Version 52 Bill Differences List for CenturyLink.  BOS Version 52 is scheduled for installation into IABS production with Release 48.00 on November 17, 2012.

The following details, by item number, what CenturyLink will be doing for BOS V52:

Item AA – With the change from BOS Version 51 to 52, the data element Version Number needs to be updated to reflect the newer version in the following header records:

| Record Identification | Data Element | Position |
| --- | --- | --- |
| 10-01-01-00 | Version Number | 83-85 (populate 520) |
| 30-01-01-00 | Version Number | 83-85 (populate 520) |
| 40-01-01-00 | Version Number | 83-85 (populate 520) |

IABS will update the Version Number data element in the records (as provided above) to be standard with V52 record production.

Item 1 – PCP-Intrastate

This item creates a new data element, Price Cap Percent-Intrastate. It provides companies, who have a need, the ability to display the Price Cap Percent (PCP) as it is applied to intrastate services.

The following record has been modified to accommodate the new data element:

| Record Identification | Data Element | Position | Field Characteristic | Comments |
| --- | --- | --- | --- | --- |
| 40-15-21-00 | Reserved | 158-159 | X(2) | Populate with spaces |
| 40-15-21-00 | Price Cap Percent-Intrastate | 160-162 | 9(3) | Populate with the default value of 999 |

There is no requirement to use the new data element. IABS will update the record, using the default value for the new data element (as detailed above), to be standard with V52 record production.

Item 2 – Miscellaneous Element “Get Data” Clarification

This item updates various existing data elements to include tariff equivalents that are also specifically referenced in the description of various phrase codes. Introductory text in Volume 4 has also been updated to include additional verbiage.

The verbiage (i.e., Switchway, Switchnet, PSDS) has been added to the Switched 56 KBPS data elements:

End Office Element

Value 30

End Office Traffic Type Ind

Value 10

Value 11

Local Transport Element

Value 21

Value 36

Miscellaneous Element

Value 16

Operator Services Type Ind

Value 2

Statistics Element

Value 13

Value 74

Value 79

Unbundled Common Line Element

Value 05

Unbundled End Office Traffic Type Ind

Value 15

Unbundled Transport Element

Value 10

The following update has been made to Volume 4, Section 2.4 – Additional Information:

It should be noted that the descriptions for the valid values are typically generic in nature and may be substituted with the appropriate tariffed language. If specific tariff-equivalent language is referenced in Volume 1A of these Specifications, it is reflected in parenthesis.

Documentation change only.

Item 3- Correction to Reference Value Field Length

This item corrects the record positions for the element Reference Value on the 10-33-04-50 record as follows:

| Record Identification | Data Element | Position | Field Characteristic | Comments |
| --- | --- | --- | --- | --- |
| 10-33-04-50 | Reference Value | 179-189 | X(11) | Record not produced |
|  | Reserved | 190-213 | X(24) | Record not produced |

10-33-04-50 record not produced in IABS – no action required.

The following changes were made with the CABS Dot Release 51.1 which was done as a result of the FCC’s Report and Order and Further Notice of Proposed Rulemaking, Docket 11-161. CenturyLink will be incorporating the changes for Version 51.1 concurrent with the changes that are being made with BOS V52.

Item 1A

New data elements have been created for use on the usage detail, usage statistics and OCC records in order to allow a company to provide information for VoIP Usage. The following data elements have been created:

Percent VoIP Usage

Percent VoIP Usage – Customer

Percent VoIP Usage – Provider

PVU Source Ind

VoIP Usage Ind

Additionally, the text has been updated in Volume 1 (section 20.49A) to provide information related to the PVU as it pertains to the detail of usage statistics bill section:

Percent VoIP Usage

| 20.49A | The Percent VoIP Usage Factor (PVU) can be provided by Exchange Carriers (PUP), their customers (PUC), or represent an aggregation of both. At minimum, the PVU must be displayed if VoIP usage is billed under the Detail of Usage section. Presentation of a customer provided, or Exchange Carrier provided factor is dependent on local business policy or a company’s tariff requirements. |  |
| --- | --- | --- |

The following records have been modified to accommodate the new VoIP data elements:

| Record Identification | Data Element | Position | Field Characteristic | Comments |
| --- | --- | --- | --- | --- |
| 10-30-05-00 | PVU Source Ind | 167 | X(1) | Populate with the default value of 0 |
|  | Percent VoIP Usage | 168-172 | 9(3)V9(2) | Populate with the default value of 00000 |
|  | Reserved | 173-223 | X(51) | Populate with spaces |
| 10-30-10-00 | PVU Source Ind | 145 | X(1) | Populate with the default value of 0 |
|  | Percent VoIP Usage | 146-150 | 9(3)V9(2) | Populate with the default value of 00000 |
|  | Reserved | 151-223 | X(73) | Populate with spaces |
| 10-30-15-02 | PVU Source Ind | 161 | X(1) | Populate with the default value of 0 |
|  | Percent VoIP Usage | 162-166 | 9(3)V9(2) | Populate with the default value of 00000 |
|  | Reserved | 167-225 | X(60) | Populate with spaces |
| 10-30-20-01 | Reserved | 130-133 | X(4) | Reserved |
|  | PVU Source Ind | 134 | X(1) | Populate with the default value of 0 |
|  | Percent VoIP Usage | 135-139 | 9(3)V9(2) | Populate with the default value of 00000 |
|  | Reserved | 140-225 | X(86) | Reserved |
| 10-35-05-01 | VoIP Usage Ind | 148 | X(1) | Populate with the default value of 0 |
|  | Reserved | 149-150 | X(2) | Populate with spaces |
| 10-35-10-00 | VoIP Usage Ind | 118 | X(1) | Populate with the default value of 0 |
|  | Reserved | 119 | X(1) | Populate with spaces |
| 10-35-15-00 | VoIP Usage Ind | 216 | X(1) | Populate with the default value of 0 |
| 10-35-20-00 | VoIP Usage Ind | 139 | X(1) | Populate with the default value of 0 |
|  | Reserved | 140-149 | X(10) | Populate with spaces |
| 10-35-27-02 | VoIP Usage Ind | 88 | X(1) | Populate with the default value of 0 |
|  | Percent VoIP Usage | 88-93 | 9(3)V9(2) | Populate with the default value of 00000 |
|  | PVU Source Ind | 94 | X(1) | Populate with the default value of 0 |
|  | Reserved | 95-104 | X(10) | Populate with spaces |
| 10-37-05-00 | VoIP Usage Ind | 205 | X(1) | Populate with the default value of 0 |
|  | Reserved | 206 | X(1) | Populate with spaces |
| 10-37-10-00 | VoIP Usage Ind | 185 | X(1) | Populate with the default value of 0 |
|  | Reserved | 186-222 | X(37) | Populate with spaces |
| 10-37-15-00 | VoIP Usage Ind | 172 | X(1) | Populate with the default value of 0 |
|  | Reserved | 173-224 | X(50) | Populate with spaces |
| 10-37-20-00 | VoIP Usage Ind | 211 | X(1) | Populate with the default value of 0 |
|  | Reserved | 212-213 | X(2) | Populate with spaces |
| 10-37-27-00 | VoIP Usage Ind | 206 | X(1) | Populate with the default value of 0 |
|  | Percent VoIP Usage | 207-211 | 9(3)V9(2) | Populate with the default value of 00000 |
|  | PVU Source Ind | 212 | X(1) | Populate with the default value of 0 |
|  | Reserved | 213 | X(1) | Populate with spaces |

IABS will update the records, using the default value for the new data elements (as detailed above), to be standard with V52 record production

Default values will be used in the usage detail and statistics records until the system changes requested with CR 30004 are implemented. Once the system changes are in place the default values will be replaced by actual values (as available).

In addition to the changes on the existing records to accommodate the new VoIP data elements, a new statistics detail record has been created for Wireless usage (10-37-27-50) which houses the new VoIP data elements.

The layout for the new wireless stats record (10-37-27-50):

| Element Name | Field Length | Record Position | Field Characteristics |
| --- | --- | --- | --- |
| Record Identification | 6 | 1-6 | X(6) |
| Record Identification Suffix | 2 | 7-8 | 9(2) |
| Suffix Record Ind | 1 | 9 | 9(1) |
| Access Customer Name Abbreviation | 5 | 10-14 | X(5) |
| Bill Date | 8 | 15-22 | X(8) (CCYYMMDD) |
| Billing Number | 10 | 23-32 | X(10) |
| Customer Code | 3 | 33-35 | X(3) |
| Pack Sequence Number | 4 | 36-39 | 9(4) |
| Record Sequence Number | 9 | 40-48 | 9(9) |
| Reserved for EC Use | 13 | 49-61 | X(13) |
| Summary Office Identification | 11 | 62-72 | X(11) (CLLI) |
| Summary Office ID Ind | 1 | 73 | X(1) |
| Wireless Statistics Element | 2 | 74-75 | X(2) |
| Percent VoIP Usage – Customer | 5 | 76-80 | 9(3)V9(2) |
| Percent VoIP Usage – Provider | 5 | 81-85 | 9(3)V9(2) |
| Reserved | 139 | 86-225 | X(139) |

No requirement to produce this record w/ implementation of BOS V52. CenturyLink will not be providing separate percentages for customer/provider. The PVU Source Ind will be used to identify the source of the PVU when we are able to process the usage.

New Phrase Code

784 – Adjustment of VoIP Usage

This phrase will be used to adjust previously billed VoIP usage

IABS Tables will be updated with the appropriate tables (e.g. XX1TIAPT, XX1TICPT, etc.) to add the phrase code.  IABS User Guide will be updated to reflect the new code.

Differences in the records or data elements specific to UNE-P (Type of Account J) and unbundled loop (Type of Account N) are listed separately and uniquely identified.

Note 1: For UNE-P (Type of Accounts J) and Unbundled Loop (Type of Account N) accounts produced in the Eastern region, the amount reflected in Monthly Charges Total (position 137-147) on the 10-05-12-00 record may not match the CSR Account Total (position 62-72) amount on the 40-15-35-00 record if orders removing service (Disconnect and From order types) have been completed during the current bill cycle.  The originating system does not produce the bill data for a CKT (unbundled loop) or TN (UNE-P) that has been disconnected, therefore no bill CABS BOS records (10 series) can be created.  The Monthly Charges Total will include the prorated (fractionalized) monthly charge for the service that has been removed.

This information is provided as a courtesy to our customers who expect the two totals to match.  Please be aware there is no requirement in the CABS/BOS documentation that requires a cross-balance between bill and CSR data.

Note 2: For UNE-P (Type of Account J) accounts produced in the Central region, the appearance of the USOC SUS (suspension of service at customer’s request) may result in the amount reflected in Monthly Charges Total (position 137-147) on the 10-05-12-00 record not matching the CSR Account Total (position 62-72) amount on the 40-15-35-00 record.  The difference between the two amounts is due to the monthly rate reflecting the full rate for the CSR and ½ rate (the suspension rate) for the bill.  The amount shown in the Monthly Charges Total matches the amount present on the CRIS paper bill.

Note 3: For UNE-P (Type of Account J) in the Western Region, the 10-30-10-00 record will contain 0’s for the OC&C Heading element (positions 77-126) when the OCC&C Heading Identifier element (positions 77-76) is a TN as the telephone number is not being provided by the originating system with the OC&C detail.  The TN will not be provided in the Eastern Region for those accounts which have only a single line (a TN will be provided in the 10-30-10-00 record for multi-line accounts).

For Unbundled Loop (Type of Account N) in all three Regions, the 10-30-10-00 record will contain either the Circuit-Id or the literal ‘UNBUNLED SERVICES’ in the OC&C heading element (position 77-126) when the OC&C Heading Identifier element (positions 72-76) is CLS as the Circuit ID is not provided by the originating system in the OC&C detail.

Note 4: For UNE-P (Type of Accounts J) and Unbundled Loop (Type of Account N) accounts the Invoice Number (positions 62-76) on the 10-25-05-00 Detail Balance Due Record will be populated with the default value of spaces because the originating billing system does not provide the bill detail by invoice number.  Additionally, the data elements of Detail Payments Applied (position 128-138) and Detail Adjustments Applied (position 139-149) will always be populated with zeros.

Note 5: For UNE-P (Type of Account J) and Unbundled Loop (Type of Account N) in all three Regions the Service Established Date (SED) passed in the 40-15-05 record for a left-handed FID (i.e. TN, CLS, CKL) may be greater than the SED value passed in the 40-15-10 record for the associated USOC.   BOS edit CER150500.01 which states the SED on the 40-15-05 (for the left-handed FID) will be less than or equal to the SED on the 40-15-10 (for the USOC) will not be enforced for UNE accounts.

If you have any further questions, please call me at (303) 992-8448.

Thank you,

Jana Charles

SR Software Developer

Info Technology

CenturyLink

| Record Name | Record ID | Record Positions | Status | Standard Version | Explanation of Difference | Item Impl Date |
| --- | --- | --- | --- | --- | --- | --- |
| OC&C SO/ Trans ID | 10-30-05-00 |  | 5 |  | Multiple Rate/BIP changes will not produce 10-30-05 on listing of USOCs | 3/1/90 |
| Resale Usage | 10-36-04 Thru 10-36-29 | 1-225 | 3 |  | Resale not mechanized in IABS |  |
| Packet Switching Transport Usage | 10-38-05 Thru 10-42-05 | 1-225 | 3 |  | Digipac (Packet Switching) not mechanized in IABS |  |
| Primary Interexchange Carrier Line Header | 30-01-01-00 | 47 | 5 |  | PICC True-up File X(1) CenturyLink will populate T in position 47 to indicate PICC verification file | 1/20/99 |

| Data Element Name | Status | Standard | Explanation of Difference | Item Impl Date |
| --- | --- | --- | --- | --- |
| Account Date | 3 |  | Contains bill date not extract date | 03/01/90 |
| Acct Tax Codes | 3 |  | Account level exemptions override USOC level taxability codes | 01/01/84 |
| Activity Date | 3 |  | SO Completion date instead of EBD when present | 03/01/90 |
| Adjustment Amount | 5 |  | Each taxable adjustment has a separate tax adjustment with the same audit number. Adj amt on the paper bill includes the assoc tax adjustment amount. | 03/01/90 |
| Bill Type | 5 |  | Value ‘4’ will not be implemented at this time until further clarification is received from customers | 11/15/97 |
| Circuit ID Tel Number | 3 |  | FGA Inventory is in WATS format. TN overrides TLI, then TER data and blanks. | 03/01/90 |
| Discount Factor Interstate | 3 |  | Not provided - see Interstate-Unit-Rate note | 11/19/94 |
| Discount Factor Intrastate | 3 |  | Not provided - see Intrastate-Unit-Rate note | 11/19/94 |
| Due By Date | 5 |  | If Hold bill and Due By Date changes, released BDT reflects new Due By Date. | 03/01/90 |
| Interstate Unit Rate | 5 |  | Except for the FTS 2000 plan, contains the rate after any discounts or is the grandfathered rate rather than tariff rate. | 11/19/94 |
| Intrastate Unit Rate | 5 |  | Except for the FTS 2000 plan, contains the rate after any discounts or is the grandfathered rate rather than tariff rate. | 11/19/94 |
| Service Established Date | 3 |  | When present, EBD posts in Service Established Date field. SED floats behind USOCs | 03/01/90 |
| Total Number of Switched Channels | 5 |  | Includes channel totals with SBAN and HBAN references | 11/19/94 |
| USOC or FID | 5 |  | BAN level FIDs, TAX, BIP and other FID/USOCs posted to deployed equipment appear in the CSR Glossary even if not appearing on the CSR. | 03/01/90 |

| Data Element Name | Status | Standard | Explanation of Difference | Item Impl Date |
| --- | --- | --- | --- | --- |
| The Elements differences listed below pertain to UNE BDT output only. |  |  |  |  |
| Activity Date | 5 |  | Bill Processing Date will be populated in Activity Date | 07/01/02 |
| Adjustment Thru Date | 5 |  | Will contain the current bill date when Adjustment Thru date is not available | 07/01/02 |
| Adjustment From Date | 5 |  | Will contain the current bill date when Adjustment From date is not available | 07/01/02 |
| Audit Number | 5 |  | Will contain zeros. | 07/01/02 |
| Circuit Format Ind | 5 |  | Will contain spaces | 07/01/02 |
| CSR Account Total | 5 |  | May not match amount for Monthly Charges Total. Refer to Notes 1, 2 (above) for details. | 05/09/03 |
| Invoice Number | 5 |  | Will contain spaces. Refer to Note 4 | 10/08/05 |
| Monthly Charges Tax | 5 |  | Will contain zeros. | 07/01/02 |
| Monthly Charges Total | 5 |  | May not match amount for CSR Account Total. Refer to Notes 1, 2 (above) for details. | 05/09/03 |
| Other Tax | 5 |  | Will contain zeros. | 07/01/02 |
| Recurring/Non-recurring Charge Ind | 5 |  | Will always contain a value of ‘1’ for Adjustments | 07/01/02 |
| Service Established Date | 5 |  | Bill Processing Date will be populated in Service Established Date field. | 07/01/02 |
| Service Established Date | 5 |  | SED passed on the 40-15-05 record for left handed FID may be greater than the SED passed on the 40-15-10 for the associated USOC. Refer to Note 5 | 10/13/05 |
| Total Taxes | 5 |  | Will include Surcharges when present. | 07/01/02 |
| Usage Rate | 5 |  | May contain zeros when data is unavailable. | 07/01/02 |
| Usage Tax | 5 |  | Will contain zeros. | 07/01/02 |
| USOC/FID Ind | 5 |  | Will always contain the value of “2”, indicating USOC. FID information is not available from the originating system. | 07/01/02 |

| Phrase Code | Phrase | Status | Standard Version | Explanation of Difference | Item Implementation Date |
| --- | --- | --- | --- | --- | --- |
| 782 | Credit for VoIP Access | 4 | 52 | Phrase for Credit for VoIP Access | 07/14/12 |
| 783 | Adjustment of VoIP Access Credit | 4 | 52 | Phrase for Adjustment of VoIP Access Credit | 07/14/12 |
| 785 | Credit for VoIP Switched Facility Access | 4 | 52 | Phrase for Credit for VoIP Switched Facility Access | 07/14/12 |
| 786 | Adjustment of VoIP Switched Facility Access | 4 | 52 | Phrase for Adjustment of VoIP Switched Facility Access | 07/14/12 |
| X01 | Charge to Meet Early Termination at 50% of Monthly Rate | 5 |  | Local Use Phrase | 1990 |
| X21 | Adjustment of Colorado Universal Service Charge | 1 |  | Local Use Phrase – used to adjust Universal Service charges in Colorado | 3/20/99 |
| X41 | Adjustment of RCP Shortfall Charge – DS3 | 5 |  | Local Use Phrase – used to distinguish RCP Adjustment of shortfall charge for DS3 from DS1 | 07/17/06 |
| X42 | Credit for Regional Commitment Program (RCP) – DS3 | 5 |  | Local Use Phrase – used to distinguish RCP Credit for DS3 from DS1 | 07/17/06 |
| X43 | Adjustment of Regional Commitment Program (RCP) Credit – DS3 | 5 |  | Local Use Phrase – used to distinguish RCP Adjustment of credit for DS3 from DS1 | 07/17/06 |
| X44 | Charge for RCP Shortfall – DS3 | 5 |  | Local Use Phrase – used to distinguish RCP shortfall for DS3 from DS1 | 07/17/06 |
| X45 | Charge for DS1 Service – National Convention | 5 |  | Local Use Phrase – used to identify charges (one time and/or monthly) for DS1 services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X46 | Credit for DS1 Service – National Convention | 5 |  | Local Use Phrase – used to identify credits (one time and/or monthly) for DS1 services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X47 | Charge for DS1 Service Move/Change – National Convention | 5 |  | Local Use Phrase – used to identify move/change charges for DS1 services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X48 | Charge for DS1 Service Cancellation – National Convention | 5 |  | Local Use Phrase – used to identify cancellation charges for DS1 services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X49 | Charge for DS3 Service – National Convention | 5 |  | Local Use Phrase – used to identify charges (one time and/or monthly) for DS3 services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X50 | Credit for DS3 Service – National Convention | 5 |  | Local Use Phrase – used to identify credits (one time and/or monthly) for DS3 services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X51 | Charge for DS3 Service Move/Change – National Convention | 5 |  | Local Use Phrase – used to identify move/change charges for DS3 services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X52 | Charge for DS3 Service Cancellation – National Convention | 5 |  | Local Use Phrase – used to identify cancellation charges for DS3 services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X53 | Charge for Broadcast Service – National Convention | 5 |  | Local Use Phrase – used to identify charges (one time and/or monthly) for Broadcast services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X54 | Credit for Broadcast Service – National Convention | 5 |  | Local Use Phrase – used to identify credits (one time and/or monthly) for Broadcast services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X55 | Charge for Broadcast Service Move/Change National Convention | 5 |  | Local Use Phrase – used to identify move/change charges for Broadcast services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X56 | Charge for Broadcast Service Cancellation – National Convention | 5 |  | Local Use Phrase – used to identify cancellation charges for Broadcast services specific to a National Convention (democratic or Republican) | 8/1/2008 |
| X57 | Charge for HDTV Service – National Convention | 5 |  | Local Use Phrase – used to identify charges (one time and/or monthly) for HDTV services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X58 | Credit for HDTV Service – National Convention | 5 |  | Local Use Phrase – used to identify credits (one time and/or monthly) for HDTV services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X59 | Charge for HDTV Service Move/Change – National Convention | 5 |  | Local Use Phrase – used to identify move/change charges for HDTV services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| X60 | Charge for HDTV Service Cancellation – National Convention | 5 |  | Local Use Phrase – used to identify cancellation charges for HDTV services specific to a National Convention (Democratic or Republican) | 8/1/2008 |
| The Phrase Codes listed below pertain to UNE BDT output only. |  |  |  |  |  |
| X15 | Charge for Unbundled Services | 5 |  | Local Use Phrase for Unbundled products’ OC&C’s | 07/01/02 |
| X18 | Adjustment for Unbundled Services | 5 |  | Local Use Phrase for Unbundled Products’ Adjustments | 07/01/02 |
| X40 | Credit for One-Time Charges | 5 |  | Local Use Phrase for Unbundled Products’ Adjustments | 12/25/02 |