Local Response (LR)
 Form Preparation Guide

# V49.0

# TABLE OF CONTENTS

SECTION										PAGE

HISTORY LOG	7

1.	GENERAL SECTION	7

2.	LR FORM DESCRIPTION	8

2.1	FIRM ORDER CONFIRMATION	8

2.2	ERROR/REJECT/JEOPARDY	9

2.3	COMPLETION	9

2.4	FACLITY BASED DIRECTORY LISTINGS (FBDL) NOTICES	10

3.	LR matricies	10

3.a	LR Matrix for Bulk Confirmation	13

4.	LR DATA ELEMENTS	15

4.1	ADMINISTRATIVE SECTION	15

1.	CCNA - Customer Carrier Name Abbreviation	15

1a.	CC - Company Code – CenturyLink-Specific Field	16

2.	PON - Purchase Order Number	17

3.	VER – Version Identification	18

4.	AN – Account Number	19

5.	ATN – Account Telephone Number – Not currently used by CenturyLink	20

6.	LSR NO – Local Service Request Number	21

7.	ORD – Order Number – Not currently used by CenturyLink	22

4.2	CLEC INFORMATION SECTION	23

8.	CNO – Case Number – Not currently used by CenturyLink	23

9.	INIT – Initiator Identification	24

10.	PG_of_ – Page _ of _ - Not currently used by CenturyLink	25

11.	D/TSENT – Date and Time Sent	26

11a.	CLECD/TSENT – CLEC Date and Time Sent – CenturyLink-Specific  Field	27

11b.	LSRREMARKS – Remarks – CenturyLink-Specific Field	28

12.	REP – Provider Contact Representative	30

13.	ST – Switch Type – Not currently used by CenturyLink	31

14.	IBT – ISDN BRI Type – Not currently used by CenturyLink	32

15.	TEL NO – Telephone Number	33

16.	RT – Response Type	34

4.3	LSR PIA SECTION	36

17.	PIA - Provider Initiated Activity	36

17a.	LSR PIA REMARKS – LSR Level PIA Remarks Other – CenturyLink-Specific Field	37

17a1.	LSR PIA REMARKS 2 – LSR Level PIA Remarks Other 2 – CenturyLink-Specific Field – GUI Only	38

17a2.	LSR PIA REMARKS 3 – LSR Level PIA Remarks Other 3 – CenturyLink-Specific Field – GUI Only	39

4.4	ERROR/REJECT SECTION	40

17b.	ERROR/REJECT CODE – Error or Reject Code – CenturyLink-Specific  Field	40

17c.	ERROR/REJECT DESCRIPTION – Error or Reject Description – CenturyLink-Specific Field	43

17d.	DIDNUM – Direct Inward Dial Reference Number – CenturyLink-Specific  Field	44

4.5	CENTURYLINK ORDER INFORMATION SECTION	45

17e.	FOC IND – Firm Order Confirmation Indicator – CenturyLink-Specific  Field	45

17f.	OREF NUM – Order Reference Number – CenturyLink-Specific Field	46

17g.	ORD – Order – CenturyLink-Specific Field	47

17h.	CD – Completion Date – CenturyLink-Specific Field	48

17i.	AN – Account Number – CenturyLink-Specific Field	49

17j.	ORD IND – Order Indicator – CenturyLink-Specific Field	50

17k.	ST – Switch Type – CenturyLink-Specific Field	51

17l.	IBT – ISDN BRI Type – CenturyLink-Specific Field	52

18.	DD - Due Date	53

18a.	DLQTYR - Number of Listings Received – CenturyLink-Specific Field	54

4.6	JEOPARDY STATUS	55

18b.	RCODE - Reason Code – CenturyLink-Specific Field	55

18c.	RDET - Reason Jeopardy Code Detail – CenturyLink-Specific Field	57

18d.	ESDD - Estimated Due Date – CenturyLink-Specific Field	61

18e.	AFVR - Additional Field Visit Required – CenturyLink-Specific Field	62

18f.	FDT - Frame Due Time – CenturyLink-Specific Field	63

19.	CHC - Coordinated Hot Cut	64

19a.	APPTIME – Appointment Time – CenturyLink-Specific Field	65

4.7	ORDER PIA SECTION	66

19b.	PIA - Provider Initiated Activity – CenturyLink-Specific Field	66

19c.	ORDER-PIA-REMARKS – Order Level PIA Remarks Other –  CenturyLink-Specific Field	67

19c1.	ORDER PIA REMARKS 2 – Order Level PIA Remarks Other 2 –	68

CenturyLink-Specific Field – GUI Only	68

19c2.	ORDER PIA REMARKS 3 – Order Level PIA Remarks Other 3 –	69

CenturyLink-Specific Field – GUI Only	69

20.	EBD - Effective Bill Date – Not currently used by CenturyLink	70

4.8	LINE INFORMATION SECTION	71

20a.	AN – Account Number – CenturyLink-Specific Field	71

20b.	LNUM – Line Number – CenturyLink-Specific Field	76

20c.	TNS - Telephone Numbers – CenturyLink-Specific Field	77

21.	DRTN - Distinctive Ring Telephone Number	78

22.	MATN - Main/Alternate Telephone Number	79

23.	ISPID - ISDN Service Profile Identification	80

23a.	HID – Hunt Group Identifier – CenturyLink-Specific Field	81

23b.	TLI – Telephone Line Identifier– CenturyLink-Specific Field	82

24.	TERS - Terminal Numbers	83

25.	PORTED NBR - Ported Telephone Number	84

26.	RTI - Route Index – Not Currently used by CenturyLink	85

27.	DISC NBR - Disconnect Telephone Number – Not currently used by CenturyLink	86

27a.	ECCKT – Exchange Company Circuit ID – CenturyLink-Specific Field	87

27b.	SAT - Subscriber Access Telephone Number – CenturyLink-Specific Field	93

28.	CKR - Customer Circuit Reference	94

28a.	CFA - Connecting Facility Assignment – CenturyLink-Specific Field	95

28b.	SEC CFA – Secondary Connecting Facility Assignment – CenturyLink-Specific Field	97

28c.	LOCNUM - Location Number – CenturyLink-Specific Field	98

4.9	DID DETAILS SECTION – CENTURYLINK - SPECIFIC SECTION	99

29.	DSTN - Disassociated Telephone Number – Not currently used by CenturyLink	99

29a.	DTLI - DID Telephone Line Identifier – CenturyLink-Specific Field	100

29b.	DTK - DID Trunk Quantity – CenturyLink-Specific Field	101

29c.	DTGN - DID Trunk Group Number – CenturyLink-Specific Field	102

29d.	DRTI - DID Route Index Number – CenturyLink-Specific Field	103

29e.	DTKID - DID Trunk ID – CenturyLink-Specific Field	104

29f.	DGOUT - DID Digits Out – CenturyLink-Specific Field	105

29g.	DTNR - DID Telephone Number Range – CenturyLink-Specific Field	106

4.10	VIRTUAL RELATED CIRCUIT DETAIL	107

29h.	LST – Local Service Termination – CenturyLink-Specific Field	107

29i.	LNEX- Line Number Extension Number – CenturyLink-Specific Field	108

29j.	DLCI - Data Link Connection Identifier – CenturyLink-Specific Field	109

29k.	CIR – Committed Information Rate – CenturyLink-Specific Field	110

29l.	Be – Excess Burst Size – CenturyLink-Specific Field	111

29m.	RPON – Related Purchase Order Number – CenturyLink-Specific Field	112

29n.	RECCKT - Related Exchange Company Circuit Identification –  CenturyLink-Specific Field	113

29o.	RORD – Related Order Number – CenturyLink-Specific Field	114

29p.	RDLCI - Related Data Link Connection Identifier – CenturyLink-Specific  Field	115

30.	BI1 - Billing Account Number Identifier 1	116

31.	BAN1 - Billing Account Number 1	117

32.	BI2 - Billing Account Number Identifier 2	118

33.	BAN2 - Billing Account Number 2	119

34.	EC VER - Exchange Carrier Version	120

35.	RCODE - Reason Code – Not currently used by CenturyLink	121

36.	RDET - Reason Jeopardy Code Detail – Not currently used by  CenturyLink	122

37.	ESDD - Estimated Due Date – Not currently used by CenturyLink	123

38.	AFVR - Additional Field Visit Required – Not currently used by  CenturyLink	124

39.	DSGCON - Design/Engineering Contact	125

40.	NSP DSGCON -Network Service Provider (NSP) Design/Engineering  Contact	126

41.	TEL NO - Telephone Number	127

42.	ONSP - Old Network Service Provider Identification – Not currently used  by CenturyLink	128

43.	TDTR - Ten Digit Trigger Response – Not currently used by CenturyLink	129

4.11	HUNT GROUP SECTION	130

44.	LOCNUM - Location Number – Not currently used by CenturyLink	130

45.	HNUM - Hunt Line Number – Not currently used by CenturyLink	131

46.	HID - Hunt Group Identifier – Not currently used by CenturyLink	132

47.	TLI - Telephone Line Identifier – Not currently used by CenturyLink	133

48.	HTSEQ - Hunt Sequence – Not currently used by CenturyLink	134

4.12	CIRCUIT DETAIL SECTION	135

49.	LNUM - Line Number – Not currently used by CenturyLink	135

50.	RNUM – Reference Number – Not currently used by CenturyLink	136

51.	LNEX - Line Number Extension Number – Not currently used by CenturyLink	137

52.	LEGNUM - Multipoint Leg Number – Not currently used by CenturyLink	138

53.	ECCKT - Exchange Company Circuit ID – Not currently used by  CenturyLink	139

54.	DSN - Dialable Station Number – Not currently used by CenturyLink	140

55.	LTC - Line Treatment Code – Not currently used by CenturyLink	141

56.	NOTYP - Number Type – Not currently used by CenturyLink	142

57.	TNS - Telephone Numbers – Not currently used by CenturyLink	143

58.	PID - Personal Identifier – Not currently used by CenturyLink	144

59.	SAT - Subscriber Access Telephone Number – Not currently used by  CenturyLink	145

60.	CKR - Customer Circuit Reference – Not currently used by CenturyLink	146

61.	CFA - Connecting Facility Assignment – Not currently used by  CenturyLink	147

62.	ORDL - Loop Order Number – Not currently used by CenturyLink	148

63.	NPORD - Number Portability Order Number – Not currently used by  CenturyLink	149

64.	DISC ECCKT – Disconnect ECCKT – Not currently used by CenturyLink	150

65.	DISC ORD - Disconnect Order Number – Not currently used by  CenturyLink	151

66.	SYSTEM ID - System Identification – Not currently used by CenturyLink	152

67.	SHELF – Shelf – Not currently used by CenturyLink	153

68.	SLOT – Slot – Not currently used by CenturyLink	154

69.	SPORT – Slot Port – Not currently used by CenturyLink	155

70.	RELAY RACK - Relay Rack – Not currently used by CenturyLink	156

71.	UNIT – Unit – Not currently used by CenturyLink	157

72.	CTI - Connection Type Indicator – Not currently used by CenturyLink	158

73.	CABLE ID - Cable Identification – Not currently used by CenturyLink	159

74.	CBCID - Cross Box Cable Identification – Not currently used by  CenturyLink	160

75.	CHAN/PAIR - Channel/Pair – Not currently used by CenturyLink	161

76.	PGI - Pair Gain Indicator – Not currently used by CenturyLink	162

77.	DEMARC - Demarc Designation – Not currently used by CenturyLink	163

78.	OOR - Out of Range Indicator – Not currently used by CenturyLink	164

79.	NID - Network Interface Device – Not currently used by CenturyLink	165

4.13	SECLOC SECTION	166

80.	LNUM - Line Number – Not currently used by CenturyLink	166

81.	LNEX - Line Number Extension Number – Not currently used by  CenturyLink	167

82.	DLCI - Data Link Connection Identifier – Not currently used by  CenturyLink	168

83.	RECCKT - Related Exchange Company Circuit Identification – Not  currently used by CenturyLink	169

84.	LST - Local Service Termination – Not currently used by CenturyLink	170

85.	RDLCI - Related Data Link Connection Identifier – Not currently used by  CenturyLink	171

4.14	DIRECTORY SECTION	172

86.	ATN - Account Telephone Number – Not currently used by CenturyLink	172

87.	DOR - Date of Receipt – Not currently used by CenturyLink	173

4.15	LISTINGS SECTION	174

89.	DLNUM - Directory Listing Number	174

90.	ALI - Alphanumeric Listing Identifier Code	175

91.	LTN – Listed Telephone Number	176

92.	NSTN - Non Standard Telephone Number	177

93.	LACT - Listing Activity Indicator	178

94.	LTY - Listing Type – Not currently used by CenturyLink	179

95.	STYC - Style Code – Not currently used by CenturyLink	180

96.	TOA – Type of Account – Not currently used by CenturyLink	181

97.	DOI - Degree of Indent – Not currently used by CenturyLink	182

98.	WPP - White Page Products – Not currently used by CenturyLink	183

99.	DIRIDL - Directory Identifier – Not currently used by CenturyLink	184

100.	DIRSUB - Directory Subsection – Not currently used by CenturyLink	185

101.	LISTNM – Listed Name – Not currently used by CenturyLink	186

102.	LNLN – Listed Name Last Name	187

103.	LNFN - Listed Name First	188

104.	LISTADR – Listed Address -  Not currently used by CenturyLink	189

105.	LTXNUM - Line of Text Reference Number – Not currently used by  CenturyLink	190

106.	LTXTY - Listing Text Type – Not currently used by CenturyLink	191

107.	LPHRASE - Listing Phrase – Not currently used by CenturyLink	192

108.	LTEXT - Listing Text – Not currently used by CenturyLink	193

109.	DIRSTAT – Directory Order Status – Not currently used by  CenturyLink	194

4.16	LISTING ERROR DETAILS SECTION	195

110.	DLLEREFNUM – DL Listing Confirmation/Error Code Reference Number	195

111.	LECODE – Listing DL Confirmation/Error Code	196

111a.	REMARKS – Remarks – CenturyLink-specific field	197

4.17	PON LISTING ERROR SECTION	199

112.	PONLEQTY – Not currently used by CenturyLink	199

113.	PONLEREFNUM – PON Listing Confirmation/Error Code Reference  Number	200

114.	LECODE - Listing PON Confirmation/Error Code	201

114a.	REMARKS – Remarks – CenturyLink-specific field	202

115.	ORDC – Order Response Code Detail – Not currently used by  CenturyLink	204

116.	LRNUM – Local Response Number – Not currently used by CenturyLink	205

117.	LRC – Listing Response Code – Not currently used by CenturyLink	206

118.	LRCD – Listing Response Code Detail – Not currently used by  CenturyLink	207

4.18	BULK REQUEST TO CREATE LSR CONFIRMATION SECTION (GUI    Only)	208

118a.	Bulk QTY NUM – CenturyLink - Specific Field	208

118b.	BNUM – Bulk Reference Number – CenturyLink - Specific Field	209

118c.	PON – Purchase Order Number – CenturyLink - Specific Field	210

118d.	TN – Telephone Number – CenturyLink - Specific Field	211

118e.	LSR ID – Local Service Request Identification – CenturyLink - Specific Field	212

4.19	SERVICE AND EQUIPMENT SECTION	213

118f.	ACTION CODE – Action Code – CenturyLink-Specific Field	213

118g.	USOC – Universal Service Order Code – CenturyLink-Specific Field	214

118h.	FID – Feature Identifier – CenturyLink-Specific Field	215

4.20	LINE INFORMATION SECTION	217

118i.	REF NUM – Reference Number – CenturyLink-Specific Field	217

118j.	HID – Hunt Group Identifier – CenturyLink-Specific Field	218

4.21	DID DISASSOCIATED SECTION	219

119.	DSTN – Disassociated Telephone Number – Not currently used by  CenturyLink	219

4.22	DID TELEPHONE NUMBER SECTION	220

119a.	DTLI – DID Telephone Line Identifier – CenturyLink-Specific Field	220

119b.	DTK – DID Trunk Quantity – CenturyLink-Specific Field	221

119c.	DTGN – DID Trunk Group Number – CenturyLink-Specific Field	222

119d.	DRTI – DID Route Index Number – CenturyLink-Specific Field	223

119e.	DTKID – DID Trunk ID – CenturyLink-Specific Field	224

119f.	DGOUT – DID Digits Out – CenturyLink-Specific Field	225

4.23	DID RANGE SECTION	226

119g.	DTNR – DID Telephone Number Range – CenturyLink-Specific Field	226

4.24	LISTINGS SECTION	227

119h.	ACTION CODE – Action Code – CenturyLink-Specific Field	227

119i.	LHLFID – Left Hand Listing Field Identifier – CenturyLink-Specific Field	228

119j.	LHLFIDDATA – Left Hand Listing Field Identifier Data – CenturyLink-Specific Field	229

4.25	BILLING SECTION	231

119k.	ACTION CODE – Action Code – CenturyLink-Specific Field	231

119l.	LHBFID – Left Handed Bill Field Identifier – CenturyLink-Specific Field	232

119m.	LHBFIDDATA – Left Handed Bill Field Identifier Data – CenturyLink-Specific  Field	233

4.26	TRAFFIC SECTION	235

119n.	ACTION CODE – Action Code – CenturyLink - Specific Field	235

119o.	LHTFID – Left Hand Traffic Field Identifier – CenturyLink-Specific Field	236

119p.	LHTFID DATA – Left Hand Traffic Field Identifier Data– CenturyLink-Specific  Field	237

4.27	CONTROL SECTION	239

119q.	ACTION CODE – Action Code – CenturyLink - Specific Field	239

119r.	LHCFID – Left Hand Control Field Identifier – CenturyLink Specific Field	240

119s.	LHCFID DATA – Left Hand Control Field Identifier Data– CenturyLink Specific  Field	241

120.	REMARKS – Remarks	243

120a.	DISCLAIMER – Disclaimer – CenturyLink-Specific Field	244

4.28	ASSIGNMENT SECTION	245

120b.	ACTION CODE – Action Code – CenturyLink-Specific Field	245

120c.	LHAFID – Left Hand Assignment Field Identifier – CenturyLink Specific Field	246

120d.	LHAFID DATA – Left Hand Assignment Field Identifier Data–  CenturyLink Specific Field	247

5.0	ALPHANUMERIC GLOSSARY	249

# LOCAL RESPONSE (LR) FORM – Numbered

# HISTORY LOG

The History Log for this document may be accessed from the Table of Contents at the following web site: http://www.centurylink.com/wholesale/clecs/lsog.html. The link to the downloadable History Log has been indented under Local Response (LR).

# 1.	GENERAL SECTION

1.1	This guide describes the Local Response (LR), which includes the Firm Order Confirmation (FOC), Cancel, Error, Reject, and Jeopardy notification fields contained in CenturyLink™’s Interconnect Mediated Access (IMA), both the XML and Graphical User Interface (GUI) versions.  The LR is provided to CLECs who utilize CenturyLink’s IMA system, (either the XML or GUI version) and is forwarded to the CLEC in response to a request for local products/services.

The LR provides the CLEC with relevant order information, including but not limited to, order number(s), due date(s), telephone number(s), circuit identification(s), error, reject, and/or jeopardy code(s)/descriptions, etc. associated with the CLEC’s request for service.

CLECs who manually fax LSRs to CenturyLink will receive a FOC as described in the Firm Order Confirmation – Manual (FOC) LSOG at http://www.centurylink.com/wholesale/clecs/lsog.html.

1.2	When a LR is issued in response to a firm order LSR, its issuance signifies CenturyLink’s good faith effort to provide the local service as ordered by the customer on the matching version of the referenced LSR form.

  - The LSOG Local Service Ordering Overview contains complete criteria for placing orders in the “Ordering Criteria Matrix” and a “Product Groups Table” identifying the products that may be requested.  This document is accessed from the following Web site http://centurylink.com/wholesale/clecs/lsog.html.

# 2.	LR FORM DESCRIPTION

# 2.1	FIRM ORDER CONFIRMATION

The LR form provides the customer with the information necessary for control and tracking of the applicable request(s) for the provisioning of local service (i.e., telephone numbers, circuit identification information, order numbers, due dates, etc.). This information is considered to be the Firm Order Confirmation (FOC).  Additionally the LR form acknowledges the receipt of a cancellation from the CLEC.

    - FOCs are sent in response to a CLEC-generated transaction.  A positive entry in the RTR field of the LSR form defines the CLEC’s expectation in regard to request notification. The FOC acknowledges to the CLEC that CenturyLink:

has received their request for service

created a CenturyLink service order

and established a due date for their request

2.1.2	In conjunction with the LR form, the REQTYP field on the LSR form will reflect the provider’s mechanized order processing indication that a Service Inquiry or Firm Order Confirmation has been processed.

| 2nd character of REQTYP is: | Type of Confirmation is: |
| --- | --- |
| B | Firm Order Confirmation |

    - LOCAL RESPONSE (LR) FORM

Included at the end of this document is a form with numbered fields to correspond with the Field Numbers within this document.  This numbered form is intended as a guide when using this document.

CenturyLink-specific forms contain:

- OBF fields which are used by CenturyLink

- OBF fields which are “Not currently used by CenturyLink” and shaded gray to indicate they are not to be used

- CenturyLink-specific fields necessary to process your request

# 2.2	ERROR/REJECT/JEOPARDY

2.2.1	The LR form provides the customer with the information that prevents an order from being completed and released.  This information is considered to be an Error Notification for non-fatal error conditions and a Reject Notification for fatal error conditions.

The LR form also provides the customer with information regarding facility problems or other impacts to meeting the scheduled due date of a service order.  This information is considered to be a Jeopardy notification.

    - Errors and Rejects are sent in response to a CLEC-generated transaction.  The Error and Reject Notification acknowledges to the CLEC that CenturyLink has determined that the request is either incomplete, incorrect, or the detail provided by the CLEC does not allow CenturyLink to process the request.

Reject notifications are only sent in those situations that are published in the Ordering Overview Product Catalog (PCAT) on the CenturyLink external web site in the ordering overview section and in some individual Product PCATs.

For additional information on reject and error notices see the Ordering Overview PCAT http://www.centurylink.com/wholesale/clecs/ordering.html.

All notices:

Define the type of notice being sent.

Provide an error, reject, or jeopardy reason.

2.2.3	Error, Reject and Jeopardy Notifications are not based on the REQTYP field on the LSR form since they are CenturyLink initiated.

# 2.3	COMPLETION

2.3.1	The LR form provides the customer with the information associated to a completed order.  This information is considered to be a Completion Notification.

2.3.2      The Completion Notice (CN) also referred to as “Completion Response” in IMA (Interconnect Mediated Access) GUI (Graphical User Interface) and IMA XML (Extensible Markup Language) and is a Post-Order function.

2.3.3	The CN is created at an LSR level (PON/Version (VER)).  When a single LSR requires multiple service orders for processing, the CN will reference and provide information for each service order. If CenturyLink processes multiple service orders for an LSR, the CLEC or Reseller will receive one CN per PON/VER.

2.3.4	The CN is returned to the CLEC when a LSR received through IMA GUI or IMA XML is provisioned.  CenturyLink may divide the LSR into multiple internal CenturyLink service orders.  A CN will be provided upon completion of all internal CenturyLink service orders for a given PON.

2.3.5 	The CN provides CLECs and Resellers with CenturyLink LSR and service order information, including but not limited to USOCs and FIDs in the Service and Equipment (S&E) section.  Only the USOCs and FIDs which represent changes, deletions or additions to the local service are returned on the CN when this information is available to CenturyLink’s IMA systems.  If any of the information is not available, a message is returned and will be provided on the CN indicating service order information is not available.

2.3.6	There is no form applicable to the CN. The CN is an electronic notice for Post-Order functionality and is available for IMA GUI and IMA XML users.

# 2.4	FACLITY BASED DIRECTORY LISTINGS (FBDL) NOTICES

2.4.1      The LR is created at an LSR/PON level and provides the customer with a status for every LSR (PON) successfully submitted via IMA GUI/XML.

2.4.2      The LR provides Confirmation and/or Error Codes at the LSR (PON) level and at the directory listing level.

2.4.2      An Initial LR is returned to the CLEC when a LSR is successfully submitted through IMA GUI or IMA XML.  A Subsequent LR will be provided on all orders with a PON status of Accepted with Change (AC) for each DL that did not successfully update as denoted on the Initial LR. Subsequent LRs are returned the next working business day after the Initial AC status was received.

2.4.3	An Initial LR that receives an RF status will remain in a rejected status for 10 calendar days.  This allows the CLEC to correct errors and resubmit the LSR using the same PON.  IMA will return a BPL error if an attempt is made to resubmit the LSR/PON after the 10 calendar day timeframe.

2.4.4	For additional information on FBDL confirmation and reject error codes/descriptions, see the IMA Facility Based Directory Listings Corrective Procedures and Error Codes document at http://www.centurylink.com/wholesale/ima/xml/.

2.4.5	A Manual LR is returned for FBDL LSRs/orders manually submitted via LSOG Forms.

# 3.	LR matricies

The following matrix is a guideline that indicates those fields that will be returned for FOC, Error, Reject, Jeopardy or Cancel notifications.

| FIELD | DESCRIPTION | RESPONSE |
| --- | --- | --- |
|  |  | FOC | ERROR | REJECT | JEOPARDY | CANCEL | COMPLETION | FBDL ONLY |
| ACTION CODE | Action Code (Service and Equipment Section) – CenturyLink-Specific Field |  |  |  |  |  | X |  |
| ACTION CODE | Action Code (Listings Section) – CenturyLink-Specific Field |  |  |  |  |  | X |  |
| ACTION CODE | Action Code (Billing Section) – CenturyLink-Specific Field |  |  |  |  |  | X |  |
| ACTION CODE | Action Code (Traffic Section) – CenturyLink-Specific Field |  |  |  |  |  | X |  |
| ACTION CODE | Action Code (Control Section) – CenturyLink-Specific Field |  |  |  |  |  | X |  |
| ACTION CODE | Action Code (Assignment Section) – CenturyLink-Specific Field |  |  |  |  |  | X |  |
| AFVR | Additional Field Visit Required – CenturyLink-Specific Field |  |  |  | X |  |  |  |
| ALI | Alphanumeric Listing Identifier Code |  |  |  |  |  |  | X |
| AN | Account Number (Administrative Section) | X |  |  |  |  |  | X |
| AN | Account Number – CenturyLink-Specific Field (Line Information Section) | X |  |  |  |  |  |  |
| APPTIME | Appointment Time – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| BAN1 | Billing Account Number 1 | X |  |  |  |  |  |  |
| BAN2 | Billing Account Number 2 | X |  |  |  |  |  |  |
| Be | Excess Burst Size – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| BI1 | Billing Account Number Identifier 1 | X |  |  |  |  |  |  |
| BI2 | Billing Account Number Identifier 2 | X |  |  |  |  |  |  |
| CC | Company Code | X | X | X | X | X |  | X |
| CCNA | Customer Carrier Name Abbreviation | X | X | X | X | X |  | X |
| CFA | Connecting Facility Assignment – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| CHC | Coordinated Hot Cut | X |  |  |  |  |  |  |
| CIR | Committed Information Rate – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| CKR | Customer Circuit Reference | X |  |  |  |  |  |  |
| CLECD/TSENT | CLEC Date and Time Sent |  |  |  |  |  |  | X |
| D/TSENT | Date and Time Sent | X | X | X | X | X |  | X |
| DD | Due Date – CenturyLink-Specific Field | X |  |  | X |  |  |  |
| DGOUT | DID Digits Out – CenturyLink-Specific Field | X |  |  |  |  | X |  |
| DIDNUM | DID Reference Number – CenturyLink-Specific Field | X |  |  | X |  |  |  |
| DISC ORD | Disconnect Order Number |  |  |  |  |  |  |  |
| DISCLAIMER | Disclaimer – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| DLCI | Data Link Connection Identifier – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| DLLEREFNUM | DL Listing Confirmation/Error Code Reference Number |  |  |  |  |  |  | X |
| DLNUM | Directory Listing Number |  |  |  |  |  |  | X |
| DLQTYR | Number of Listings – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| DRTI | DID Route Index Number – CenturyLink-Specific Field | X |  |  |  |  | X |  |
| DRTN | Distinctive Ring Telephone Number | X |  |  |  |  |  |  |
| DSGCON | Design/Engineering Contact | X |  |  | X |  |  |  |
| DTGN | DID Trunk Group Number – CenturyLink-Specific Field | X |  |  |  |  | X |  |
| DTK | DID Trunk Quantity – CenturyLink-Specific Field | X |  |  |  |  | X |  |
| DTKID | DID Trunk ID – CenturyLink-Specific Field | X |  |  |  |  | X |  |
| DTLI | DID Telephone Line Identifier – CenturyLink-Specific Field | X |  |  |  |  | X |  |
| DTNR | DID Telephone Number Range – CenturyLink-Specific Field | X |  |  |  |  | X |  |
| EC VER | Exchange Carrier Version | X | X | X | X | X |  |  |
| ECCKT | Exchange Company Circuit ID – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| ERROR/REJECT CODE | Error/Reject Code– CenturyLink-Specific Field |  | X | X |  |  |  |  |
| ERROR/REJECT DESCRIPTION | Error/Reject Description– CenturyLink-Specific Field |  | X | X |  |  |  |  |
| ESDD | Estimated Due Date– CenturyLink-Specicif Field |  |  |  | X |  |  |  |
| FDT | Frame Due Time – CenturyLink-Specific Field | X |  |  | X |  |  |  |
| FID | Field Identifier |  |  |  |  |  | X |  |
| FOC IND | Firm Order Confirmation Indicator – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| HID | Hunt Group Identifier – CenturyLink-Specific Field | X |  |  |  |  | X |  |
| IBT | ISDN BRI Type – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| INIT | Initiator Identification | X | X | X | X | X |  |  |
| ISPID | ISDN Service Profile Identification | X |  |  |  |  |  |  |
| LACT | Listing Activity |  |  |  |  |  |  | X |
| LECODE | Listing DL Confirmation/Error Code (Listing Error Detail Section) |  |  |  |  |  |  | X |
| LECODE | Listing DL Confirmation/Error Code (PON Listing Section) |  |  |  |  |  |  | X |
| LHAFID | Left Hand Assignment Field Identifier |  |  |  |  |  | X |  |
| LHAFIDDATA | Left Hand Assignment Field Identifier Data |  |  |  |  |  | X |  |
| LHBFID | Left Hand Billing Field Identifier |  |  |  |  |  | X |  |
| LHBFIDDATA | Left Hand Billing Field Identifier Data |  |  |  |  |  | X |  |
| LHCFID | Left Hand Control Field Identifier |  |  |  |  |  | X |  |
| LHCFIDDATA | Left Hand Control Field Identifier Data |  |  |  |  |  | X |  |
| LHLFID | Left Hand Listing Field Identifier |  |  |  |  |  | X |  |
| LHLFIDDATA | Left Hand Listing Field Identifier Data |  |  |  |  |  | X |  |
| LHTFID | Left Hand Traffic Field Identifier |  |  |  |  |  | X |  |
| LHTFIDDATA | Left Hand Traffic Field Identifier Data |  |  |  |  |  | X |  |
| LNEX | Line Number Extension Number – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| LNFN | Listed Name First Name |  |  |  |  |  |  | X |
| LNLN | Listed Name Last Name |  |  |  |  |  |  | X |
| LNUM | Line Number – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| LOCNUM | Location Number – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| LSR NO | Local Service Request Number | X | X | X | X | X |  | X |
| LSR_PIA_REMARKS | LSR_ Provider Initiated Activity Remarks – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| LSR_PIA_REMARKS 2 | LSR_ Provider Initiated Activity Remarks Other 2 – CenturyLink-Specific Field – GUI Only | X |  |  |  |  |  |  |
| LSR_PIA_REMARKS 3 | LSR_ Provider Initiated Activity Remarks Other 3 – CenturyLink-Specific Field – GUI Only | X |  |  |  |  |  |  |
| LST | Local Service Termination – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| LTN | Listed Telephone Number |  |  |  |  |  |  | X |
| MATN | Main/Alternate Telephone Number | X |  |  |  |  |  |  |
| NSP DSGCON | Network Service Provider (NSP) Design/Engineering Contact | X |  |  |  |  |  |  |
| NSTN | Non-Standard Telephone Number |  |  |  |  |  |  | X |
| ORD | Order Number – CenturyLink-Specific Field | X |  |  | X |  |  |  |
| ORD IND | Order Indicator – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| ORDER_PIA_ REMARKS | Order Provider Initiated Activity Remarks – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| ORDER_PIA_ REMARKS 2 | Order Provider Initiated Activity Remarks 2 – CenturyLink-Specific Field – GUI Only | X |  |  |  |  |  |  |
| ORDER_PIA_ REMARKS 3 | Order Provider Initiated Activity Remarks 3 – CenturyLink-Specific Field – GUI Only | X |  |  |  |  |  |  |
| OREF NUM | Order Reference Number – CenturyLink-Specific Field | X |  |  | X |  |  |  |
| PIA | Provider Initiated Activity | X |  |  |  |  |  |  |
| PON | Purchase Order Number | X | X | X | X | X |  |  |
| PONLEREFNUM | PON Listing Confirmation/Error Code Reference Number |  |  |  |  |  |  | X |
| PORTED NBR | Ported Telephone Number | X |  |  |  |  |  |  |
| RCODE | Reason Code |  |  |  | X |  |  |  |
| RDET | Reason/Jeopardy/Code Description |  |  |  | X |  |  |  |
| RDLCI | Related Data Link Connection Identifier – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| REF NUM | Reference Number |  |  |  |  |  | X |  |
| REMARKS | Remarks (Control Section) | X | X | X | X |  |  | X |
| REMARKS | Remarks (Listing Error Detail Section |  |  |  |  |  |  | X |
| REMARKS | Remarks (PON Listing Section) |  |  |  |  |  |  | X |
| REP | Provider Contact Representative | X | X | X | X | X |  |  |
| RORD | Related Order Number – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| RPON | Related Purchase Order Number – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| RT | Response Type | X | X | X | X | X |  | X |
| ST | Switch Type | X |  |  |  |  |  |  |
| TEL NO | Telephone Number (CLEC Information Section) | X | X | X | X | X |  |  |
| TEL NO | Telephone Number (Virtual Related Circuit Detail) | X |  |  |  |  |  |  |
| TERS | Terminal Numbers | X |  |  |  |  |  |  |
| TLI | Telephone Line Identifier – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| TNS | Telephone Numbers – CenturyLink-Specific Field | X |  |  |  |  |  |  |
| USOC | Universal Service Order Code |  |  |  |  |  | X |  |
| VER | Version Identification | X | X | X | X | X |  |  |

## 3.a	LR Matrix for Bulk Confirmation

Note: Common fields for most notices will not appear on the Bulk Confirmation; e.g., AN, SUP, VER.

| FIELD | DESCRIPTION | BULK CONFIRMATION |
| --- | --- | --- |
| BNUM | Bulk Reference Number – CenturyLink - Specific Field | X |
| BULK QTY NUM | Bulk Quantity Number – CenturyLink - Specific Field | X |
| CCNA | Customer Carrier Name Abbreviation | X |
| DT SENT | Date Sent | X |
| PON | Purchase Order Number – CenturyLink - Specific Field | X |
| REP | Provider Contact Representative | X |
| RT | Response Type | X |
| TN | Telephone Number – CenturyLink - Specific Field | X |
| LSR ID | Local Service Request Identification – CenturyLink - Specific Field | X |

# 4.	LR DATA ELEMENTS

## 4.1	ADMINISTRATIVE SECTION

1. CCNA - Customer Carrier Name Abbreviation

Identifies the RSID for resellers or ZCID for Interconnection. The RSID or ZCID is assigned by CenturyLink and provided to the customer during the negotiation process. The customer is required to provide either a RSID or ZCID on all requests.

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel, Error, Reject, Jeopardy | R | ANN (A= Alpha and N= Numeric) | Obtained from the LSR form. Either CCNA or CC is required for all Response Types. |
| REQTYP=JB Notices only, refer to RT field #18 | R | AAA (A= Alpha) |  |

| DATA CHARACTERISTICS: | 3 alphanumeric characters |
| --- | --- |

| EXAMPLE: | Z | 9 | 9 |
| --- | --- | --- | --- |

1a. CC - Company Code – CenturyLink-Specific Field

Identifies the Exchange Carrier requesting service.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel Error, Reject, Jeopardy | C |  | This field is required if populated on the LSR. Either CCNA or CC is required for all Response Types. |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 4 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 2 | 1 | 0 | 5 |
| --- | --- | --- | --- | --- |

2. PON - Purchase Order Number

Identifies the customer’s unique purchase-order or requisition number that authorizes the issuance of this request or supplement.

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel Error, Reject, Jeopardy | R |  | Obtained from the LSR form for all response types. |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |
| DATA CHARACTERISTICS: | 16 alphanumeric characters |

| EXAMPLE: | J | O | N | E | S | 1 | 0 | 1 | 9 | 2 | 0 | 0 | 1 | N |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

3. VER – Version Identification

Identifies the customer's version number.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel, Error, Reject, Jeopardy | C | AA - ZZ 00 - 99 Blank | For an initial request, CenturyLink assumes the version to be 1 and returns VER = 1 on the XML response. For any subsequent request whether as a supplement or in response to a manually generated error, the VER field will be echoed from the LSR form for all response types. |

| DATA CHARACTERISTICS: | 2 alphanumeric characters |
| --- | --- |

| EXAMPLE: | A | A |
| --- | --- | --- |

4. AN – Account Number

Identifies the main account number assigned by the NSP.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | Account Number Can be either 12 characters (a stand-alone telephone number) or 16 characters (a telephone number with a CUS code.) | Obtained from the LSR form, if populated for Response Type B, C, D, N, or X, otherwise not populated. If the AN field on the LSR is not populated (ACT = N), there will be no entry returned in this field and the CenturyLink-generated AN will be returned with the line-level information. The AN will contain either a TN or an SBN/MAN entry. See AN Field 21a in Line Information section, below. |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 16 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | - | 1 | 2 | 3 | - | 4 | 5 | 6 | 7 |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

See the AN Matrix under Field 20a – AN for response returned on an FOC.

5. ATN – Account Telephone Number – Not currently used by CenturyLink

Identifies the account telephone number assigned by the NSP. CenturyLink has chosen to use AN field in place of ATN.

6. LSR NO – Local Service Request Number

Identifies the number that is generated by CenturyLink’s mechanized systems, or manually assigned by CenturyLink to identify a customer's request for service.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel Error, Reject, Jeopardy | C |  | Not CenturyLink Generated for Response Type = Y. CenturyLink generated for all other Response Types. |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 11 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 2 | 2 | 2 | 2 | 5 | 6 |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

7. ORD – Order Number – Not currently used by CenturyLink

Identifies the provider’s order number for the service requested.

## 4.2	CLEC INFORMATION SECTION

8. CNO – Case Number – Not currently used by CenturyLink

Identifies the case number assigned by the provider in response to a Diversity Inquiry Request.

9. INIT – Initiator Identification

Identifies the initiator as specified on the LSR form by the customer.

| USAGE: | This field is optional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel, Error, Reject, Jeopardy | O |  | Obtained from the LSR form for all response types. |

| DATA CHARACTERISTICS: | 15 alphanumeric characters |
| --- | --- |

| EXAMPLE: | J | O | H | N |  | S | M | I | T | H |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

10. PG_of_ – Page _ of _ - Not currently used by CenturyLink

Identifies the page number and total number of pages contained in this request.

| 11. D/TSENT – Date and Time Sent |
| --- |
|  | XML: NOTICE AVAIL DT TM |  |
| Identifies the date and time that the Local Response is sent by CenturyLink. |

| VALID ENTRIES: |
| --- |
| U.S. Standard – Not currently used by CenturyLink | Metric Format – CCYYMMDDHHMinMin |
| Two Digit Month (01-12) | Two Digit Century (00-99) |
| Two Digit Day (01-31) | Two Digit Year (00-99) |
| Two Digit Century (00-99) | Two Digit Month (01-12) |
| Two Digit Year (00-99) | Two Digit Day (01-31) |
| Two Digit Hour (01-12) | Two Digit Hour (01-12) |
| Two Digit Minute (00-59) | Two Digit Minute (00-59) |
| AM or PM | AM or PM |

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel, Error, Reject, Jeopardy | C | See Valid Entries | CenturyLink generated for all Response Types except Response Type = V. |
| REQTYP=JB Notices only, refer to RT field #18 | R | See Valid Entries | CenturyLink generated |

| DATA CHARACTERISTICS: | 12 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 2 | 0 | 0 | 1 | 0 | 8 | 0 | 3 | 0 | 9 | 1 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

11a. CLECD/TSENT – CLEC Date and Time Sent – CenturyLink-Specific Field

Identifies the official time the LSR was sent into the IMA System.

| VALID ENTRIES: |
| --- |
| U.S. Standard | Metric Format – CCYYMMDDHHMinMin |
| Two Digit Month (01-12) | Two Digit Century (00-99) |
| Two Digit Day (01-31) | Two Digit Year (00-99) |
| Two Digit Century (00-99) | Two Digit Month (01-12) |
| Two Digit Year (00-99) | Two Digit Day (01-31) |
| Two Digit Hour (01-12) | Two Digit Hour (01-12) |
| Two Digit Minute (00-59) | Two Digit Minute (00-59) |
| AM or PM | AM or PM |
| Military Time |  |

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R | See Valid Entries |  |

| DATA CHARACTERISTICS: | 12 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 2 | 0 | 0 | 1 | 0 | 8 | 0 | 3 | 0 | 9 | 1 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

11b. LSRREMARKS – Remarks – CenturyLink-Specific Field

Identifies a free flowing field, which can be used to expand upon and clarify other data on this form.

| USAGE: | This field is optional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Error, Reject, Jeopardy | C |  |  |

| DATA CHARACTERISTICS: | 1000 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| D | I | S | C |  | O | F |  | F | I | R | S | T |  | C | K | T |  | I | N |  | G | R | O | U |
| P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

12. REP – Provider Contact Representative

Identifies CenturyLink’s representative handling this service request.

| USAGE: | This field is conditional on LR. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel, Error, Reject, Jeopardy | C | If RT = Y, then this field will be populated with SYSTEM. | CenturyLink Generated for all Response Types except Response Type V. |

| DATA CHARACTERISTICS: | 15 alphanumeric characters |
| --- | --- |

| EXAMPLE: | M | E | L | V | I | N |  | S | I | M | C | O | E |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

13. ST – Switch Type – Not currently used by CenturyLink

Indicates the type of local serving office (LSO) switch that is used to provide the BRI. This information may be needed to correctly configure the end user's customer premises equipment (CPE).

14. IBT – ISDN BRI Type – Not currently used by CenturyLink

Indicates the type of national ISDN BRI.

15. TEL NO – Telephone Number

Identifies the telephone number of CenturyLink’s representative handling this request.

| USAGE: | This field is conditional on the LR. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel, Error, Reject, Jeopardy | C | Dashes are returned in positions four and eight. | CenturyLink Generated for all Response Types except Response Type = Y. |

| DATA CHARACTERISTICS: | 12 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 2 | 0 | 1 | - | 9 | 8 | 1 | - | 3 | 5 | 8 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

16. RT – Response Type

Identifies the type of Local Response being returned to the customer. It does not necessarily match the entry from the RTR field on the Local Service Request (LSR).

VALID ENTRIES:

| All Products except FBDL | A = Completion B = Firm Order with Facility Information (72 Hour FOC) C = Firm Order Confirmation (FOC) D = Confirmation and DLR E = Errors Only F = Facility Confirmation – Not currently used by CenturyLink G = Confirmation and DSR Errors (Directory) – Not currently used by CenturyLink H = Combined (Service and Directory Listing) Confirmation and DSR errors – Not currently used by CenturyLink J = Jeopardy Notice L = Directory Only Completion – Not currently used by CenturyLink N = Confirmation of customer requested cancellation – CenturyLink - Specific Value S = Verbal Cancel V = Reject notice generated before the LSR is accepted by the IMA System - CenturyLink - Specific Value W = Bulk LSR Confirmation – CenturyLink - Specific Value (GUI Only) X = Confirmation of LSR, DLR and CDLR – CenturyLink - Specific Y = Fax to Fax Gateway confirmation Z = Reject notice generated after the LSR is accepted by the IMA System – CenturyLink - Specific Value |
| --- | --- |
| FBDL | L = Accepted (AT - Confirmed Update On PON) C = Acknowledge - With Detail and Change (AC - Processed With Changes/Errors-CenturyLink Follow Up) E = Reject with Exception Detail only (RF – Initial Fatal Update On PON) N = Reject with Cancel (RF – Subsequent Fatal Update On PON) W = Acknowledge – With Detail No change (AD - Processed With Changes/Errors-Provider Follow Up) |

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel, Error, Reject, Jeopardy | R | See Valid Entries | CenturyLink generated for all Response Types. This field identifies the type of LR being returned to the CLEC. It does not necessarily match the entry from the RTR field on the LSR. The entry of D or X in the RTR field of the LSR indicates that DLR must be included as a critical date on the service order. Population of the DLR FID and date on the service order trigger Network to send the DLR to the CLEC once RID is met. In other words, the sending of the FOC is completely separate from the sending of the DLR For a completion notice, Response Type = A For an original FOC, if RTR = C, D or X, and 72 hour FOC criteria are met, Response Type = B, otherwise echo the RTR entry from the LSR. For a subsequent FOC, echo the RT entry from the original FOC (B,C,D, or X). For a re-sent notice, echo the RT entry from the prior notice. For an error notice, Response Type = E. For a jeopardy notice, Response Type = J. For confirmation of a customer-initiated cancellation, Response Type = N. For a Fax to Fax Gateway confirmation, Response Type = Y For a reject notice generated after the LSR is accepted by the IMA System, Response Type = Z. For a reject notice generated before the LSR is accepted by the IMA System, Response Type = V |

| DATA CHARACTERISTICS: | 1 alpha character |
| --- | --- |

| EXAMPLE: | C |
| --- | --- |

## LSR PIA SECTION

The following two fields may repeat as a group.

17. PIA - Provider Initiated Activity

Indicates a provider initiated response that is not the result of a customer Local Service Request or supplement, prior to order completion.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | 4 = Other (clarify in LSR Level PIA remarks) 13 = BAN Change 16 = Other 2 (clarify in LSR Level PIA remarks) 17 = Other 3 (clarify in LSR Level PIA remarks) | This field is required when CenturyLink initiates a response that is not the result of a CLEC LSR or SUP prior to completion and if PIA (Field 20b) is not populated. This field is optional for an initial FOC. This field is required for subsequent FOC if PIA (Field 20b) is not populated. An entry is Valid if Response Type = B, C, D or X, otherwise not populated. This field can be repeated as many times as LSR Level PIAs and can include any combination of LSR Level type PIA values. IMA will generate 13 automatically. (4, 16, and 17 are manual only.) All entries may be manual. |

| DATA CHARACTERISTICS: | 3 numeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| 1 | 2 |  |

17a. LSR PIA REMARKS – LSR Level PIA Remarks Other – CenturyLink-Specific Field

Indicates the LSR Level PIA remarks in free-formed text when a value of Other (PIA = 4) is selected.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Business Rule |
| --- | --- | --- |
| FOC | C | This field entry is required only if a PIA value of 4, 16 and/or 17 is among the selected LSR level PIA entries, else prohibited. |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

EXAMPLE:

| A | d | d | e | d |  | H | S | H | P | G | & | H | S | H | P | T |  | i | n |  | p | l | a | c |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| e |  | o | f |  | H | S | O |  | w | h | i | c | h |  | i | s |  | n | o | t |  | a | l | l |
| o | w | e | d | . |  | O | n |  | t | h | e |  | l | a | s | t |  | l | i | n | e | , | a |  |
| h | u | n | t |  | c | h | a | r | g | e |  | i | s |  | n | o | t |  | v | a | l | i | d | . |

17a1. LSR PIA REMARKS 2 – LSR Level PIA Remarks Other 2 – CenturyLink-Specific Field – GUI Only

Indicates the LSR Level PIA remarks in free-formed text when a value of Other 2 (PIA= 16) is selected.

NOTE: This field does not appear on the form accompanying this document.

| USAGE: | This field is conditional. |
| --- | --- |

| RULE # | Notice Type | Products | Business Rule |
| --- | --- | --- | --- |
| 1 | FOC | All Products | The information in this field is taken from the original request. If PIA 16 is selected, then this field must be populated |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

EXAMPLE:

| A | d | d | e | d |  | H | S | H | P | G | & | H | S | H | P | T |  | i | n |  | p | l | a | c |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| e |  | o | f |  | H | S | O |  | w | h | i | c | h |  | i | s |  | n | o | t |  | a | l | l |
| o | w | e | d | . |  | O | n |  | t | h | e |  | l | a | s | t |  | l | i | n | e | , | a |  |
| h | u | n | t |  | c | h | a | r | g | e |  | i | s |  | n | o | t |  | v | a | l | i | d | . |

17a2. LSR PIA REMARKS 3 – LSR Level PIA Remarks Other 3 – CenturyLink-Specific Field – GUI Only

Indicates the LSR Level PIA remarks in free-formed text when a value of Other 3 (PIA = 17) is selected.

NOTE: This field does not appear on the form accompanying this document.

| USAGE: | This field is conditional. |
| --- | --- |

| RULE # | Notice Type | Products | Business Rule |
| --- | --- | --- | --- |
| 1 | FOC | All Products | The information in this field is taken from the original request. If PIA 17 is selected, then this field must be populated. |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

EXAMPLE:

| A | d | d | e | d |  | H | S | H | P | G | & | H | S | H | P | T |  | i | n |  | p | l | a | c |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| e |  | o | f |  | H | S | O |  | w | h | i | c | h |  | i | s |  | n | o | t |  | a | l | l |
| o | w | e | d | . |  | O | n |  | t | h | e |  | l | a | s | t |  | l | i | n | e | , | a |  |
| h | u | n | t |  | c | h | a | r | g | e |  | i | s |  | n | o | t |  | v | a | l | i | d | . |

## 4.4	ERROR/REJECT SECTION

The following three fields my repeat as a group.

17b. ERROR/REJECT CODE – Error or Reject Code – CenturyLink-Specific Field

Identifies the CenturyLink generated error or reject code.

VALID ENTRIES:

Reject Code nnn

Error Code service order processing error = nnn all other errors = nnn

3 character code for rejects/error (post order) 14 character code for fatal errors (integrity edits) The 14 character code is a fatal error code, while the 3 character error code is used for post-submission rejects and errors.

| 601 | = | Circuit not found |
| --- | --- | --- |
| 602 | = | Contract information missing or invalid |
| 603 | = | Contract number not valid |
| 604 | = | Customer Carrier Name Abbreviation (CCNA) missing or invalid |
| 605 | = | End User Authorization information missing |
| 606 | = | End User Name, TN, and Address mismatched, missing or invalid |
| 607 | = | Features on account are not compatible with requested features |
| 608 | = | Last name does not match CSR |
| 609 | = | MEGACENTNM field not populated with valid data |
| 610 | = | Message waiting or call forwarding with non-CenturyLink voice mail needs MSS FID data NOTE: MSS FID data is no longer needed for call forwarding but this reject code will still be used for message waiting scenarios. |
| 611 | = | SANO cannot be populated for a descriptive or unnumbered address, Please resubmit address |
| 612 | = | SANO/Last Name must match data on CSR |
| 613 | = | USOC missing some or all associated Field Identifiers (FIDs) |
| 614 | = | Service/feature requested is not available in this wire center |
| 691 | = | Required entry not populated – USED FOR DYNAMIC REJECT REASONS ONLY |
| 692 | = | Invalid entry – USED FOR DYNAMIC REJECT REASONS ONLY |
| 693 | = | Incomplete entry – USED FOR DYNAMIC REJECT REASONS ONLY |
| 694 | = | Conditional entry not provided – USED FOR DYNAMIC REJECT REASONS ONLY |
| 700 | = | Requested Product Not Available |
| 701 | = | Centrex Category (CAT) code missing |
| 702 | = | Centrex 21 must have a minimum of 2 and a maximum of 50 station lines |
| 703 | = | DEPT/LOCN code not provided for Western Centrex Plus |
| 711 | = | DSS trunk New Connect or Disconnect request does not reference related Purchase Order Number (PON) for facility, facility Disconnect or New Connect does not reference related PON for trunks NOTE: This reject reason can also apply to similar products, e.g., PRI. When combined services are being converted, all elements and associated PONs must be addressed. Exception: If retention of the DS1 facility is required, the CLEC must put a Remark on the LSR containing: "Retain DS1 facility authorized by (end user customer name)". |
| 721 | = | CIR and Be are not matching the port speed requested |
| 731 | = | NP request includes numbers disconnected more than 3 days ago |
| 732 | = | No FOC received from current provider. Cannot process Port In request |
| 733 | = | Rejected by current provider. Cannot process Port In request |
| 734 | = | Account does not qualify for Simple Port Request |
| 735 | = | Simple Port Request not supported via fax |

| 17b. ERROR/REJECT CODE – Error or Reject Code – CenturyLink-Specific Field (cont’d) |
| --- |
| 741 | = | CAP DSL not available as new Grand-fathered product |
| 742 | = | Loop does not qualify – conditioning not authorized |
| 743 | = | Speed requested not available on facility |
| 751 | = | Voice mail provider must contact CenturyLink Service Manager to establish Message Desk number before message waiting can be added |
| 752 | = | USOC not allowed on the LSR/CSR without certifying CLEC TAP Lifeline Guideline Compliance NOTE: Reject is based on the first identified TAP USOC. |
| 761 | = | Certification option number is required for New Service Activity |
| 762 | = | Conditioning not approved on original LSR, no response from CLEC 4 hours after request for additional info NOTE: For 72 Hour FOC eligible Unbundled Loop requests related to this scenario, the reject notification is sent immediately. There is no 4 hour waiting period. |
| 763 | = | Extension Technology not available on Pair Gain |
| 764 | = | Loops on this request don’t qualify for the activity requested |
| 765 | = | No compatible facilities |
| 766 | = | Delayed for no facilities |
| 767 | = | Unbundled Loop request contains missing or invalid Point of Interface (POI) or CFA, or specified slot is in use |
| 768 | = | Validation code and certification option number are required for Conversion activity |
| 769 | = | Validation code is required for Conversion activity |
| 770 | = | DSL cable is not valid for Unbundled Distribution Loop - Subloop. Resubmit with qualified CABCONN data |
| 771 | = | CFA, NC, NCI, or SEC NCI do not match the CSR on UBL requests with ACT = T or M |
| 781 | = | Voice mail provider must contact CenturyLink Service Manager to establish Message Desk number before message waiting can be added |
| 790 | = | FMC request cannot contain Directory Listings |
| 791 | = | FMC request cannot contain non-FMC numbers |
| 801 | = | Account not in CenturyLink local exchanges territory |
| 802 | = | Cannot issue supplement when one or more service orders are completed from the original LSR |
| 803 | = | Cannot mix measured and non-measured lines on same Account |
| 804 | = | Cannot mix contracted and month to month service on same account |
| 805 | = | Change activity is not allowed unless the CLEC owns the account |
| 806 | = | Circuit not active for disconnect request |
| 807 | = | CLEC name and RSID/ZCID do not match on LSR |
| 808 | = | Conversion or Disconnect request fails to address all telephone numbers on account, or on Centrex Department, or DPA |
| 809 | = | Invalid REQ Type/COS combination |
| 810 | = | Local Service Freeze in place – no pending order to remove |
| 811 | = | LSR involves multiple Account Telephone Numbers |
| 812 | = | LSR requests work on non-working account |
| 813 | = | No response to Customer Jeopardy after 10 business days for disconnect activity and 30 business days for all other activity |
| 814 | = | No response to C05 or SX Jeopardy from CLEC 4 hours after request for additional information |
| 815 | = | No response to Error Notification within 4 business hours |
| 816 | = | No valid address in Facility Check, no response from CLEC 4 hours after request for additional information |
| 817 | = | Not able to contact CLEC |
| 818 | = | Not able to resolve questions after CLEC has been contacted |
| 819 | = | Not valid Interconnect agreement or tariff |

17b.	ERROR/REJECT CODE – Error or Reject Code – CenturyLink-Specific Field 	(cont’d)

| 820 | = | Pending orders exist which are work impacting |
| --- | --- | --- |
| 821 | = | Pending order in conflict with Retail order |
| 822 | = | Pending order associated with CenturyLink Wholesale RSID/ZCID orders is in conflict with order |
| 823 | = | PON and Version combination cannot be reused for 2 years from the due date of the original request |
| 824 | = | Product and service description on LSR does not enable CenturyLink QC to determine USOCs or FIDs |
| 825 | = | Requested activity has already been requested or performed |
| 826 | = | Some or all telephone numbers on LSR not associated with Account Telephone Number on LSR |
| 827 | = | Unable to locate premise address |
| 828 | = | End User account is currently in denied status |
| 829 | = | This address requires a Location |
| 830 | = | Wrong form submitted for type of service requested |
| 831 | = | Related PON is rejected |
| 832 | = | Cannot issue conversion order. Request pending for LNP or LSNP |
| 833 | = | TSP code must be unique for each circuit on the request. Cannot use same TSP code for multiple circuits. |
| 899 | = | Non Defined Reason |
| 950 | = | LSR has been automatically faxed IIS, as the result of CLEC request reject override (RT = Y) |
| 965 | = | Non-fatal error (clarify in remarks) |

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Error, Reject | C |  | This field will be populated if RT = E, V, Y, or Z. |

| DATA CHARACTERISTICS: | 14 alphanumeric characters |
| --- | --- |

| EXAMPLES: | 9 | 6 | 5 |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 9 | 0 | 1 |  |  |  |  |  |  |  |  |  |  |  |

17c. ERROR/REJECT DESCRIPTION – Error or Reject Description – CenturyLink-Specific Field

This is a narrative English text description for the error or reject.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Error, Reject | C |  | This field is required if ERROR/REJECT CODE is populated. |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| A | C | C | O | U | N | T |  | N | O | T |  | I | N |  | L | O | C | A | L |  | E | X | C | H |
| A | N | G | E |  | T | E | R | R | I | T | O | R | Y |  |  |  |  |  |  |  |  |  |  |  |

17d. DIDNUM – Direct Inward Dial Reference Number – CenturyLink-Specific Field

Identifies each DID group as a unique number and each additional DID group as a unique number.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | Required when DIDNUM field is populated on the DID Resale form. Obtained from LSR form if Response Type = C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 3 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 2 | 3 |
| --- | --- | --- | --- |

## 4.5	CENTURYLINK ORDER INFORMATION SECTION

This section will not be returned on the FOC for a SUP to Cancel a request. CenturyLink Order Information Section - Within this section, OREF NUM through APPTTIME repeat as a group.  This section can repeat up to five times for all products.

17e. FOC IND – Firm Order Confirmation Indicator – CenturyLink-Specific Field

Identifies a partial FOC in the case of an LSR with both physical work and complex listings.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | P = Partial F = Full | The partial indicates physical work only. An entry is valid if Response Type = C, D or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 1 alpha character |
| --- | --- |

| EXAMPLE: | P |
| --- | --- |

17f. OREF NUM – Order Reference Number – CenturyLink-Specific Field

Identifies the line or trunk as a unique number and each additional occurrence as a unique number.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Jeopardy | C |  | Generated by CenturyLink. Required if RT = B, C, D, X, or J, otherwise not populated. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- |

17g. ORD – Order – CenturyLink-Specific Field

Identifies CenturyLink’s order number for the service requested.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Jeopardy | C |  | This field is present if OREF NUM is present, otherwise not populated. Generated by CenturyLink. |

| DATA CHARACTERISTICS: | 10 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| N | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |

17h. CD – Completion Date – CenturyLink-Specific Field

Identifies the date the service order was completed and turned up to the customer.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Returned for RT = A when available. |

| DATA CHARACTERISTICS: | 8 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| N | 1 | 2 | 3 | 4 | 5 | 6 | 7 |

17i. AN – Account Number – CenturyLink-Specific Field

Identifies the account number associated with the request.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | This value can be 12 or 16 characters in length. Dashes may be in positions 4 & 8 and may be in position 13 if 16 characters are used. | Returned when AN is available on the service order |

| DATA CHARACTERISTICS: | 16 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| N | 1 | 2 | - | 4 | 5 | 6 | - | 7 | 8 | 9 | 0 |  |  |  |  |

17j. ORD IND – Order Indicator – CenturyLink-Specific Field

Identifies whether it’s a designed or non-designed order.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | Y = design order N = non-design order | This field is required if OREF NUM is present, otherwise not populated. Generated by CenturyLink. |

| DATA CHARACTERISTICS: | 1 alphanumeric character |
| --- | --- |

| EXAMPLE: | Y |
| --- | --- |

17k. ST – Switch Type – CenturyLink-Specific Field

Indicates the type of local serving office (LSO) switch that is used to provide the ISDN BRI service.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | 1 = 5ESS 2 = DMS100 | Required for Response Type B, C, D or X when the product is BRI ISDN Resale or UNE-P BRI ISDN and the ACT = N, otherwise not populated. |

| DATA CHARACTERISTICS: | 1 numeric character |
| --- | --- |

| EXAMPLE: | 1 |
| --- | --- |

17l. IBT – ISDN BRI Type – CenturyLink-Specific Field

Indicates the type of ISDN BRI.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | 2 = NI-2 (National ISDN #2) 4 = Custom | This field is required for Response Type B, C, D, or X when the product is BRI ISDN Resale or UNE-P BRI ISDN and the ACT = N, otherwise not populated. |

| DATA CHARACTERISTICS: | 1 numeric character |
| --- | --- |

| EXAMPLE: | 1 |
| --- | --- |

18. DD - Due Date

Identifies the date the service order(s) is due to be completed.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | CCYYMMDD | Required if OREF NUM is populated, otherwise not populated. IMA will set the entry on flow through requests if the original DDD provided is changed when processed by the SOP. If RT = B,C,D, or X, PIA should be set to 2. |

| DATA CHARACTERISTICS: | 8 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 2 | 0 | 0 | 1 | 0 | 8 | 0 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

18a. DLQTYR - Number of Listings Received – CenturyLink-Specific Field

Identifies the number of listings provided for this request.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | Will be returned if RT = B, C, D, or X. |

| DATA CHARACTERISTICS: | 3 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 2 |
| --- | --- | --- | --- |

## 4.6	JEOPARDY STATUS

The following four fields repeat as a group: RCODE, RDET, ESDD, AFVR

18b. RCODE - Reason Code – CenturyLink-Specific Field

Identifies the reason the order may not meet the Due Date.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Jeopardy | C | 1A = Interoffice facility shortage 1B = Scheduling/work load 1C = Customer not ready 1D = No loop available 1E = End User not ready 1F = Missed Appointment 1G = No access to end user premises 1H = Central office freeze 1J = Special construction 1K = Natural disaster 1L = Frame due time cannot be met 1M = Requested due date is less than published interval 1N = DD and frame due time cannot be met 1P = Other 1Q = Assignment problem 1R = Customer could not be reached at the reach number 1S = Building not ready, customer will advise 1T = Pole at trailer site not set 1W = Entrance facilities required 1X = Not technically feasible 1Y = No central office equipment available 1Z = Loop requires installation of additional equipment | An entry is required when the Response Type field is populated with “J”, otherwise not populated. This field repeats as a group with RDET, ESDD, and AVR |

18b. RCODE - Reason Code – CenturyLink-Specific Field - continued

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
|  |  | 2A = LSR error, incorrect or missing information 2B = Facility work order pending, no Bona Fide Request required 3A = Records 3B = Facilities Incorrect/Busy 3C =Dependent/Related Order Not Complete 3D = Translations Problems 3E = Order Information/ Codes Incorrect/Missing 3F = Public Agency/Right of Way Delays 3G = Pre-Service Testing 3H = No Trunks Available 3I = Busy Cable ID and Channel Pair 4A = Field Visit Determined Address Invalid – Send Supplement 4B = Verify address, or provide nearby TN – Send Supplement 4C = New Access Required – Send Supplement 4D = Access Refused – Send Supplement 4E = CFA/POI Defective/Busy – Send Supplement 4F = Invalid/Duplicate Circuit ID – Send Supplement 4G = Need to revise TN – Send Supplement 4H = Invalid Feature/Feature Detail – Send Supplement 4I = Provide Driving Instructions – Send Supplement 5A = Notification of New Due Date Only 5B = Additional Paperwork Required – Contact Service Center 5C = Jeop Prev Sent w/o ESDD Now Provi |  |

| DATA CHARACTERISTICS: | 2 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 1 | Z |
| --- | --- | --- |

18c. RDET - Reason Jeopardy Code Detail – CenturyLink-Specific Field

Identifies the CenturyLink two or three-character JEP code followed by the description associated to the CenturyLink assigned jeopardy code.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Jeopardy | C | Format:2 or 3 character CenturyLink Jep Code: CenturyLink Jep Descriptions Colon shall be passed. Design: A34: Wholesale Markets-Weather/Disaster/Work Stoppage B14: Field Forces-Installation/Wiring Problem B31: Field Forces-Inadequate Pre-Service Testing or Conformance Testing B33: Field Forces-Work Force B34: Field Forces-Weather/Disaster/Work Stoppage C01: Customer-Not Ready C02: Customer-End User No Access C03: Customer-Subscriber Change in Requirements C05: Customer-Error or Reject Condition Identified After the FOC was Sent to the CLEC C09: Customer-Problem with Related Order C12: Customer-Customer Accepts Billing/Wholesale Only C24: Customer-CLEC/Customer Provided Conduit or Entrance Cable C29: Customer-Pending Customer Status in RTT C30: Customer-Unbundled Order Dependant on Left-In C31: Customer-Inadequate Pre-Service Testing or Conformance Testing C34: Customer-Weather/Disaster/Work Stoppage C40: Customer-Project Managed Order Held for CLEC/Customer Reason D01: Independent Companies-Not Ready D34: Independent Companies-Weather/Disaster/Work Stoppage | For RT = J this field is required if the RCODE field is populated, otherwise not populated. For RT = B, this field will be populated with the 72 Hour FOC Jeopardy Code and Description when a known jeopardy condition exists. RCODE is not requested to be populated if RT = B. This field repeats as a group with RCODE, ESDD, and AVR |

18c. RDET - Reason Jeopardy Code Detail – CenturyLink-Specific Field - continued

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
|  |  | E14: Central Office-Installation/Wiring Problem E31: Central Office-Inadequate Pre-Service Testing or Conformance Testing E33: Central Office-Work Force E34: Central Office-Weather/Disaster/Work Stoppage F31: Construction-Inadequate Pre-Service Testing or Conformance Testing F33: Construction-Work Force F34: Construction-Weather/Disaster/Work Stoppage G33: Other Field Forces-Work Force G34: Other Field Forces-Weather/Disaster/Work Stoppage H13: NROC/Complex Translations-Translations Problem H33: NROC/Complex Translations-Work Force H34: NROC/Complex Translations-Weather/Disaster/Work Stoppage J08- Local Loop Requires Conditioning K08: Engineering-Local Loop Requires Conditioning K09:Engineering – Problem with Related Order K10:Engineering – RTT Status will be awaiting funding SNRE K11:Engineering – Dependent order has RTT issued or SNRE status K14:Engineering – Installation Wiring Problem K15:Engineering – Records and Physical Wiring and/or Cable Makeup Do Not Agree K17: Engineering-Local Facility Not Available K18: Engineering-Local Facility Defective |  |

18c. RDET - Reason Jeopardy Code Detail – CenturyLink-Specific Field - continued

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
|  |  | K20: Engineering – Interoffice Facility Not Available K22: Engineering – Switch Equipment Not Available K31: Engineering – Inadequate Pre-Service Testing or Conformance Testing K32:Engineering – Inaccessible Plant/BT K33: Engineering – Work Force K34: Engineering – Weather/Disaster/Work Stoppage. K45: Engineering-Unbundled Only/RTT Issued N13: RMAC-Translations Problem N33: RMAC-Work Force N34: RMAC-Weather/Disaster/Work Stoppage P31: Design Service Center-Inadequate Pre-Service Testing or Conformance Testing P33: Design Service Center-Work Force P34: Design Service Center-Weather/Disaster/Work Stoppage Q33: Consolidated Design Group-Work Force Q34: Consolidated Design Group-Weather/Disaster/Work Stoppage V25: BRI/PICS-Plug-In Problem V33: BRI/PICS-Work Force V34: BRI/PICS-Weather/Disaster/Work Stoppage |  |

18c. RDET - Reason Jeopardy Code Detail – CenturyLink-Specific Field - continued

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
|  |  | Non-Design: CA: Company Assignments CE: Company Exceptions CF: Company Facility CL: Can’t Complete Work/Load CO: Company Other CS: Company Switching HD: Disaster HP: Hold for Payment/Identification SA: Subscriber Access SI: Subscriber Infrastructure SL: Subscriber Later SO: Subscriber Other SR: Working Left-In SX: Error Condition Identified After the FOC was Sent to the CLEC S1: Failed Synchronization Testing |  |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

EXAMPLE:

| B | 1 | 4 | : | F | i | e | l | d | - | I | n | s | t | a | l | l | a | t | i | o | n | / | W | i |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| r | i | n | g |  | P | r | o | b | l | e | m |  |  |  |  |  |  |  |  |  |  |  |  |  |

18d. ESDD - Estimated Due Date – CenturyLink-Specific Field

Identifies the date CenturyLink expects to have service available.

VALID ENTRIES:

Metric Format – ccyymmdd Two Digit Century (00-99) Two Digit Year (00-99) Two Digit Month (01-12) Two Digit Day (01-31)

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Jeopardy | C | See Valid Entries | This field is optional if the Response Type field is populated with “J”, otherwise not populated. This field repeats as a group with RCODE, RDET, and AVR |

| DATA CHARACTERISTICS: | 8 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 2 | 0 | 0 | 1 | 0 | 8 | 0 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

18e. AFVR - Additional Field Visit Required – CenturyLink-Specific Field

Identifies if a field visit is required at the customer/end user location that requires arrangements to be established.

| USAGE: | This field is optional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Jeopardy | O | Y = Yes | Optional if Response Type = J, otherwise not populated. |

| DATA CHARACTERISTICS: | 1 alpha character |
| --- | --- |

| EXAMPLE: | Y |
| --- | --- |

18f. FDT - Frame Due Time – CenturyLink-Specific Field

Identifies the frame due times that CenturyLink attempts to meet.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Jeopardy | C | HHMM (Military Time) | Required if OREF NUM is populated and if the DFDT field is populated on the LSR form, otherwise optional. NOTE: Simple Port Request provides time in the SPDDD/T field. CenturyLink will use the time from the SPDDD/T to identify frame due times. |
| FOC | C | XX | Required if OREF NUM is populated and if the DFDT field is populated on the LSR form, otherwise optional. NOTE: Simple Port Request provides time in the SPDDD/T field. CenturyLink will use the time from the SPDDD/T to identify frame due times. |

| DATA CHARACTERISTICS: | 4 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 0 | 9 | 0 | 4 |
| --- | --- | --- | --- | --- |

19. CHC - Coordinated Hot Cut

Indicates that CenturyLink agrees to the coordinated hot cut on the LSR form, if populated.

| NOTE 1: | This field may require manual intervention and coordination between the provider/customer. |
| --- | --- |

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | Y = Yes N = No B = Batch Hot Cut | Echo back entry based on preorder activity if Response Type = B, C, D or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 1 alpha character |
| --- | --- |

| EXAMPLE: | Y |
| --- | --- |

19a. APPTIME – Appointment Time – CenturyLink-Specific Field

Identifies the time period during which the end-user’s service will be established and/or a technician is scheduled to visit the end-user’s premises.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | The appointment time format is in military time. If appointment or desired appointment time is a time range, the format is HHMM-HHMM. If the appointment time is a commitment, the format is HHMM. | Echo back entry based on preorder activity if Response Type = B, C, D, or X, and an appointment was scheduled, otherwise not populated. This will repeat one time per order. |

| DATA CHARACTERISTICS: | 9 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  | 1 | 4 | 4 | 5 | - | 1 | 5 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

4.7 ORDER PIA SECTION The following two fields may repeat as a group. 19b. PIA - Provider Initiated Activity – CenturyLink-Specific Field

Indicates a provider initiated response that is not the result of a customer Local Service Request or supplement, prior to order completion.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | 1 = ECCKT(s) change 2 = Due date change by CenturyLink 3 = ECCKT and due date change (not used by CenturyLink) 4 = Other (clarify in Order Level PIA remarks) 5 = Service order number change 6 = Route Index (RTI) change 7 = Change to TERS/HID 9 = Telephone number change 10 = Verbal CFA/Slot change accepted 11 = Dispatch entry not valid 12 = AN (SBN/BTN/MAN) Change 16 = Other 2 (clarify in Order Level PIA remarks) 17 = Other 3 (clarify in Order Level PIA remarks) 18 = Verbal due date change by CLEC 19 = Verbal SUP to add cooperative test on DD | This field is required when CenturyLink initiates a response that is not the result of a CLEC LSR or SUP prior to completion and if PIA (Field 17) is not populated. This field is required for subsequent FOC if PIA (Field 17) is not populated. This field is optional for an initial FOC. An entry is Valid if Response Type = B, C, D, or X, otherwise not populated. This field can be repeated as many times as Order Level PIAs and can include any combination of Order Level type PIA values. |

| DATA CHARACTERISTICS: | 3 numeric characters |
| --- | --- |

EXAMPLE:

| 4 | , | 17 |
| --- | --- | --- |

19c. ORDER-PIA-REMARKS – Order Level PIA Remarks Other – CenturyLink-Specific Field

Indicates the Order Level PIA remarks in free-formed text when a value of Other (PIA = 4) is selected.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Business Rule |
| --- | --- | --- |
| FOC | C | This field entry is required only if a PIA value of 4 is among the selected Order level PIA entries, else prohibited. |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

EXAMPLE:

| L | D | 1 |  | s | h | o | u | l | d |  | b | e |  | L | O | T |  | p | e | r |  | T | A | G |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| / | P | R | E | M | I | S |  | n | o | t |  | S | U | I | T | . |  |  |  |  |  |  |  |  |

19c1. ORDER PIA REMARKS 2 – Order Level PIA Remarks Other 2 – CenturyLink-Specific Field – GUI Only

Indicates the LSR Level PIA remarks in free-formed text when a value of Other 2 (PIA = 16) is selected.

| USAGE: | This field is conditional. |
| --- | --- |

NOTE: This field does not appear on the form accompanying this document.

| RULE # | Notice Type | Products | Business Rule |
| --- | --- | --- | --- |
| 1 | FOC | All Products | The information in this field is taken from the original request. If PIA 16 is selected, then this field must be populated |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

EXAMPLE:

| A | d | d | e | d |  | H | S | H | P | G | & | H | S | H | P | T |  | i | n |  | p | l | a | c |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| e |  | o | f |  | H | S | O |  | w | h | i | c | h |  | i | s |  | n | o | t |  | a | l | l |
| o | w | e | d | . |  | O | n |  | t | h | e |  | l | a | s | t |  | l | i | n | e | , | a |  |
| h | u | n | t |  | c | h | a | r | g | e |  | i | s |  | n | o | t |  | v | a | l | i | d | . |

19c2. ORDER PIA REMARKS 3 – Order Level PIA Remarks Other 3 – CenturyLink-Specific Field – GUI Only

Indicates the LSR Level PIA remarks in free-formed text when a value of Other 3 (PIA = 17) is selected.

NOTE: This field does not appear on the form accompanying this document.

| USAGE: | This field is conditional. |
| --- | --- |

| RULE # | Notice Type | Products | Business Rule |
| --- | --- | --- | --- |
| 1 | FOC | All Products | The information in this field is taken from the original request. If PIA 17 is selected, then this field must be populated |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

EXAMPLE:

| A | d | d | e | d |  | H | S | H | P | G | & | H | S | H | P | T |  | i | n |  | p | l | a | c |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| e |  | o | f |  | H | S | O |  | w | h | i | c | h |  | i | s |  | n | o | t |  | a | l | l |
| o | w | e | d | . |  | O | n |  | t | h | e |  | l | a | s | t |  | l | i | n | e | , | a |  |
| h | u | n | t |  | c | h | a | r | g | e |  | i | s |  | n | o | t |  | v | a | l | i | d | . |

20. EBD - Effective Bill Date – Not currently used by CenturyLink

Identifies the effective date to begin or cease billing when the billing date is different from the desired due date.

## 4.8	LINE INFORMATION SECTION

Line Information Section: LNUM through LOCNUM repeat as a group (within the repeating CenturyLink Order Information Section).

20a. AN – Account Number – CenturyLink-Specific Field

Identifies the main account number assigned by CenturyLink.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | If Response Type = B, C, D or X, populate with the account number and CUS code entered on the service orders, not with the account number and CUS code from the LSR. Prohibited on all other response types. CenturyLink generated if ACT = N (New Account) or ACT = C with an LNA of X (Number Change.) Depending on the request activity, the Account Number may be a telephone number format or an SBN/MAN format (nnnannnnnn). IMA will auto-correct the entry on flow through requests if the original AN provided is changed when processed by the SOP. PIA should be set to 12. |

20a. AN – Account Number – CenturyLink-Specific Field - continued

The following matrix is to show the response returned on a FOC when the appropriate entry is populated in the LSR and other product specific forms.

| If the REQTYP on the LSR is: | And the ACT on the LSR is: | And the Version of the LSR is: | The AN field in the Administrative Section of the FOC will be: | The AN field in the Line Information Section of the FOC will be: | Additionally, the following data will be returned on the FOC in the Line Information Section: |
| --- | --- | --- | --- | --- | --- |
| AB (LS) | N | Version 1 (Initial Request) or Subsequent Version SUP Type 3 | Blank | Populated with the new CenturyLink assigned SBN/MAN | ECCKT CFA |
|  |  | Subsequent Version with a DD change SUP Type 2 | Blank | Populated with the new CenturyLink assigned SBN/MAN | ECCKT CFA |
|  |  | Subsequent Version to Cancel SUP Type 1 | Blank | Blank | Blank |
| AB (LS) | D, V, C or T | Version 1 (Initial Request) or Subsequent Version SUP Type 3 | An echo of the TN for ACT=V or SBN/MAN for all other ACTs, as populated on the LSR | Populated with the existing CenturyLink assigned SBN/MAN format Account Number | ECCKT |
|  |  | Subsequent Version with a DD change SUP Type 2 | An echo of the TN for ACT=V or SBN/MAN for all other ACTs, as populated on the LSR | Populated with the existing CenturyLink assigned SBN/MAN format Account Number | ECCKT |
|  |  | Subsequent Version to Cancel SUP Type 1 | An echo of the TN for ACT=V or SBN/MAN for all other ACTs, as populated on the LSR | Blank | Blank |
|  | V (CLEC to CLEC Conversion) | Version 1 (Initial Request) or Subsequent Version SUP Type 3 | Blank or populated with the placeholder 000-000-0000 | Populated with the new CenturyLink Assigned SBN/MAN | New CenturyLink assigned ECCKT |
|  |  | Subsequent Version with a DD change SUP Type 2 | Blank or populated with the placeholder 000-000-0000 | Populated with the new CenturyLink Assigned SBN/MAN | New CenturyLink assigned ECCKT |
|  |  | Subsequent Version to Cancel | Blank or populated with the placeholder 000-000-0000 | Blank | Blank |
| BB (LSNP) | V or Z | Version 1 (Initial Request) or Subsequent Version SUP Type 3 | An echo of the TN populated on the LSR | Populated with the new CenturyLink assigned SBN/MAN format Account Number | PORTED NBR ECCKT CFA |
|  |  | Subsequent Version with a DD change SUP Type 2 | An echo of the TN populated on the LSR | Populated with the new CenturyLink assigned SBN/MAN format Account Number | PORTED NBR ECCKT CFA |
|  |  | Subsequent Version to Cancel SUP Type 1 | An echo of the TN populated on the LSR | Blank | Blank |

| 20a. AN – Account Number – CenturyLink-Specific Field - continued |
| --- |
| If the REQTYP on the LSR is: | And the ACT on the LSR is: | And the Version of the LSR is: | The AN field in the Administrative Section of the FOC will be: | The AN field in the Line Information Section of the FOC will be: | Additionally, the following data will be returned on the FOC in the Line Information Section: |
| CB (NP) | V or Z | Version 1 (Initial Request) or Subsequent Version SUP Type 3 | An echo of the TN format Account Number populated on the LSR | Populated with the current CenturyLink TN format Account Number. | PORTED NBR |
|  |  | Subsequent Version with a DD change SUP Type 2 | An echo of the TN format Account Number populated on the LSR | Populated with the current CenturyLink TN format Account Number. | PORTED NBR |
|  |  | Subsequent Version to Cancel SUP Type 1 | An echo of the TN format Account Number populated on the LSR | Blank | Blank |
| EB (Resale) FB (Unbundled Switch Ports) MB (UNE-P) NB (DID Resale) PB (Centrex Resale) | N | Version 1 (Initial Request) or Subsequent Version SUP Type 3 | Blank | Populated with the new CenturyLink assigned TN format Account Number | TNS ECCKT ISPID HID TLI TERS |
|  |  | Subsequent Version with a DD change SUP Type 2 | Blank | Populated with the new CenturyLink assigned TN format Account Number | TNS ECCKT ISPID HID TLI TERS |
|  |  | Subsequent Version to Cancel SUP Type 1 | Blank | Blank | Blank |
|  | All but N | Version 1 (Initial Request) or Subsequent Version SUP Type 3 | An echo of the TN format Account Number populated on the LSR | Populated with the existing CenturyLink TN format Account Number. | TNS ECCKT ISPID HID TLI TERS |
|  |  | Subsequent Version with a DD change SUP Type 2 | An echo of the TN format Account Number populated on the LSR | Populated with the existing CenturyLink TN format Account Number. | TNS ECCKT ISPID HID TLI TERS |
|  |  | Subsequent Version to Cancel SUP Type 1 | An echo of the TN format Account Number populated on the LSR | Blank | Blank |

20a. AN – Account Number – CenturyLink-Specific Field - continued

| If the REQTYP on the LSR is: | And the ACT on the LSR is: | And the Version of the LSR is: | The AN field in the Administrative Section of the FOC will be: | The AN field in the Line Information Section of the FOC will be: | Additionally, the following data will be returned on the FOC in the Line Information Section: |
| --- | --- | --- | --- | --- | --- |
| KB (Resale Private Line) LB (Resale Frame Relay) MB (UNE-C) | N | Version 1 (Initial Request) or Subsequent Version SUP Type 3 | Blank for REQTYP = KB and MB AN = CLEC Detail BAN for REQTYP = LB | Populated with the CenturyLink assigned SBN/MAN format Account Number | ECCKT |
|  |  | Subsequent Version with a DD change SUP Type 2 | Blank for REQTYP = KB and MB AN = CLEC Detail BAN for REQTYP = LB | Populated with the CenturyLink assigned SBN/MAN format Account Number | ECCKT |
|  |  | Subsequent Version to Cancel SUP Type 1 | Blank for REQTYP = KB and MB AN = CLEC Detail BAN for REQTYP = LB | Blank | Blank |
| KB (Resale Private Line) LB (Resale Frame Relay) MB (UNE-C) | All but N | Version 1 (Initial Request) or Subsequent Version SUP Type 3 | Populated with the existing CenturyLink assigned SBN/MAN format Account Number | Populated with the existing CenturyLink assigned SBN/MAN format Account Number | ECCKT |
|  |  | Subsequent Version with a DD change SUP Type 2 | Populated with the existing CenturyLink assigned SBN/MAN format Account Number | Populated with the existing CenturyLink assigned SBN/MAN format Account Number | ECCKT |
|  |  | Subsequent Version to Cancel SUP Type 1 | Populated with the existing CenturyLink assigned SBN/MAN format Account Number | Blank | Blank |

| DATA CHARACTERISTICS: | 16 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | - | 1 | 2 | 3 | - | 4 | 5 | 6 | 7 |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

20b. LNUM – Line Number – CenturyLink-Specific Field

Identifies the line or trunk as a unique number and each additional occurrence as a unique number.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | If Response Type = B, C, D, or X, this field is required and obtained from the Product Specific form, otherwise not populated. LNUM 0001 should always be the primary Account Number. LNUM 0001 will be processed as the primary AN, and will be the number published if it is associated with a directory listing. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- |

20c. TNS - Telephone Numbers – CenturyLink-Specific Field

Identifies the telephone number or consecutive range of telephone numbers for this request.

| NOTE 1: | There may be one or more ISDN telephone numbers assigned per ISDN BRI line. |
| --- | --- |

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | For a single TN, the format is: NPA-NXX-LLLL (12 characters) Dashes are required in positions 4 and 8. For a range of TNs, the format is: NPA-NXX-LLLL-HHHH (17 characters), where L and H are numeric and HHHH is always greater than LLLL. If a range is used, a dash is also required in position 13. | If Response Type = B, C, D, or X, obtain from Product Specific form (if present) or provide CenturyLink assigned Telephone Numbers, otherwise not populated. For Resale BRI ISDN and Unbundled Digital Line-Side Switch Ports, the ECCKT and TN will always be returned as a pair. The BRI ISDN circuit ID may remain the same while the TN changes. |

| DATA CHARACTERISTICS: | 17 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | - | 1 | 2 | 3 | - | 4 | 5 | 6 | 7 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

21. DRTN - Distinctive Ring Telephone Number

Identifies the additional telephone number(s) associated with unique ringing.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | An entry is required when the USOC for unique ringing is requested on the Product Service form and the Response Type = B, C, D, or X, otherwise not populated. This field repeats up to three times per TNS when necessary. |

| DATA CHARACTERISTICS: | 12 alphanumeric characters |
| --- | --- |

The format is NPA-NXX-LLLL. Dashes are required in positions 4 and 8

| EXAMPLE: |
| --- |
| 3 | 0 | 3 | - | 5 | 5 | 5 | - | 1 | 2 | 3 | 4 |

22. MATN - Main/Alternate Telephone Number

Indicates the dialable telephone number(s) assigned to the ISDN BRI line.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | M = Main Telephone Number A = Alternate telephone number(s) | This field indicates the dialable telephone numbers assigned to the ISDN BRI line if Response Type = B, C, D or X, otherwise not populated. There can only be one main telephone number but multiple alternate telephone numbers may exist. |

| DATA CHARACTERISTICS: | 1 alphanumeric characters |
| --- | --- |

| EXAMPLE: | M |
| --- | --- |

23. ISPID - ISDN Service Profile Identification

Provides a code that must be programmed into the ISDN BRI customer premises equipment (CPE). This code is transmitted from the CPE over the ISDN BRI D-channel to the LSO switch. It must be present in order for the BRI to become active.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | The format of the ISPID is NPA555121211-11 where 5551212 represents the telephone number and NPA and 11-11 are constant. | Required if the product is BRI ISDN or UNE_P_BRI ISDN and HID is not populated. |

| DATA CHARACTERISTICS: | 15 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 7 | 0 | 3 | 5 | 5 | 5 | 1 | 2 | 1 | 2 | 1 | 1 | - | 1 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

23a. HID – Hunt Group Identifier – CenturyLink-Specific Field

Identifies the hunt group.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | Required if present on the HGI form and if Response Type = B, C, D or X, otherwise not populated. If a placeholder is used on the HGI, then CenturyLink assigns HID. |

| DATA CHARACTERISTICS: | 5 alphanumeric characters |
| --- | --- |

| EXAMPLES: | 1 | 2 | 2 | 4 | A |
| --- | --- | --- | --- | --- | --- |

23b. TLI – Telephone Line Identifier– CenturyLink-Specific Field

Identifies the pilot number of a multi-line hunt group.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | This field is required if a HNTYP = 4, 5, 13, 14, or 15 and HA on the LSR = ‘N’ and if Response Type = B, C, D or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 12 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | - | 1 | 2 | 3 | - | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

24. TERS - Terminal Numbers

Identifies the number for a non-lead line in a multi-line hunt group or consecutive range of terminal numbers associated with the TNS field for this request.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | Required if ‘hunt type’ of ‘multi-line hunting’ is requested and if Response Type = B, C, D, or X, otherwise not populated Obtain from the product specific form, or assigned by CenturyLink when a placeholder is sent. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 3 |  |  |  |
| --- | --- | --- | --- | --- |

25. PORTED NBR - Ported Telephone Number

Identifies the telephone number (TN) and/or consecutive range of TN’s residing in the same switch that are to be ported.

| NOTE 1: | A single number of the first number of the range may also be used to identify the billing account number. |
| --- | --- |
| NOTE 2: | May include two or three hyphens as delimiters between the telephone number components and range. |
| NOTE 3: | When the NPT field is “B”, a number range may only be specified when all numbers within the range are remote call forwarded to the same TN. |
| NOTE 4: | A range of numbers can be presented as a block of numbers or multiple iterations. |

| USAGE: | This field conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | NPA-NXX-LLLL = Single Ported NBR NPA-NXX-LLLL-HHHH = Range of Ported NBRs L and H are numeric and HHHH is always greater than LLLL. Dashes are returned in positions four and eight. If a range is used, a dash is also returned in position 13. | This field is required when present on the Product Specific form and when Response Type = B, C, D, or X otherwise not populated. If a single Ported NBR was used on the Product Specific form, this field is an echo from the Product Specific form. If a range of Ported NBRs were used on the Product Specific form, this field can either be an echo from the Product Specific form, or a subset of the range (to reflect the subset of numbers associated with a specific CenturyLink service order). |

| DATA CHARACTERISTICS: | 17 alphanumeric characters |
| --- | --- |

| EXAMPLES: | 9 | 0 | 8 | - | 6 | 9 | 9 | - | 7 | 0 | 0 | 0 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

|  | 9 | 0 | 8 | - | 6 | 9 | 9 | - | 7 | 0 | 0 | 0 | - | 7 | 0 | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

26. RTI - Route Index – Not Currently used by CenturyLink

Identifies the routing index to be used by CenturyLink’s switching equipment to forward/port CenturyLink’s telephone number to the customer's non-RCF trunk group.

27. DISC NBR - Disconnect Telephone Number – Not currently used by CenturyLink

Identifies the end-user telephone number to be disconnected.

27a. ECCKT – Exchange Company Circuit ID – CenturyLink-Specific Field

Identifies CenturyLink’s circuit identification.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | See Examples below where n = number and A = Alpha | The LNUM and ECCKT must match the sequence on the Product Specific forms (e.g. Resale, Loop Service), if provided. For new circuits, CenturyLink will provide assigned circuit ids that must be supplied on all subsequent orders. For Private Line formatted services, ECCKT is obtained from the Primary Location Service Details section. For Resale BRI ISDN and Unbundled Digital Line-Side Switch Ports, the ECCKT and TN will always be returned as a pair. The circuit ID may remain the same while the TN changes. Valid if Response Type = B, C, D, or X, otherwise not populated. If the original ECCKT provided is changed when processed by the SOP, PIA should be set to 1. |

| DATA CHARACTERISTICS: | 42 alphanumeric characters |
| --- | --- |

EXAMPLES:

CenturyLink CLCI formats are region specific. Where n = number and A = alpha. The format will vary by product.

| A | . | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| A | . | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n | . | A | A |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| A | . | A | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n | . | A | n |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| A | A | . | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| A | A | . | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n | . | A | A |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

27a. ECCKT – Exchange Company Circuit ID – CenturyLink-Specific Field - continued

| A | A | . | A | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n | . | A | n |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| n | . | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n | . | A | A |  |  |  |

| n | . | A | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | . | . | A | A |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | . | . | A | A | A | A |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | . | A | A |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | . | A | A | A | A |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | . | . | A | A |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | . | . | A | A | A | A |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | . | A | A |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | . | A | A | A | A |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | n | . | . | A | A |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | n | . | . | A | A | A | A |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | n | . | A | A |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | n | . | A | A | A | A |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | n | n | . | . | A | A |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| 27a. ECCKT – Exchange Company Circuit ID – CenturyLink-Specific Field - continued |
| --- |
| n | . | A | A | A | A | . | n | n | n | n | n | n | n | . | . | A | A | A | A |  |  |  |  |

| n | . | A | A | A | A | . | n | n | n | n | n | n | n | . | A | A |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | . | A | A | A | A | . | n | n | n | n | n | n | n | . | A | A | A | A |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n | . | A | A |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | . | n | n | n | . | n | n | n | n | . | A | n |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | . | . | A | A |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | . | . | A | A | A | A |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | . | A | A |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | . | A | A | A | A |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | . | . | A | A |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | . | . | A | A | A | A |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | . | A | A |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | . | A | A | A | A |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | n | . | . | A | A |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | n | . | . | A | A | A | A |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | n | . | A | A |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| 27a. ECCKT – Exchange Company Circuit ID – CenturyLink-Specific Field - continued |
| --- |
| n | n | . | A | A | A | A | . | n | n | n | n | n | n | . | A | A | A | A |  |  |  |  |  |

| n | n | . | A | A | A | A | . | n | n | n | n | n | n | n | . | . | A | A |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | n | n | . | . | A | A | A | A |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | n | n | . | A | A |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| n | n | . | A | A | A | A | . | n | n | n | n | n | n | n | . | A | A | A | A |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

27b. SAT - Subscriber Access Telephone Number – CenturyLink-Specific Field

Identifies the telephone number, which allows remote access to make feature configuration changes.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | An entry is required when new access to voice messaging is requested on the Product Service form and when Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 12 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | - | 5 | 5 | 5 | - | 1 | 2 | 1 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

28. CKR - Customer Circuit Reference

Identifies the circuit number assigned by the customer.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | This field is required if present on Product Specific forms. Obtain from the product specific form if Response Type = B, C, D, or X, otherwise not populated. For Private Line, the CKR is obtained from the Primary Location Service Details section. |

| DATA CHARACTERISTICS: | 36 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| 1 | 5 | . | I | B | S | A | . | 1 | 2 | 6 | 7 | 4 | 7 | . | . | N | W |  |  |  |  |  |  |  |

28a. CFA - Connecting Facility Assignment – CenturyLink-Specific Field

Identifies the CenturyLink carrier system and channel to be used.

| NOTE 1: | The format and structure of this field is defined by ANSI in document T1.238, Identification of Telecommunication Facilities for the North American Telecommunications System. The Facility Identifier consists of the following elements: |
| --- | --- |

| 1. | Facility Designation - A code that, for a specific type of facility, uniquely identifies a path between two network nodes (variable length, 1-5 alphanumeric characters). |
| --- | --- |
| 2. | Facility Type - A code that describes a type of facility when it is other than a single baseband channel on cable. Valid entries are outlined in Telcordia Technologies practice BR 795-450-100 (variable length, 1-6 alphanumeric characters). |
| 3. | Channel/Pair/Time Slot - A code that identifies a specific assignable portion of a facility (variable length, 1-5 alphanumeric characters). |
| 4. | Location A - A standardized code that uniquely identifies the location of facility terminal A, which has the lower in alphanumeric sequence of the two facility location codes. Valid values are outlined in Telcordia Technologies practice BR 795-100-100 (8 or 11 alphanumeric characters). |
| 5. | Location Z - A standardized code that uniquely identifies the location of facility terminal Z, which has the higher in alphanumeric sequence of the two facility location codes. Valid values are outlined in Telcordia Technologies practice BR 795-100-100 (8 or 11 alphanumeric characters). |
| NOTE 2: | Either virgules (/) or periods (.) are used consistently as delimiters to separate all elements of the CFA. |
| NOTE 3: | All element entries of the CFA are left justified with no trailing spaces. |
| NOTE 4: | When multiple levels of CFA are being provided, the highest level of CFA is populated in the CFA field and the lower level CFA is populated in the SCFA field. |

| USAGE: | This field is conditional. |
| --- | --- |

28a. CFA - Connecting Facility Assignment – CenturyLink-Specific Field - continued

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | The values below are examples only. Example: ALT01.VF-2WIRE.48.ALBQzNMMN.ALBQNMMNHJ1 Or ALT01/VF-2WIRE/48/ALBQNMMN/ALBQNMMNHJ1 Valid CFA format = <CABNM, 1 to 10 a/n><either 1 period char or 1 virgule char><CABTYP, 1 to 13 a/n><either 1 period char or I virgule char><SLOT 1 to 5 a/n><either 1 period char or 1 virgule char><LOCA, 1 to 11 a/n><either 1period char or 1 virgule char><LOCZ, 1 to 11 a/n> CFA_NNNAN where AN = the facility. | This field is required if present on Product Specific form and if Response Type = B, C, D, or X, otherwise not populated. Obtain from Product Specific Form. |

| DATA CHARACTERISTICS: | 54 alphanumeric characters |
| --- | --- |

EXAMPLE:

| 1 | 0 | 1 | / | T | 1 | / | 3 | / | B | S | T | N | M | A | G | T | C | G | O | / | B | S | T | N |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M | A | M | T | K | 3 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

28b. SEC CFA – Secondary Connecting Facility Assignment – CenturyLink-Specific Field

Identifies the customer carrier system and channel to be used from a Wideband Analog or a High Capacity Facility for a thru-connect configuration or for communicating additional carrier system and channel information for Switched Access facilities.

| USAGE: | This field is optional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | O | The values below are examples only. Example: ALT01.VF-2WIRE.48.ALBQNMMN.ALBQNMMNHJ1 Or ALT01/VF-2WIRE/48/ALBQNMMN/ALBQNMMNHJ1 Valid CFA format = <CABNM, 1 to 10 a/n><either 1 period char or 1 virgule char><CABTYP, 1 to 13 a/n><either 1 period char or I virgule char><SLOT 1 to 5 a/n><either 1 period char or 1 virgule char><LOCA, 1 to 11 a/n><either 1period char or 1 virgule char><LOCZ, 1 to 11 a/n> CFA_NNNAN where AN = the facility. |  |

| DATA CHARACTERISTICS: | 54 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| 1 | 0 | 1 | / | T | 1 | / | 3 | / | B | S | T | N | M | A | G | T | C | G | O | / | B | S | T | N |
| M | A | M | T | K | 3 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

28c. LOCNUM - Location Number – CenturyLink-Specific Field

Identifies the number assigned by the co-provider or end-user to this leg of a multipoint circuit. It also may identify an existing leg on a CenturyLink Customer Service Record (CSR).

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | This field is required when the LOCNUM field on the RPL form is populated and Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 3 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 3 |
| --- | --- | --- | --- |

## 4.9	DID DETAILS SECTION – CENTURYLINK - SPECIFIC SECTION

The following fields DTLI through DTNR repeat as a group.

29. DSTN - Disassociated Telephone Number – Not currently used by CenturyLink

Identifies the telephone number disassociated from the DID Telephone Number Range.

29a. DTLI - DID Telephone Line Identifier – CenturyLink-Specific Field

Identifies the lead telephone line assigned to the DID Trunk Group and only applicable for products that use the DRS form.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | NPA-NXX-LLLL | Obtain from the entry on the DRS form if present. Otherwise the entry will contain CenturyLink assigned DID TLIs when Multi-Line Hunting is requested. Valid if Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 12 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | - | 5 | 5 | 5 | - | 1 | 2 | 1 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

29b. DTK - DID Trunk Quantity – CenturyLink-Specific Field

Identifies the quantity of trunks being requested and is only applicable for products that use the DRS form.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | This entry will contain the quantity of CenturyLink DID Trunks ordered. Obtained from the DRS form, if present, and if Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 1 | 0 |
| --- | --- | --- | --- | --- |

29c. DTGN - DID Trunk Group Number – CenturyLink-Specific Field

Identifies the DID Trunk Group Number which has been assigned by the provider and is only applicable for products that use the DRS form.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | 2-4 numerics | This entry will contain the CenturyLink DID Group Number(s). Obtain from the DRS form, if present, and when Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 1 | 2 | 3 |  |
| --- | --- | --- | --- | --- |

29d. DRTI - DID Route Index Number – CenturyLink-Specific Field

Identifies the Route Index Number assigned to the DID Trunk Group Number and is only applicable for products that use the DRS form.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | 2-4 numerics | This entry will contain CenturyLink assigned DID Route Index Number(s) assigned to the DID Trunk Group. Obtain from the DRS form, if present, and if Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 1 | 2 | 3 |  |
| --- | --- | --- | --- | --- |

29e. DTKID - DID Trunk ID – CenturyLink-Specific Field

Identifies the trunk ID of the existing DID service and is only applicable for products that use the DRS form.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | 2-5 alphanumerics For example: ‘DI’ or ‘3001’ | Obtain from the DRS form, if present, and when Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 10 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  |  |  |  |  |  | 3 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

29f. DGOUT - DID Digits Out – CenturyLink-Specific Field

Indicates the number of digits out-pulsed from the Central Office to the customer’s equipment and is only applicable for products using the DRS form.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | Obtain from the DRS form, if present, and when Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 2 numeric characters |
| --- | --- |

| EXAMPLE: |  | 3 |
| --- | --- | --- |

29g. DTNR - DID Telephone Number Range – CenturyLink-Specific Field

Identifies the range of DID telephone numbers within the same switch and is only applicable for products that use the DRS form.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | For a single TN, the format is: NPA-NXX-LLLL (12 characters) For a range of TNs, the format is: NPA-NXX-LLLL-HHHH (17 characters), where L and H are numeric and HHHH is always greater than LLLL. Dashes are required in positions 4 and 8. If a range is used, a dash is also required in position 13. | This field will contain the range of DID telephone numbers. Obtain from the DRS form if present and when Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 17 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | - | 5 | 5 | 5 | - | 1 | 2 | 1 | 2 | - | 1 | 3 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

## 4.10	VIRTUAL RELATED CIRCUIT DETAIL

Virtual Related Circuit Detail repeats as a group from LNEX to RDLCI

29h. LST – Local Service Termination – CenturyLink-Specific Field

Identifies the CLLI code of the end office switch from which service is being provided.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | For Resale Frame Relay only and if Response Type = C, D, or X, otherwise not populated. CenturyLink assigned to indicate the Resale Frame Relay switch. |

| DATA CHARACTERISTICS: | 11 alphanumeric characters |
| --- | --- |

| EXAMPLE: | C | H | Y | N | W | Y | M | A | D | S | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

29i. LNEX- Line Number Extension Number – CenturyLink-Specific Field

Identifies the additional telephone number, virtual circuit or related virtual circuit as a unique number and each additional occurrence as a unique number.

| NOTE 1: | LNEX is customer assigned and is returned on the Local Response (LR) to the customer. |
| --- | --- |
| NOTE 2: | Once LNEX is generated, it cannot be changed and is retained through completion of the request. |
| NOTE 3: | The values are to be assigned consecutively and must be unique throughout the request at the LNUM level. |

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | The LNEX is CLEC assigned and returned on the LR form to the CLEC. For Resale Frame Relay only. Obtain from the Resale Frame Relay form if Response Type = C, D, or X otherwise not populated. |

| DATA CHARACTERISTICS: | 5 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 0 | 1 | 0 |
| --- | --- | --- | --- | --- | --- |

29j. DLCI - Data Link Connection Identifier – CenturyLink-Specific Field

Identifies the logical connection address between CenturyLink’s switch and the ECCKT.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | Only for Resale Frame Relay if Response Type = C, D, or X, otherwise not populated Obtain from the Resale Frame Relay form (if present), otherwise CenturyLink assigned. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 1 | 6 |
| --- | --- | --- | --- | --- |

29k. CIR – Committed Information Rate – CenturyLink-Specific Field

Identifies the rate of ingress traffic across the ECCKT under normal conditions.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | For Resale Frame Relay only and if Response Type = C, D, or X, otherwise not populated. Obtained from the Resale Frame Relay form (if present), otherwise CenturyLink assigned or manually corrected if invalid. |

| DATA CHARACTERISTICS: | 5 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  |  | 1 | 6 | K |
| --- | --- | --- | --- | --- | --- |

29l. Be – Excess Burst Size – CenturyLink-Specific Field

Identifies the maximum amount of data that a user is permitted to offer to the network that exceeds Bc during time interval (Tc) across the ECCKT.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | For Resale Frame Relay only if Response Type = C, D, or X, otherwise not populated. Obtain from the Resale Frame Relay form (if present) or manually corrected if invalid. |

| DATA CHARACTERISTICS: | 5 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  |  | 2 | 4 | K |
| --- | --- | --- | --- | --- | --- |

29m. RPON – Related Purchase Order Number – CenturyLink-Specific Field

Identifies the PON, which is establishing the physical connection for this end of the virtual connection.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | For Resale Frame Relay only and if Response Type = C, D, or X, otherwise not populated. Obtain from the Resale Frame Relay form (if present). |

| DATA CHARACTERISTICS: | 16 alphanumeric characters |
| --- | --- |

| EXAMPLE: | R | E | C | 1 | 2 | 3 | 4 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

29n. RECCKT - Related Exchange Company Circuit Identification – CenturyLink-Specific Field

Identifies CenturyLink’s related physical circuit ID against which the VC activity is requested.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | For Resale Frame Relay only and If Response Type = C, D, or X, otherwise not populated. Obtained from the Resale Frame Relay form (if present). |

| DATA CHARACTERISTICS: | 42 alphanumeric characters |
| --- | --- |

EXAMPLE:

| 1 | 1 | H | W | D | K | 0 | 1 | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

29o. RORD – Related Order Number – CenturyLink-Specific Field

Identifies CenturyLink’s order number that is establishing the physical link.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | For Resale Frame Relay only and if Response Type = C, D, or X, otherwise not populated. Obtain from the Resale Frame Relay form (if present) or CenturyLink generated or manually corrected. |

| DATA CHARACTERISTICS: | 10 alphanumeric characters |
| --- | --- |

| EXAMPLE: | C | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

29p. RDLCI - Related Data Link Connection Identifier – CenturyLink-Specific Field

Identifies the logical connection address between CenturyLink’s switch and the RECCKT.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | For Resale Frame Relay only and if Response Type = C, D, or X, otherwise not populated. Obtained from the Resale Frame Relay form (if present). |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 1 | 7 |
| --- | --- | --- | --- | --- |

30. BI1 - Billing Account Number Identifier 1

Identifies the service type of the Billing Account Number 1 (BAN1).

VALID ENTRIES:

A = All services on this request – Not currently used by CenturyLink

C = Directory Assistance listings and directory listings – Not currently used by CenturyLink

D = Directory listings – Not currently used by CenturyLink

L = Loop

M = Combined loop and unbundled local switching (port) – Not currently used by CenturyLink

N = Number Portability (NP) – Not currently used by CenturyLink

O = Directory Assistance listings – Not currently used by CenturyLink

P = Port – Not currently used by CenturyLink

R = Resale – Not currently used by CenturyLink

U = Usage – Not currently used by CenturyLink

V = Loop with NP and usage – Not currently used by CenturyLink

W = Loop with NP – Not currently used by CenturyLink

X = CENTREX resale – Not currently used by CenturyLink

Z = NP with usage – Not currently used by CenturyLink

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | See Valid Entries | This field is required if present on the LSR. Obtained from the LSR form if Response Type = B, C, D, or X, otherwise not populated. |

| DATA CHARACTERISTICS: | 1 alpha character |
| --- | --- |

| EXAMPLE: | L |
| --- | --- |

31. BAN1 - Billing Account Number 1

Identifies the billing account to which the recurring and non-recurring charges for this request will be billed.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | Dashes are returned in positions four and eight. A dash is returned in position 13 when an extension is included. | This field is required if present on LSR form and if Response Type = B, C, D, or X, otherwise not populated. Obtained from the LSR Form or CenturyLink generated if newly created or changed during the service order process. IMA will auto-correct the entry on flow through requests if the original BAN provided is changed when processed by the SOP. PIA should be set to 4 and a remark should be entered indicating the BAN was changed. |

| DATA CHARACTERISTICS: | 16 alphanumeric characters |
| --- | --- |

| EXAMPLES: | 1 | 2 | 3 | - | Z | 4 | 5 | - | 6 | 7 | 8 | 9 | - | 1 | 2 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

|  | 5 | 2 | 0 | - | B | 1 | 1 | - | 1 | 2 | 3 | 4 | - | 1 | 2 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

32. BI2 - Billing Account Number Identifier 2

Identifies the service type of the Billing Account Number 2 (BAN2).

VALID ENTRIES:

A = All services on this request – Not currently used by CenturyLink

C = Directory Assistance listings and directory listings – Not currently used by CenturyLink

D = Directory listings – Not currently used by CenturyLink

L = Loop – Not currently used by CenturyLink.

M = Combined loop and unbundled local switching (port) – Not currently used by CenturyLink

N = INP

O = Directory Assistance listings – Not currently used by CenturyLink

P = Port – Not currently used by CenturyLink

R = Resale – Not currently used by CenturyLink

U = Usage – Not currently used by CenturyLink

V = Loop with NP and usage – Not currently used by CenturyLink

W = Loop with NP – Not currently used by CenturyLink

X = CENTREX resale – Not currently used by CenturyLink

Z = NP with usage – Not currently used by CenturyLink

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | See Valid Entries | This field is required if present on the LSR if Response Type = B, C, D, or X, otherwise not populated. Obtained from the LSR form. |

| DATA CHARACTERISTICS: | 1 alpha character |
| --- | --- |

| EXAMPLE: | N |
| --- | --- |

33. BAN2 - Billing Account Number 2

Identifies the billing account to which the recurring and non-recurring charges for this request will be billed.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | Valid Billing Account Number Dashes are returned in positions four and eight. A dash is returned in position 13 when an extension is included. | This field is returned if present on the LSR and if Response Type = B, C, D, or X, otherwise not populated. Obtained from the LSR Form or CenturyLink generated if newly created or changed during the service order process. IMA will auto-correct the entry on flow through requests if the original BAN provided is changed when processed by the SOP. PIA should be set to 4 and a remark should be entered indicating the BAN was changed. |

| DATA CHARACTERISTICS: | 16 alphanumeric characters |
| --- | --- |

| EXAMPLES: | 1 | 2 | 3 | - | Z | 4 | 5 | - | 6 | 7 | 8 | 9 | - | 1 | 2 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 5 | 2 | 0 | - | B | 1 | 1 | - | 1 | 2 | 3 | 4 | - | 1 | 2 | 3 |

34. EC VER - Exchange Carrier Version

Identifies CenturyLink’s initiated response type and the version of the response.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Cancel, Error, Jeopardy, Reject | C | The first two characters identify the version (01-99). The third character identifies the response reason. C = Correction R = Resend J = Jeopardy Not Populated Example: 01C | Populated when an initial automatic or manual FOC, JEP, Error, Reject or Cancel is generated for a CCNA/PON/VER. Required if Response Type = B, C, D, X, E, J, V, and Z. Prohibited if Response Type = N. Populate the first two bytes (left justified) “01” when an initial automatic or manual FOC, JEP, Error, Reject or Cancel is generated for a CCNA/PON/VER. The version number increases by one for each notice type sent (except notice type N) within the CCNA/PON/VER. |

| DATA CHARACTERISTICS: | 3 alphanumeric characters |
| --- | --- |

| EXAMPLES: | 0 | 1 | C |
| --- | --- | --- | --- |

35. RCODE - Reason Code – Not currently used by CenturyLink

Identifies the reason the order may not meet the requested Due Date at confirmation and/or Post Confirmation.

36. RDET - Reason Jeopardy Code Detail – Not currently used by CenturyLink

Identifies the CenturyLink two or three-character JEP code followed by the description associated to the CenturyLink assigned jeopardy code.

37. ESDD - Estimated Due Date – Not currently used by CenturyLink

Identifies the estimated due date associated with the delayed order/jeopardy.

38. AFVR - Additional Field Visit Required – Not currently used by CenturyLink

Identifies if a field visit is required at the customer/end-user location, which requires arrangements to be established.

39. DSGCON - Design/Engineering Contact

Identifies the representative of the customer or agent that should be contacted on design/engineering matters.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | This field is required if present on the LSR if Response Type = B, C, D, or X, otherwise not populated. Obtained from the LSR form. |

| DATA CHARACTERISTICS: | 15 alphanumeric characters |
| --- | --- |

| EXAMPLE: | J | O | H | N |  | S | M | I | T | H |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

40. NSP DSGCON -Network Service Provider (NSP) Design/Engineering Contact

Identifies the representative of CenturyLink that should be contacted on design/engineering matters.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | This field is returned if RT = D or X, otherwise not populated. CenturyLink generated. |

| DATA CHARACTERISTICS: | 15 alphanumeric characters |
| --- | --- |

| EXAMPLE: | J | U | D | Y |  | J | O | N | E | S |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

41. TEL NO - Telephone Number

Identifies the telephone number of CenturyLink’s design/engineering contact.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | Dashes are required in positions four and eight, and position 13 if applicable. | This field is returned if DSGCON is present, otherwise not populated. CenturyLink generated. |

| DATA CHARACTERISTICS: | 17 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | - | 1 | 2 | 3 | - | 4 | 5 | 6 | 7 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

42. ONSP - Old Network Service Provider Identification – Not currently used by CenturyLink

Identifies the NPAC SPI of the current Network Service Provider.

43. TDTR - Ten Digit Trigger Response – Not currently used by CenturyLink

Indicates the activation of a ten-digit trigger for local routing number portability.

## 4.11	HUNT GROUP SECTION

44. LOCNUM - Location Number – Not currently used by CenturyLink

Identifies this service location number for the service requested.

45. HNUM - Hunt Line Number – Not currently used by CenturyLink

Identifies the Hunt Line number.

46. HID - Hunt Group Identifier – Not currently used by CenturyLink

Identifies the hunt group.

47. TLI - Telephone Line Identifier – Not currently used by CenturyLink

Identifies the pilot number of a multi-line hunt group.

48. HTSEQ - Hunt Sequence – Not currently used by CenturyLink

Identifies the desired hunting sequence.

## 4.12	CIRCUIT DETAIL SECTION

49. LNUM - Line Number – Not currently used by CenturyLink

Identifies the line or trunk as a unique number and each additional occurrence of either as a unique number.

50. RNUM – Reference Number – Not currently used by CenturyLink

Identifies each group as a unique number and each additional group as a unique number.

51. LNEX - Line Number Extension Number – Not currently used by CenturyLink

Identifies the additional telephone number, virtual circuit or related virtual circuit as a unique number and each additional occurrence as a unique number.

52. LEGNUM - Multipoint Leg Number – Not currently used by CenturyLink

Identifies the number assigned by the customer to this leg of a multipoint circuit.

53. ECCKT - Exchange Company Circuit ID – Not currently used by CenturyLink

Identifies a provider’s circuit identification.

54. DSN - Dialable Station Number – Not currently used by CenturyLink

Identifies the dialable 1-7 digit Station Digit Dialing number.

55. LTC - Line Treatment Code – Not currently used by CenturyLink

Identifies the unique treatment profile code required for this line, when the CENTREX Common Block contains more than one treatment code.

56. NOTYP - Number Type – Not currently used by CenturyLink

Identifies the type of telephone number entered in the TNS or OTN fields.

57. TNS - Telephone Numbers – Not currently used by CenturyLink

Identifies the telephone number or consecutive range of telephone numbers for this request.

58. PID - Personal Identifier – Not currently used by CenturyLink

Identifies the authorization number to be utilized with the telephone number provided in the SAT field.

59. SAT - Subscriber Access Telephone Number – Not currently used by CenturyLink

Identifies the telephone number, which allows remote access to make feature configuration changes.

60. CKR - Customer Circuit Reference – Not currently used by CenturyLink

Identifies the circuit number assigned by the customer.

61. CFA - Connecting Facility Assignment – Not currently used by CenturyLink

Identifies the CenturyLink carrier system and channel to be used.

62. ORDL - Loop Order Number – Not currently used by CenturyLink

Identifies the provider's order number for the loop.

63. NPORD - Number Portability Order Number – Not currently used by CenturyLink

Identifies the provider's order number for number portability.

64. DISC ECCKT – Disconnect ECCKT – Not currently used by CenturyLink

Identifies the end-user ECCKT to be disconnected.

65. DISC ORD - Disconnect Order Number – Not currently used by CenturyLink

Identifies the provider's order number for the disconnect of end-user service associated with this request.

4.10.1	Tie Down

66. SYSTEM ID - System Identification – Not currently used by CenturyLink

Identifies the customer's system to be used in a collocation arrangement.

67. SHELF – Shelf – Not currently used by CenturyLink

Identifies the number assigned to the customer's shelf to be used in a collocation arrangement.

68. SLOT – Slot – Not currently used by CenturyLink

Identifies the customer's specific connection slot to be used in a collocation arrangement.

69. SPORT – Slot Port – Not currently used by CenturyLink

Identifies the customer’s specific connection port of the slot to be used in a collocation arrangement.

70. RELAY RACK - Relay Rack – Not currently used by CenturyLink

A code that identifies the bay/cabinet in a central office and may include the floor and aisle where the specific piece of equipment is located.

71. UNIT – Unit – Not currently used by CenturyLink

Identifies the number assigned to a panel, shelf or case within the bay/cabinet indicated in the relay rack field.

72. CTI - Connection Type Indicator – Not currently used by CenturyLink

Identifies the configuration of the facility connection assignment.

73. CABLE ID - Cable Identification – Not currently used by CenturyLink

Identifies the provider’s central office cable to be connected to the customer’s collocated equipment.

74. CBCID - Cross Box Cable Identification – Not currently used by CenturyLink

Identifies the provider’s cable to be connected to the customer’s terminal in a field location.

75. CHAN/PAIR - Channel/Pair – Not currently used by CenturyLink

Identifies the specific channel or pair within the provider's cable to be used for connection.

4.10.2	Facility Transmission

76. PGI - Pair Gain Indicator – Not currently used by CenturyLink

Indicates whether pair gain will be used for this service.

77. DEMARC - Demarc Designation – Not currently used by CenturyLink

Identifies the point where the provider terminates service at the end user premises.

78. OOR - Out of Range Indicator – Not currently used by CenturyLink

Identifies the loop as out of range and additional engineering and/or an extended range card may be required.

79. NID - Network Interface Device – Not currently used by CenturyLink

Indicates if the existing network interface device (NID) will be reused.

## 4.13	SECLOC SECTION

80. LNUM - Line Number – Not currently used by CenturyLink

Identifies the line or trunk as a unique number and each additional occurrence as a unique number.

81. LNEX - Line Number Extension Number – Not currently used by CenturyLink

Identifies the additional telephone number, virtual circuit or related virtual circuit as a unique number and each additional occurrence as a unique number.

82. DLCI - Data Link Connection Identifier – Not currently used by CenturyLink

Identifies the logical connection address between CenturyLink’s switch and the ECCKT.

83. RECCKT - Related Exchange Company Circuit Identification – Not currently used by CenturyLink

Identifies CenturyLink’s related physical circuit ID against which the VC activity is requested.

84. LST - Local Service Termination – Not currently used by CenturyLink

Identifies the CLLI code of the end office switch from which service is being provided.

85. RDLCI - Related Data Link Connection Identifier – Not currently used by CenturyLink

Identifies the logical connection address between CenturyLink’s switch and the RECCKT.

## 4.14	DIRECTORY SECTION

86. ATN - Account Telephone Number – Not currently used by CenturyLink

Identifies the main telephone number used to associate the main listing with any additional listings. CenturyLink has chosen to use AN field in place of ATN.

87. DOR - Date of Receipt – Not currently used by CenturyLink

Identifies the date this directory service request was received.

## 4.15	LISTINGS SECTION

This is a repeating section.  DLNUM through LNFN repeats as a group.

89. DLNUM - Directory Listing Number

Identifies each listing within a request with a unique number.

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- |

90. ALI - Alphanumeric Listing Identifier Code

Identifier assigned to uniquely identify each non-main listing for an account.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | C |  | Not populated when RTY is LML |

| DATA CHARACTERISTICS: | 6 alphanumeric characters |
| --- | --- |

| EXAMPLE: | A | Q |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |

91. LTN – Listed Telephone Number

Identifies the telephone number that may be included in the directory and/or Directory Assistance (DA).

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | C |  | Not populated when NSTN is populated |

| DATA CHARACTERISTICS: | 10 numeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | 5 | 5 | 5 | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

92. NSTN - Non Standard Telephone Number

Identifies a telephone number which is not in the standard North American Numbering Plan format, e.g., vanity numbers, Enterprise, 911.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | C |  | Not populated when LTN is populated |

| DATA CHARACTERISTICS: | 20 alphanumeric characters |
| --- | --- |

| EXAMPLES: |
| --- |
| 3 | 0 | 3 |  | 8 | 9 | 6 | - | C | * | A | * | S | * | H |  |  |  |  |  |
| 1 |  | 8 | 0 | 0 |  | F | * | O | * | R | - | H | * | E | * | L | * | P |  |
| 9 | 1 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

93. LACT - Listing Activity Indicator

Identifies the activity involved for this listing request.

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R | N = New listing D = Delete listing I = Change listing (new data to be inserted O = Change listing (old data) Z = No change to listing (recap) |  |

| DATA CHARACTERISTICS: | 1 alpha character |
| --- | --- |

EXAMPLES:

N

94. LTY - Listing Type – Not currently used by CenturyLink

Identifies the type of listing with respect to publication and Directory Assistance (DA) appearance rules.

95. STYC - Style Code – Not currently used by CenturyLink

Identifies whether the listing format is straight-line, Straight-line Under (SLU) header, or caption/SLU indent.

96. TOA – Type of Account – Not currently used by CenturyLink

Identifies the type of account for this listing.

97. DOI - Degree of Indent – Not currently used by CenturyLink

Identifies the degree of indentation for this listing which is the number of character spaces to the right of the margin.

98. WPP - White Page Products – Not currently used by CenturyLink

Identifies information about the White Page Products, Signature Listings, Personality Logo and Lines of Distinction.

99. DIRIDL - Directory Identifier – Not currently used by CenturyLink

Identifies the directory in which to place the listing.

100. DIRSUB - Directory Subsection – Not currently used by CenturyLink

Identifies the community name for the subsection of a multiple sectioned directory other than the publisher assigned default section in which to place the listing.

101. LISTNM – Listed Name – Not currently used by CenturyLink

Identifies the name contained in the listing.

102. LNLN – Listed Name Last Name

Indicates the first word for business listings or the complete last name for residence listings.

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 50 alphanumeric characters |
| --- | --- |

| EXAMPLES: |
| --- |
| A | m | e | r | i | c | a | n |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

| K | i | l | e | y | - | S | m | i | t | h |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| S | a | i | n | t |  | J | a | m | e | s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

103. LNFN - Listed Name First

Indicates all except the first word for business listings or all of the first name or names and middle name/initials for residence listings.

| NOTE 1: | Identifies the continuation of the name for business and government listings. |
| --- | --- |
| NOTE 2: | For residence listings it identifies the first name(s), middle name(s) and initials. |

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | C |  |  |

| DATA CHARACTERISTICS: | 100 alphanumeric characters |
| --- | --- |

| EXAMPLES: |
| --- |
| R | e | d |  | C | r | o | s | s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

| A | n | n | e |  | m | * | d |  | & |  | J | a | c | k |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

104. LISTADR – Listed Address - Not currently used by CenturyLink

Identifies the entire address as it is to be listed.

105. LTXNUM - Line of Text Reference Number – Not currently used by CenturyLink

Identifies each line of information for a listing with a unique number.

106. LTXTY - Listing Text Type – Not currently used by CenturyLink

Identifies the type of the associated text that will appear in the directory to assist the end user.

107. LPHRASE - Listing Phrase – Not currently used by CenturyLink

Identifies a pre-defined phrase associated with a listing.

108. LTEXT - Listing Text – Not currently used by CenturyLink

Identifies the descriptive, informative, or indent text that will appear in the directory.

109. DIRSTAT – Directory Order Status – Not currently used by CenturyLink

Identifies the status of the directory order.

## 4.16	LISTING ERROR DETAILS SECTION

This is a repeating section within the Listing Error Details Section.  DLLEREFNUM through REMARKS repeats as a group.

110. DLLEREFNUM – DL Listing Confirmation/Error Code Reference Number

DL Listing Confirmation/Error Code reference number.

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 2 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 0 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

111. LECODE – Listing DL Confirmation/Error Code

Identifies a listing level Confirmation/Error code.

VALID ENTRIES:

|  |  | Character 1 will always be ‘U’ representing CenturyLink Character 2 will represent whether the Error was created out of the Listing Interface or the Listing Database: I = Interface L = Listing Database NOTE: Interface Confirmation/Error Codes are not processed to the listing database. Character 3-5 represents the Confirmation/Error Code Character 6 represents the status condition for each Confirmation/Error Code: A = Advice - Listing database has been updated; however, some of the data may have been discarded or assumed. Provider follow-up. C = Confirmed – No Error F = Fatal – No Update to Listing Database – Provider follow-up. R = Fatal – No Update to Listing Database – CenturyLink follow-up. N = Partial – Listing Database updated – may be in error – Requires Provider Follow-Up and may require a new PON to correct Database P = Partial – Listing database has been updated; however, some of the data may be in error. CenturyLink follow-up. |
| --- | --- | --- |

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 6 alphanumeric characters |
| --- | --- |

| EXAMPLE: | U | I | 0 | 0 | 0 | C |
| --- | --- | --- | --- | --- | --- | --- |

111a. REMARKS – Remarks – CenturyLink-specific field

Contains the DL Confirmation/Error Code Text/Message associated with the respective error code.

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 1000 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| D | I | S | C |  | O | F |  | F | I | R | S | T |  | C | K | T |  | I | N |  | G | R | O | U |
| P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

## 4.17	PON LISTING ERROR SECTION

This is a repeating section within the PON Listing Error Section.  PONLEREFNUM* through REMARKS repeats as a group.

112. PONLEQTY – Not currently used by CenturyLink

Identifies the number of listing response segments on the PON containing confirmation and error detail information.

113. PONLEREFNUM – PON Listing Confirmation/Error Code Reference Number

Identifies the PON Listing Error Code reference number.

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 2 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 0 | 2 |
| --- | --- | --- |

114. LECODE - Listing PON Confirmation/Error Code

Identifies the FBDL Order Status and may include PON level error codes.

| USAGE: | This field is required. |
| --- | --- |
|  |  | The first six character code represents the overall FBDL Order Status: AC – Processed With Changes/Errors-CenturyLink Follow Up AD – Processed With Changes/Errors-Provider Follow Up AT – Confirmed Update On PON RF – Fatal Update On PON If PON level errors occur, they will be represented as follows: Character 1 will always be ‘U’ representing CenturyLink Character 2 will represent whether the error was created out of the Listing Interface or the Listing Database: I = Interface L = Listing Database NOTE: Interface Confirmation/Error Codes are not processed to the listing database. Character 3-5 represents the Confirmation/Error code Character 6 represents the status condition for each Confirmation/Error code: A = Advice - Listing Database may have been updated; however, some of the data may have been discarded or assumed. Provider follow-up. C = Confirmed – No Error F = Fatal – No Update to Listing Database – Provider follow-up R = Fatal – No Update to Listing Database – CenturyLink follow-Up N = Partial – Listing database has been updated; however, some of the data may be in error. Provider follow-up. P = Partial – Listing database has been updated; however, some of the data may be in error. CenturyLink follow-up. |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R |  |  |

| DATA CHARACTERISTICS: | 6 alphanumeric characters |
| --- | --- |

| EXAMPLE: | U | L | A | T | 0 | C |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

114a. REMARKS – Remarks – CenturyLink-specific field

Contains the PON Confirmation/Error Code Text/Message associated with the respective Confirmation/Error code.

| USAGE: | This field is required. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| REQTYP=JB Notices only, refer to RT field #18 | R |  | Required if 114-LECODE is populated, otherwise not required. |

| DATA CHARACTERISTICS: | 1000 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| D | I | S | C |  | O | F |  | F | I | R | S | T |  | C | K | T |  | I | N |  | G | R | O | U |
| P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

115. ORDC – Order Response Code Detail – Not currently used by CenturyLink

Provides a description of the response code.

116. LRNUM – Local Response Number – Not currently used by CenturyLink

Identifies each listing response segment with a unique number.

117. LRC – Listing Response Code – Not currently used by CenturyLink

Identifies a confirmation and/or error code for the listing.

118. LRCD – Listing Response Code Detail – Not currently used by CenturyLink

Provides a description of the response code.

## 4.18	BULK REQUEST TO CREATE LSR CONFIRMATION SECTION (GUI 			Only)

NOTE: The following fields 94a through 94e do not appear on the Local Response Form accompanying this document.

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = W. This section BNUM through LSR ID repeats BULK QTY NUM of times. |

118a. Bulk QTY NUM – CenturyLink - Specific Field

Identifies the quantity of individual LSRs for the Bulk Request to create LSRs.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | 001-100 | Generated by CenturyLink. Required if RT = W. |

| DATA CHARACTERISTICS: | 3 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 1 |
| --- | --- | --- | --- |

118b. BNUM – Bulk Reference Number – CenturyLink - Specific Field

Identifies the DISC NBR as a unique number and each additional occurrence as a unique number

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | 001-100 | Generated by CenturyLink. Required if BULK QTY NUM is not populated, otherwise not populated. Starts at 1 and increments sequentially by 1. Repeats BULK QTY NUM of times. |

| DATA CHARACTERISTICS: | 3 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 1 |
| --- | --- | --- | --- |

118c. PON – Purchase Order Number – CenturyLink - Specific Field

Identifies the Purchase Order Number of the individual LSR.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | This field is required if BNUM is populated. Generated by CenturyLink for each individual LSR. Repeats BULK QTY NUM of times. |

| DATA CHARACTERISTICS: | 16 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 8 | 2 | 4 | Z | 9 |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

118d. TN – Telephone Number – CenturyLink - Specific Field

Identifies the Telephone Number of the individual LSR.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | Dashes are required in positions 4 and 8. | This field is required if BNUM is populated. Repeats BULK QTY NUM of times. |

| DATA CHARACTERISTICS: | 12 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 0 | 3 | - | 3 | 2 | 1 | - | 0 | 1 | 0 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

118e. LSR ID – Local Service Request Identification – CenturyLink - Specific Field

Identifies the LSR ID for the individual LSR.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C |  | This field is required if BNUM is populated. Repeats BULK QTY NUM of times. |

| DATA CHARACTERISTICS: | 11 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 3 | 2 | 2 | 2 | 2 | 5 | 6 |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

## 4.19	SERVICE AND EQUIPMENT SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. This section applies for each Service Order when available. ACTION CODE through FID may repeat as a group. |

118f. ACTION CODE – Action Code – CenturyLink-Specific Field

Identifies the action and quantity associated with the USOC.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | 1st character - alpha action code: C = Change From I = In O = Out T = To D = Delete E = Enter R = Recap (Eastern/Western region) Not Populated = Recap (Central region) 2nd character - numeric quantity. | Valid when orders exist for the LSR and S&E data is available. This field is required if BNUM is populated. Repeats BULK QTY NUM of times. |

| DATA CHARACTERISTICS: | 2 alphanumeric characters |
| --- | --- |

| EXAMPLE: | C | 2 |
| --- | --- | --- |

118g. USOC – Universal Service Order Code – CenturyLink-Specific Field

A code that is associated with a charge for the service. CenturyLink utilizes USOC and field identifiers to provision, bill and maintain services and equipment.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Valid when orders exist for the LSR and S&E data is available. |

| DATA CHARACTERISTICS: | 999 alphanumeric characters |
| --- | --- |

| EXAMPLE: | E | X | L | C | N |
| --- | --- | --- | --- | --- | --- |

118h. FID – Feature Identifier – CenturyLink-Specific Field

Identifies additional information for the type of feature associated with the line.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Valid when orders exist for the LSR and S&E data available. |

| DATA CHARACTERISTICS: | 999 alphanumeric characters (character string for multiple FIDs) |
| --- | --- |

| EXAMPLE: |
| --- |
| A | C | N | A |  | C | A | B | I |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

## 4.20	LINE INFORMATION SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. Within this section, fields REF NUM through HID repeat as a group. |

118i. REF NUM – Reference Number – CenturyLink-Specific Field

Identifies the line or trunk as a unique number and each additional occurrence as a unique number.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Required if present on Product Specific form. REF NUM should be sequential and incremented by 1. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 0 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- |

118j. HID – Hunt Group Identifier – CenturyLink-Specific Field

Identifies the hunt group.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Required if present on LSR form. |

| DATA CHARACTERISTICS: | 5 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 1 | 2 | 3 | 4 | A |
| --- | --- | --- | --- | --- | --- |

## 4.21	DID DISASSOCIATED SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. The following field is a repeating field. |

119. DSTN – Disassociated Telephone Number – Not currently used by CenturyLink

Identifies the telephone number disassociated from the DID Telephone Number Range.

## 4.22	DID TELEPHONE NUMBER SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. The following fields (DTLI through DGOUT) repeat as a group. This group shall appear within the Order section. |

119a. DTLI – DID Telephone Line Identifier – CenturyLink-Specific Field

Identifies the lead telephone line assigned to the DID Trunk Group.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Required if DID TLI(s) are involved in the service order. |

| DATA CHARACTERISTICS: | 12 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 1 | 2 | 3 | - | 4 | 5 | 6 | 7 | - | 8 | 9 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

119b. DTK – DID Trunk Quantity – CenturyLink-Specific Field

Identifies the quantity of trunks being requested.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Required if DID trunks are involved in the service order. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |

119c. DTGN – DID Trunk Group Number – CenturyLink-Specific Field

Identifies the DID Trunk Group Number which has been assigned by the provider.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Required if DID trunks are involved in the service order. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |

119d. DRTI – DID Route Index Number – CenturyLink-Specific Field

Identifies the Route Index Number assigned to the DID Trunk Group Number.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Required if DID trunks are involved in the service order. |

| DATA CHARACTERISTICS: | 4 numeric characters |
| --- | --- |

| EXAMPLE: | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |

119e. DTKID – DID Trunk ID – CenturyLink-Specific Field

Identifies the trunk ID of the existing DID service.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Required if DID trunks are involved in the service order. |

| DATA CHARACTERISTICS: | 10 alphanumeric characters |
| --- | --- |

| EXAMPLE: | A | B | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

119f. DGOUT – DID Digits Out – CenturyLink-Specific Field

Indicates the number of digits outpulsed from the Central Office to the customer’s equipment.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Required if DID trunks are involved in the service order. |

| DATA CHARACTERISTICS: | 2 numeric characters |
| --- | --- |

| EXAMPLE: | 1 | 2 |
| --- | --- | --- |

## 4.23	DID RANGE SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. The following field is a repeating field. |

119g. DTNR – DID Telephone Number Range – CenturyLink-Specific Field

Identifies the range of DID telephone numbers within the same switch.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C |  | Required if range(s) of DID TN (s) are involved in the service order. |

| DATA CHARACTERISTICS: | 17 alphanumeric characters |
| --- | --- |

| EXAMPLE: | 1 | 2 | 3 | - | 4 | 5 | 6 | 7 | - | 8 | 9 | 0 | - | 8 | 9 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

## 4.24	LISTINGS SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. This section applies for each Service Order when there is activity for this section. ACTION CODE through LHLFIDDATA may repeat as a group. |

119h. ACTION CODE – Action Code – CenturyLink-Specific Field

Identifies the action code associated with the Listing FID.

| USAGE: | This field is optional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | O | I = In O = Out R = Recap (Eastern/Western region) Not Populated = Recap (Central region) | Required when listings exist for the LSR and Listing data is available. |

| DATA CHARACTERISTICS: | 1 alphanumeric characters |
| --- | --- |

| EXAMPLE: | I |
| --- | --- |

119i. LHLFID – Left Hand Listing Field Identifier – CenturyLink-Specific Field

This field contains a Listing field identifier. Note: In XML, this field is identified as LFID.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | LN, NP, NLST, NL, LA, SA, LOC, AC, AL, AM, AML, ASL, CML, CR, EUN, EL, ENT, ENU, FL, JU, NT, SL, SRL, XL, TN. | Required when listings exist for the LSR and Listing data is available. |

| DATA CHARACTERISTICS: | 5 alphanumeric characters |
| --- | --- |

| EXAMPLE: | E | U | N |
| --- | --- | --- | --- |

119j. LHLFIDDATA – Left Hand Listing Field Identifier Data – CenturyLink-Specific Field

This field provides additional information about the Left Handed Listing FID. Note: In XML, this field is identified as LFID_DATA.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | DOI, DST, FOL, LNR, NON LIST, NON LODA, NON PUB, NSOL, OAD, OATD, OCLS, OFEM, OTDM, OTML, PLA, PRE, SPNP. (Plus Free form text or Number format –Dashes included) | Required when listings exist for the LSR and Listing data is available. |

| DATA CHARACTERISTICS: | 999 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| D | O | I | - | 2 |  | O | A | T | D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

## 4.25	BILLING SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. This section applies for each Service Order when there is activity for this section. ACTION CODE through LHBFIDDATA may repeat as a group.. |

119k. ACTION CODE – Action Code – CenturyLink-Specific Field

Identifies the action code associated with the Billing FID.

| USAGE: | This field is optional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | O | O = Out (Central region) Not Populated = In (Central region) | Only returned in the Central Region. |

| DATA CHARACTERISTICS: | 1 alphanumeric characters |
| --- | --- |

| EXAMPLE: | O |
| --- | --- |

119l. LHBFID – Left Handed Bill Field Identifier – CenturyLink-Specific Field

This field contains a Billing field Identifier. Note: In XML, this FID is identified as LFID

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | BN1, BN2, CBN1, CBN2, BA1, CBA1, BA2, BA5, CBA2, CBA5, PO, PON, EBD, BTN, CCN, CCL, CCON, NRC, SB, NEC, NRAC, NRS, NRSC, NRTC, SOC. | Required when Billing exists for the LSR and Billing data available. |

| DATA CHARACTERISTICS: | 5 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  | C | B | A | 1 |
| --- | --- | --- | --- | --- | --- |

119m. LHBFIDDATA – Left Handed Bill Field Identifier Data – CenturyLink-Specific Field

This field provides additional information about the Left Handed Billing FID. Note: In XML, this FID is identified as LFID DATA

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | Free form text or Number format – Dashes included. | Required when Billing exists for the LSR and Billing data available. |

| DATA CHARACTERISTICS: | 999 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| A | B | C | - | 2 |  | D | E | F | G |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

## 4.26	TRAFFIC SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. This section applies for each Service Order when there is activity for this section. ACTION CODE through LHTFIDDATA may repeat as a group. |

119n. ACTION CODE – Action Code – CenturyLink - Specific Field

Identifies the action code associated with the Traffic FID.

| USAGE: | This field is optional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | O | Not Populated = In |  |

| DATA CHARACTERISTICS: | 1 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  |
| --- | --- |

119o. LHTFID – Left Hand Traffic Field Identifier – CenturyLink-Specific Field

This field contains a Traffic field identifier. Note: In XML, this FID is identified as LFID

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | TC, TCI, TCP, TCS | Required when Traffic exists for the LSR and Traffic data available. |

| DATA CHARACTERISTICS: | 5 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  |  | T | C | P |
| --- | --- | --- | --- | --- | --- |

119p. LHTFID DATA – Left Hand Traffic Field Identifier Data– CenturyLink-Specific Field

This field provides additional information about the Left Handed Traffic FID. Note: In XML, this FID is identified as LFID DATA.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | Free form text, Date Format | Required when Traffic exists for the LSR and Traffic data available. |

| DATA CHARACTERISTICS: | 999 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| A | B | C | - | 2 |  | D | E | F | G |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

## 4.27	CONTROL SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. This section applies for each Service Order when there is activity for this section. ACTION CODE through LHCFIDDATA may repeat as a group. |

119q. ACTION CODE – Action Code – CenturyLink - Specific Field

Identifies the action code associated with the Control FID.

| USAGE: | This field is optional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | O | Not Populated = In |  |

| DATA CHARACTERISTICS: | 1 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  |
| --- | --- |

119r. LHCFID – Left Hand Control Field Identifier – CenturyLink Specific Field

This field contains a Control field identifier. Note: In XML, this FID is identified as LFID.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | SID, LAM, TRID, DLRD, RID, DVA, FCD, PTD, DSG, IMP. | Required when Control exists for the LSR and Control data available. |

| DATA CHARACTERISTICS: | 5 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  |  | S | I | D |
| --- | --- | --- | --- | --- | --- |

119s. LHCFID DATA – Left Hand Control Field Identifier Data– CenturyLink Specific Field

This field provides additional information about the Left Handed Control FID. Note: In XML, this FID is identified as LFID DATA.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | Free form text, Date Format | Required when Control exists for the LSR and Control data available. |

| DATA CHARACTERISTICS: | 999 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| A | B | C | - | 2 |  | D | E | F | G |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

120. REMARKS – Remarks

Identifies a free flowing field, which can be used to expand upon and clarify other data on this form.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC, Error, Reject, Jeopardy | C |  | Remarks are optional except in the following cases: Remarks are prohibited for flow through if Response Type = N. If Response Type = Y, IMA will auto-populate this field with “Please contact the Interconnect Service Center with any questions.” |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| D | I | S | C |  | O | F |  | F | I | R | S | T |  | C | K | T |  | I | N |  | G | R | O | U |
| P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

120a. DISCLAIMER – Disclaimer – CenturyLink-Specific Field

This is for Unbundled products where no facility verification indicator is found.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| FOC | C | “Order is issued pending design and implementation, interval may be re-established in Held/Delayed order process, if facilities/scheduling problems arise.” | For Unbundled products the disclaimer is displayed on FOCs for Unbundled products that do not require facility verification. |

| DATA CHARACTERISTICS: | 255 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| O | R | D | E | R |  | I | S |  | I | S | S | U | E | D |  | P | E | N | D | I | N | G |  | D |
| E | S | I | G | N |  | A | N | D |  | I | M | P | L | E | M | E | N | T | A | T | I | O | N |  |
| I | N | T | E | R | V | A | L |  | M | A | Y |  | B | E |  | R | E | - | E | S | T | A | B | L |
| I | S | H | E | D |  | I | N |  | H | E | L | D | / | D | E | L | A | Y | E | D |  | O | R | D |
| E | R |  | P | R | O | C | E | S | S |  | I | F |  | F | A | C | I | L | I | T | I | E | S | / |
| S | C | H | E | D | U | L | I | N | G |  | P | R | O | B | L | E | M | S |  | A | R | I | S | E |

## 4.28	ASSIGNMENT SECTION

| Rule # | Business Rule |
| --- | --- |
| 1 | Used for RT = A. This section applies for each Service Order when there is activity for this section. ACTION CODE through LHCFIDDATA may repeat as a group. |

### 120b.	ACTION CODE – Action Code – CenturyLink-Specific Field

Identifies the action code associated with the Assignment FID.

| USAGE: | This field is optional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification | O | Not populated = In |  |

| DATA CHARACTERISTICS: | 1 alphanumeric character |
| --- | --- |

EXAMPLE:

120c. LHAFID – Left Hand Assignment Field Identifier – CenturyLink Specific Field

This field contains an Assignment field identifier. Note: In XML, this FID is identified as LFID.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | CA, PR, BP | Required when Assignment exists for the LSR and Assignment data available. |

| DATA CHARACTERISTICS: | 5 alphanumeric characters |
| --- | --- |

| EXAMPLE: |  |  |  | C | A |
| --- | --- | --- | --- | --- | --- |

120d. LHAFID DATA – Left Hand Assignment Field Identifier Data– CenturyLink Specific Field

This field provides additional information about the Left Handed Assignment FID. Note: In XML, this FID is identified as LFID DATA.

| USAGE: | This field is conditional. |
| --- | --- |

| Response Type | R/O/C | Valid Values | Business Rule |
| --- | --- | --- | --- |
| Completion Notification (CN) | C | Free form text, Date Format | Required when Assignment exists for the LSR and Assignment data is available. |

| DATA CHARACTERISTICS: | 999 alphanumeric characters |
| --- | --- |

| EXAMPLE: |
| --- |
| A | B | C | - | 2 |  | D | E | F | G |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

## 5.0	ALPHANUMERIC GLOSSARY

# The following table is an alphanumeric cross-reference glossary of the Local Response form.

| Field Abbreviation | Field # | Field Name |
| --- | --- | --- |
| ACTION CODE | 118f | Action Code (Service and Equipment Section) – CenturyLink-Specific Field |
| ACTION CODE | 119h | Action Code (Listings Section) – CenturyLink-Specific Field |
| ACTION CODE | 119k | Action Code (Billing Section) – CenturyLink-Specific Field |
| ACTION CODE | 119n | Action Code (Traffic Section) – CenturyLink-Specific Field |
| ACTION CODE | 119q | Action Code (Control Section) – CenturyLink-Specific Field |
| ACTION CODE | 120b | Action Code (Assignment Section) – CenturyLink-Specific Field |
| AFVR | 18e | Additional Field Visit Required – CenturyLink-Specific Field (Jeopardy Section) |
| AFVR | 38 | Additional Field Visit Required – Not currently used by CenturyLink (Virtual Related Circuit Detail Section) |
| ALI | 90 | Alphanumeric Listing Identifier Code |
| AN | 17i | Account Number (CenturyLink Order Information Section) |
| AN | 20a | Account Number (Line Information Section) |
| AN | 4 | Account Number (Administrative Section) |
| AN | 21a | Account Number – CenturyLink-Specific Field (Line Information Section) |
| APPTIME | 19a | Appointment Time – CenturyLink-Specific Field |
| ATN | 5 | Account Telephone Number – Not currently used by CenturyLink (Administrative Section) |
| ATN | 86 | Account Telephone Number – Not currently used by CenturyLink |
| BAN1 | 31 | Billing Account Number 1 |
| BAN2 | 33 | Billing Account Number 2 |
| Be | 29l | Excess Burst Size – CenturyLink-Specific Field |
| BI1 | 30 | Billing Account Number Identifier 1 |
| BI2 | 32 | Billing Account Number Identifier 2 |
| BNUM | 118b | Bulk Reference Number – CenturyLink-Specific Field |
| BULK QTY NUM | 118a | Bulk Quantity Number – CenturyLink-Specific Field |
| CABLE ID | 73 | Cable Identification – Not currently used by CenturyLink |
| CBCID | 74 | Cross Box Cable Identification – Not currently used by CenturyLink |
| CC | 1a | Company Code – CenturyLink-Specific Field |
| CCNA | 1 | Customer Carrier Name Abbreviation |
| CD | 17i | Completion Date |
| CFA | 28a | Connecting Facility Assignment – CenturyLink-Specific Field (Line Information Section) |
| CFA | 61 | Connecting Facility Assignment – Not currently used by CenturyLink (Circuit Detail Section) |
| CHAN/PAIR | 75 | Channel/Pair – Not currently used by CenturyLink |
| CHC | 19 | Coordinated Hot Cut |
| CIR | 29k | Committed Information Rate – CenturyLink-Specific Field |
| CKR | 28 | Customer Circuit Reference (Line Information Section) |
| CKR | 60 | Customer Circuit Reference – Not currently used by CenturyLink |
| CLECD/TSENT | 11a | CLEC Date/Time Sent – CenturyLink-Specific field |
| CNO | 8 | Case Number – Not currently used by CenturyLink |
| CTI | 72 | Connection Type Indicator – Not currently used by CenturyLink |
| D/TSENT | 11 | Date and Time Sent |
| DD | 18 | Due Date |
| DEMARC | 77 | Demarc Designation – Not currently used by CenturyLink |
| DGOUT | 29f | DID Digits Out – CenturyLink-Specifc Field (DID Details Section) |
| DGOUT | 119f | DID Digits Out – CenturyLink-Specific Field (DID Telephone Number Section) |
| DIDNUM | 17d | DID Reference Number – CenturyLink-Specific Field |
| DIRIDL | 99 | Directory Identifier – Not currently used by CenturyLink |
| DIRSTAT | 109 | Directory Order Status – Not currently used by CenturyLink |
| DIRSUB | 100 | Directory Subsection – Not currently used by CenturyLink |
| DISC ECCKT | 64 | Disconnect ECCKT – Not currently used by CenturyLink |
| DISC NBR | 27 | Disconnect Telephone Number – Not currently used by CenturyLink |
| DISC ORD | 65 | Disconnect Order Number – Not currently used by CenturyLink |
| DISCLAIMER | 120a | Disclaimer – CenturyLink-Specific Field |
| DLCI | 29j | Data Link Connection Identifier – CenturyLink-Specific Field (Virtual Related Circuit Detail Section) |
| DLCI | 82 | Data Link Connection Identifier – Not currently used by CenturyLink (SECLOC Section) |
| DLLEREFNUM | 110 | DL Listing Confirmation/Error Code Reference Number |
| DLNUM | 89 | Directory Listing Number |
| DLQTYR | 18a | Number of Listings Received –CenturyLink-Specific Field (CenturyLink Order Information Section) |
| DNTR | 99 | DID Telephone Number Range – CenturyLink - Specific Field |
| DOI | 97 | Degree of Indent – Not currently used by CenturyLink |
| DOR | 87 | Date of Receipt – Not currently used by CenturyLink |
| DRTI | 29d | DID Route Index Number – CenturyLink-Specific Field (DID Details Section) |
| DRTI | 119d | DID Route Index Number – CenturyLink-Specific Field (DID Telephone Number Section) |
| DRTN | 21 | Distinctive Ring Telephone Number |
| DSGCON | 39 | Design/Engineering Contact |
| DSN | 54 | Dialable Station Number – Not currently used by CenturyLink |
| DSTN | 29 | Disassociated Telephone Number – Not currently used by CenturyLink (DID Details Section) |
| DSTN | 119 | Disassociated Telephone Number – Not currently used by CenturyLink (DID Disassociated Section) |
| DTGN | 29c | DID Trunk Group Number – CenturyLink-Specific Field (DID Details Section) |
| DTGN | 119c | DID Trunk Group Number – CenturyLink-Specific Field (DID Telephone Number Section) |
| DTK | 29b | DID Trunk Quantity – CenturyLink-Specific Field (DID Telephone Number Section) |
| DTK | 119b | DID Trunk Quantity – CenturyLink-Specific Field (DID Telephone Number Section) |
| DTKID | 29e | DID Trunk ID – CenturyLink-Specific Field (DID Details Section) |
| DTKID | 119c | DID Trunk ID – CenturyLink-Specific Field (DID Telephone Number Section) |
| DTLI | 29a | DID Telephone Line Identifier – CenturyLink-Specific Field (DID Telephone Number Section) |
| DTLI | 119a | DID Telephone Line Identifier – CenturyLink-Specific Field (DID Telephone Number Section) |
| DTNR | 29g | DID Telephone Number Range (DID Details Section) |
| DTNR | 119g | DID Telephone Number Range – CenturyLink-Specific Field (DID Range Section) |
| EBD | 20 | Effective Bill Date – Not currently used by CenturyLink |
| EC VER | 34 | Exchange Carrier Version |
| ECCKT | 27a | Exchange Company Circuit ID – CenturyLink-Specific Field (Line Information Section) |
| ECCKT | 53 | Exchange Company Circuit ID – Not currently used by CenturyLink (Circuit Detail Section) |
| ERROR NUM | 17a | Error Number – CenturyLink-Specific Field |
| ERROR/REJECT CODE | 17b | Error Code – CenturyLink-Specific Field |
| ERROR/REJECT DESCRIPTION | 17c | Error Description – CenturyLink-Specific Field |
| ESDD | 18d | Estimated Due Date – CenturyLink-Specific Field (Jeopardy Section) |
| ESDD | 37 | Estimated Due Date – Not currenlty used by CenturyLink (Virtual Related Circuit Detail Section) |
| FDT | 18f | Frame Due Time |
| FID | 118h | Field Identifier – CenturyLink-Specific Field |
| FOC IND | 17e | Firm Order Confirmation Indicator – CenturyLink-Specific Field |
| HID | 23a | Hunt Group Identifier (Line Information Section) |
| HID | 46 | Hunt Group Identifier – CenturyLink-Specific Field (Hunt Group Section) |
| HID | 118j | Hunt Group Identifier – CenturyLink-Specific Field (Line Information Section) |
| HNUM | 45 | Hunt Line Number – Not currenly used by CenturyLink |
| HTSEQ | 48 | Hunt Sequence – Not currently used by CenturyLink |
| IBT | 14 | ISDN BRI Type – Not currently used by CenturyLink (CLEC Information Section) |
| IBT | 17l | ISDN BRI Type – CenturyLink-Specific Field (CenturyLink Order Information Section) |
| INIT | 9 | Initiator Identification |
| ISPID | 23 | ISDN Service Profile Identification |
| LACT | 93 | Listing Activity Indicator |
| LECODE | 111 | Listing DL Confirmation/Error Code (Listing Error Detail Section) |
| LECODE | 114 | Listing PON Confirmation/Error Code (PON Listings Section) |
| LEGNUM | 52 | Multipoint Leg Number – Not currently used by CenturyLink |
| LHAFID | 120c | Left Hand Assignment Field Identifier – CenturyLink-Specific Field |
| LHAFIDDATA | 120d | Left Hand Assignment Field Identifier Data – CenturyLink-Specific Field |
| LHBFID | 119l | Left Hand Billing Field Identifier – CenturyLink-Specific Field |
| LHBFIDDATA | 119m | Left Hand Billing Field Identifier Data – CenturyLink-Specific Field |
| LHCFID | 119r | Left Hand Control Field Identifier – CenturyLink-Specific Field |
| LHCFIDDATA | 119s | Left Hand Control Field Identifier Data – CenturyLink-Specific Field |
| LHLFID | 119i | Left Hand Listing Field Identifier – CenturyLink - Specific Field |
| LHLFIDDATA | 119j | Left Hand Listing Field Identifier Data – CenturyLink - Specific Field |
| LHTFID | 119o | Left Hand Traffic Field Identifier – CenturyLink-Specific Field |
| LHTFIDDATA | 119p | Left Hand Traffic Field Identifier Data – CenturyLink-Specific Field |
| LISTADR | 104 | Listed Address – Not currently used by CenturyLink |
| LISTNM | 101 | Listed Name – Not currently used by CenturyLink |
| LNEX | 29i | Line Number Extension Number – CenturyLink-Specific Field (Virtual Related Circuit Detail Section) |
| LNEX | 51 | Line Number Extension Number – Not currently used by CenturyLink (Circuit Detail Section) |
| LNEX | 81 | Line Number Extension Number – Not currently used by CenturyLink (SECLOC Section) |
| LNFN | 103 | Listed Name First Name |
| LNLN | 102 | Listed Name Last Name |
| LNUM | 20b | Line Number – CenturyLink-Specific Field (Line Information Section) |
| LNUM | 49 | Line Number – Not currently used by CenturyLink (Circuit Detail Section) |
| LNUM | 80 | Line Number – Not currently used by CenturyLink (SECLOC Section) |
| LOCNUM | 28c | Location Number – CenturyLink-Specific Field (Line Information Section) |
| LOCNUM | 44 | Location Number – Not currently used by CenturyLink (Hunt Group Section) |
| LPHRASE | 107 | Listing Phrase – Not currently used by CenturyLink |
| LRC | 117 | Listing Response Code – Not currently used by CenturyLink |
| LRCD | 118 | Listing Response Code Detail – Not currently used by CenturyLink |
| LRNUM | 116 | Local Response Number – Not currently used by CenturyLink |
| LSR ID | 118c | Local Service Request Identification – CenturyLink-Specific Field |
| LSR NO | 6 | Local Service Request Number |
| LSR_PIA_REMARKS | 17a | LSR Level PIA Remarks Other – CenturyLink-Specific Field |
| LSR_PIA_REMARKS 2 | 17a1 | LSR Level PIA Remarks2 Other 2 – CenturyLink-Specific Field – GUI Only |
| LSR_PIA_REMARKS 3 | 17a2 | LSR Level PIA Remarks 3 Other 3 – CenturyLink-Specific Field – GUI Only |
| LSRREMARKS | 11b | LSR Remarks – CenturyLink-Specific field |
| LST | 29h | Local Service Termination – CenturyLink-Specific Field (Virtual Related Circuit Detail Section) |
| LST | 84 | Local Service Termination – Not currently used by CenturyLink (SECLOC Section) |
| LTC | 55 | Line Treatment Code – Not currently used by CenturyLink |
| LTEXT | 108 | Listing Text – Not currently used by CenturyLink |
| LTN | 91 | Listed Telephone Number |
| LTXNUM | 105 | Line of Text Reference Number – Not currently used by CenturyLink |
| LTXTY | 106 | Listing Text Type – Not currently used by CenturyLink |
| LTY | 94 | Listing Type – Not currently used by CenturyLink |
| MATN | 22 | Main/Alternate Telephone Number – CenturyLink-Specific |
| NID | 79 | Network Interface Device – Not currently used by CenturyLink |
| NOTYP | 56 | Number Type – Not currently used by CenturyLink |
| NPORD | 63 | Number Portability Order Number – Not currently used by CenturyLink |
| NSP DSGCON | 40 | Network Service Provider (NSP) Design/Engineering Contact |
| NSTN | 92 | Non-Standard Telephone Number |
| ONSP | 42 | Old Network Service Provider Identification – Not currently used by CenturyLink |
| OOR | 78 | Out of Range Indicator – Not currently used by CenturyLink |
| ORCD | 115 | Order Response Code Detail – Not currently used by CenturyLink |
| ORD | 7 | Order Number – Not currently used by CenturyLink (Administrative Section) |
| ORD | 17g | Order Number – CenturyLink-Specific Field (CenturyLink Order Information Section) |
| ORD IND | 17j | Order Indicator – CenturyLink-Specific Field |
| ORD PIA REMARKS | 19c | Order Level PIA Remarks Other |
| ORD PIA REMARKS 2 | 19c1 | Order Level PIA Remarks Other 2 – CenturyLink-Specific Field – GUI Only |
| ORD PIA REMARKS 3 | 19c2 | Order Level PIA Remarks Other 3 – CenturyLink-Specific Field – GUI Only |
| ORDL | 62 | Loop Order Number – Not currently used by CenturyLink |
| OREF NUM | 17f | Order Reference Number – CenturyLink-Specific Field |
| PG_of_ | 10 | Page _ of _ |
| PGI | 76 | Pair Gain Indicator – Not currently used by CenturyLink |
| PIA | 17 | Provider Initiated Activity |
| PIA | 19b | Provider Initiated Activity – CenturyLink-Specific Field (Line Information Section) |
| PID | 58 | Personal Identifier – Not currently used by CenturyLink |
| PON | 2 | Purchase Order Number (Administrative Section) |
| PON | 118c | Purchase Order Number - – CenturyLink-Specific Field (Bulk Request to Create LSR Confirmation Section) |
| PONLEQTY | 112 | PON Listing Confirmation Error Code Quantity |
| PONLEREFNUM | 113 | PON Listing Confirmation/Error Code Reference Number |
| PORTED NBR | 25 | Ported Telephone Number |
| RCODE | 18b | Reason Code – CenturyLink-Specific Field (Jeopardy Section) |
| RCODE | 35 | Reason Code – Not currently used by CenturyLink (Virtual Related Circuit Detail Section) |
| RDET | 18c | Reason Jeopardy Code Detail -– CenturyLink-Specific Field (Jeopardy Section) |
| RDET | 36 | Reason Jeopardy Code Detail – Not currently used by CenturyLink (Virtual Related Circuit Detail Section) |
| RDLCI | 29p | Related Data Link Connection Identifier – CenturyLink-Specific Field (Virtual Related Circuit Detail Section) |
| RDLCI | 85 | Related Data Link Connection Identifier – Not currently used by CenturyLink (SECLOC Section) |
| RECCKT | 29n | Related Exchange Company Circuit Identification – CenturyLink-Specific Field (Virtual Related Circuit Detail Section) |
| RECCKT | 83 | Related Exchange Company Circuit Identification – Not currently used by CenturyLink (SECLOC Section) |
| REF NUM | 118i | Reference Number – CenturyLink-Specific Field |
| RELAY RACK | 70 | Relay Rack – Not currently used by CenturyLink |
| REMARKS | 120 | Remarks (Control Section) |
| REMARKS | 88x | Remarks – CenturyLink-Specific field (Listing Error Detail Section) |
| REMARKS | 111a | Remarks – CenturyLink-Specific field (PON Listing Error Section) |
| REP | 12 | Provider Contact Representative |
| RNUM | 50 | RNUM – Reference Number – Not currently used by CenturyLink |
| RORD | 29o | Related Order Number – CenturyLink-Specific Field |
| RPON | 29m | Related Purchase Order Number – CenturyLink-Specific Field |
| RT | 16 | Response Type |
| RTI | 26 | Route Index – Not currently used by CenturyLink |
| SAT | 27b | Subscriber Access Telephone Number – CenturyLink-Specific Field (Line Information Section) |
| SAT | 59 | Subscriber Access Telephone Number – Not currently used by CenturyLink (Circuit Detail Section) |
| SEC CFA | 28b | Secondary Connecting Facility Assignment – CenturyLink-Specific Field |
| SHELF | 67 | Shelf – Not currently used by CenturyLink |
| SLOT | 68 | Slot – Not currently used by CenturyLink |
| SPORT | 69 | Slot Port – Not currently used by CenturyLink |
| ST | 13 | Switch Type – Not currently used by CenturyLink (CLEC Information Section) |
| ST | 17k | Switch Type – CenturyLink-Specific Field (CenturyLink Order Information Section) |
| STYC | 95 | Style Code – Not currently used by CenturyLink |
| SYSTEM ID | 66 | System Identification – Not currently used by CenturyLink |
| TDTR | 43 | Ten Digit Trigger Response – Not currently used by CenturyLink |
| TEL NO | 15 | Telephone Number (CLEC Information Section) |
| TEL NO | 41 | Telephone Number (Virtual Related Circuit Section) |
| TERS | 24 | Terminal Numbers |
| TLI | 23b | Telephone Line Identifier – CenturyLink-Specific Field (Line Information Section) |
| TLI | 47 | Telephone Line Identifier – Not currently used by CenturyLink (Hunt Group Section) |
| TN | 118d | Telephone Number – CenturyLink-Specific Field |
| TNS | 20c | Telephone Numbers – CenturyLink-Specific Field (Line Information Section) |
| TNS | 57 | Telephone Numbers – Not currently used by CenturyLink (Circuit Detail Section) |
| TOA | 96 | Type of Account – Not currently used by CenturyLink |
| UNIT | 71 | Unit – Not currently used by CenturyLink |
| USOC | 118g | Universal Service Order Code – CenturyLink-Specific Field |
| VER | 3 | Version Identification |
| WPP | 98 | White Page Products – Not currently used by CenturyLink |