Maintenance Ticketing Gateway

CenturyLink™

Implementation Guidelines

September 22, 2014

For MTG Software Version 1.7

Versioning

All releases of this document are listed in chronological order.

There is no relationship between the document number and the software release number.

| Document Release | Date | Description |
| --- | --- | --- |
| 1.0 | January 13, 2012 | Initial document for MTG release 1.0 |
| 1.1 | August 6, 2012 | Document update in support of implementation in Minnesota. |
| 1.2 | October 8, 2012 | Added clarification to section 5.3.2 |
| 1.3 Draft | December 21, 2012 | Added Clarification to connectivity in Authentication section (Section 4.2) as per SCR120612-1. |
| 1.3 Final | January 18, 2013 | Added Clarification to connectivity in Authentication section (Section 4.2) as per SCR120612-1. For production date of March 4, 2013 |
| 1.4 Draft | February 26, 2013 | Added Clarification to connectivity in Authentication section (4.2). For production date of April 20, 2013. |
| 1.4 Final | March 15, 2013 | Added Clarification to connectivity in Authentication section (4.2). For production date of April 20, 2013. |
| 1.5 Draft | September 06, 2013 | Document update in support of the added features to Alocation access hours, Managed access hours and Authorization list. For production date of November 10, 2013. |
| 1.5 Final | October 4, 2013 | Document update in support of the added features to Alocation access hours, Managed access hours and Authorization list. For production date of November 10, 2013. |
| 1.6 Draft | August 28, 2014 | Added Request CST (Design service test) section (5.1.10), Appendix T (Client self test response codes) and Appendix U (MTG supported transactions’), in support of the added functionality to perform Client Self Test for circuit IDs before creating Design repair ticket. For production date of November 09th, 2014. |
| 1.7 Draft | September 22, 2014 | Added Request CST (Design service test) section (5.1.10), Appendix T (Client self test response codes) and Appendix U (MTG supported transactions’), in support of the added functionality to perform Client Self Test for circuit IDs before creating Design repair ticket. For production date of November 09th, 2014. |

Copyright and Trademarks

( 2014 CenturyLink, Inc. All Rights Reserved. The CenturyLink mark, pathways logo and certain CenturyLink product names are the property of CenturyLink, Inc. All other marks are the property of their respective owners.

Disclaimer

This document provides an overview of a CenturyLink™ service. It is intended to assist users in determining the type and structure of information requested and returned by the service.

The information contained herein does not constitute an offer by CenturyLink to provide services, equipments, or materials. Any such services and items will only be provided pursuant to an effective agreement between CenturyLink and the Wholesale customer.

Contents

1	Introduction	7

1.1	Purpose of Document	7

1.2	Acronyms	8

2	Implementation Activities	9

2.1	Implementing Access to Maintenance Ticketing Gateway Interface	9

2.1.1	Business to Business Maintenance Ticketing Gateway	9

2.2	Trouble Ticket Capabilities	10

2.3	Initial Communications Activities	10

2.4	Initial Communications Phase Completion	11

2.5	Project Timeline Negotiation	11

2.5.1	Project Timeline Negotiation Activities	12

2.5.2	Project Timeline Negotiation Phase Completion	12

2.5.3	Requirements Review	12

2.5.4	Requirements Review Activities	12

2.5.5	CenturyLink MTG Implementation Documentation Overview	13

2.5.6	Requirements Review Phase Completion	13

2.5.7	Connectivity Testing	14

2.5.8	Progression Testing	14

2.6	Production	14

2.6.1	Production Support Contacts	15

2.6.2	Change Management Process	15

2.6.3	Hours of Availability for Maintenance Ticketing Gateway	16

2.6.4	Service Level Agreements	16

3	Communication Protocol	17

4	Security	18

4.1	CenturyLink/customer Responsibilities	18

4.2	Authentication	18

4.3	Validation of Ownership (Authorization)	18

4.3.1	Create Request	18

4.3.2	All Other Requests (After Successful Create Request)	18

5	Business Functions	19

5.1	Definition of Functions	19

5.1.1	Create Trouble Report (RequestTroubleReportCreationRequest)	19

5.1.2	Retrieve Trouble Report (RetrieveAttributesByTroubleReportIdRequest)	20

5.1.3	Add Trouble Information (AddTroubleInfoRequest)	20

5.1.4	Update Trouble Report (ModifyAttributesRequest)	21

5.1.5	Status/Log Notes Change Event Notification (AttributeValueChangeNotification (AVCN))	22

5.1.6	POTS Closeout Process	22

5.1.7	Design Service Closeout Process	24

5.1.8	Cancel Trouble Report	26

5.1.9	Request MLT Test (POTS Service Test)	27

5.1.10	Request CST (Design Service Test)	28

Numbers of Tests Allowed	28

5.2	Attribute Implementation Definition	29

5.3	Implementation Exclusions	30

5.3.1	Manual Processes	30

5.3.2	Authorization	30

5.3.3	Escalation	30

5.3.4	Scheduled Dispatch	31

5.3.5	Modifications to Trouble Reports	31

5.3.6	Missed Commitments	31

5.4	Critical Attributes for Flow-Through	32

5.5	Error Conditions	36

5.5.1	Customer Process for Error Conditions or No Response	36

6	Production Availability	38

6.1	CenturyLink Maintenance Ticket Gateway (MTG)	38

6.1.1	LMOS	38

6.1.2	WFA/C	38

7	Recovery Procedures	39

7.1	Off-Nominal Status	39

7.1.1	CenturyLink Process	39

7.2	Electronic Recovery and Late Bonding	39

7.2.1	CenturyLink Process	39

7.2.2	Manual to Electronic Recovery – Late Bonding	39

7.2.3	Customer Process – Late Bonding	40

7.3	MTG Single Point of Contact	40

Appendix A: Attribute Definitions	41

A Location Access Address	41

A Location Access Hours	41

A Location Access Person	41

Activity Duration	42

Additional Trouble Information List	42

Additional Trouble Status Information	43

Agent Contact Person	43

Authorization List	43

Called Number	44

Cancel Requested By Manager	44

Close Out Narrative	44

Commitment Time	44

Commitment Time Request	44

Customer Trouble Ticket Number	45

Escalation List	45

Maintenance Service Charge	45

Managed Object Access Hours	45

Managed Object Instance	45

Manager Contact Person	46

Outage Duration	46

Perceived Trouble Severity	46

Preferred Priority	46

Received Time	47

Repeat Report	47

Restored Time	47

Target Object Name	47

Trouble Clearance Person	48

Trouble Found	48

Trouble Report Format Identifier	48

Trouble Report Identifier	48

Trouble Report State	48

Trouble Report Status	49

Trouble Report Status Time	49

Trouble Report Status Window	49

Trouble Type	49

TSP Priority	49

Appendix B - MTG Supported Transactions – Trouble Administration	50

Appendix C - MTG Supported Transactions – POTS Service Test	51

Appendix D - Fallback Error Conditions	52

Appendix E - References to Other Documents	53

References	53

Appendix F – Abbreviations for Problem Descriptions	54

APPENDIX G - TROUBLE STATE Mapping	61

APPENDIX H - TROUBLE STATUS Mapping	62

APPENDIX I – Valid State/Status Combinations for POTS	63

APPENDIX J - Trouble Types	65

APPENDIX K - POTS Disposition Code to Trouble Found	69

APPENDIX L - Disposition Code to Maintenance Service Charge	76

APPENDIX M - Non-Applicable Trouble Types for POTS	77

APPENDIX N – Valid State/Status Combinations for Design Service	80

APPENDIX O - Trouble Found Codes	81

Appendix P - Non-Applicable Trouble Types for Design Service	83

Appendix R - Glossary/Acronyms	85

Appendix S - Managed Object Instance (Service ID component) formats	88

POTS Formats	88

Design Service Formats	88

Unbundled Loop Circuit Formats	88

Unbundled Switch Circuit Formats	88

Guide to Circuit ID Formats	88

Appendix T - Client Self Test (CST) Response codes	91

1.	Full Test Responses	91

2.	Loop Back Responses	91

3.	Supplemental Intrusive Responses	92

4.	Non-Intrusive Responses	92

Appendix U – MTG Supported Transactions – CST	93

# Introduction

## Purpose of Document

This document is intended for Wholesale customers wishing to implement electronic trouble ticketing capabilities with CenturyLink™ for the exchange of Trouble Ticket information for various CenturyLink products and services purchased by the customer.  This document addresses the MTG Implementation Process in terms of both business and technical information.  Following the Introduction, the Implementation Activities section addresses the Wholesale customer requirements and processes for implementing access to MTG.  The remainder of the document contains detailed information about the various transactions and data used within MTG.

A separate document used during the implementation process contains a set of questions for Wholesale customers to answer with the support of their CenturyLink Electronic Implementation Services team, in order to determine the system requirements needed to support trouble ticket transactions via MTG.

CenturyLink’s Maintenance Ticketing Gateway (MTG) provides a mechanism to automate communication and the processing of trouble ticket information. This mechanism is available for use by Wholesale customers of legacy Qwest.

MTG provides an electronic bonding facility that enables CenturyLink Wholesale customers of legacy Qwest to use their own repair/ticketing system to manage troubles on their CenturyLink products and services in legacy Qwest territory. This application is used primarily to mechanically process telephone circuit repair activities including repair ticket generation, MLT (Mechanized Loop Tests) and CST (Client Self Test).

MTG is available for use only in legacy Qwest territories in the following states:

| Arizona Colorado Idaho Iowa Minnesota | Montana Nebraska New Mexico North Dakota Oregon | South Dakota Utah Washington Wyoming |
| --- | --- | --- |

The CenturyLink MTG Ticketing System is based on:

- ATIS Standard “XML Schema Interface for Fault Management (Trouble Administration),” ATIS-0300003.2010, an industry standard for exchange of trouble ticket information

- ATIS- 0300079 –tML Transport Profile: This document recommends a Transport Profile Specification to support the Telecommunications Markup Language (tML) Framework. The intent is to facilitate the interchange of XML formatted business transactions between service requestor and service provider. MTG does not implement every detail of the transport profile, but does use many of the asynchronous concepts described within the guidelines.

- XML POTS Service Test ATIS-0300002.2009, “XML Schema Interface for POTS Service Test.” This standard provides an XML schema information model for POTS Service Test based on ATIS-0300262.2007 and an XML schema interface for POTS Service Test function specified in the same ANSI standard.

This service uses Telecommunication Markup Language (tML).

## Acronyms

BA	Business Analyst

CM	Configuration Management

HTTPS	Hyper Text Transfer Protocol Secure

EISM	Electronic Implementation Services Manager (CenturyLink)

LAN	Local Area Network

MTG	Maintenance Ticketing Gateway

OSS	Operational Support Systems

SM	CenturyLink Service Manager

SOAP	Simple Object Access Protocol

SSL	Secure Sockets Layer

XML 	Extensible Markup Language

# Implementation Activities

## Implementing Access to Maintenance Ticketing Gateway Interface

If you determine that your company can support an XML environment and you would like to conduct business with CenturyLink via the Maintenance Ticketing Gateway (MTG), contact your CenturyLink Service Manager (SM) for a referral to an Electronic Implementation Services Manager (EISM).

### Business to Business Maintenance Ticketing Gateway

The use of MTG via XML provides an effective mechanism to automate the communication and processing of trouble ticket information and to reduce manual processes.  The MTG Implementation Process will progress according to an agreed upon plan and timeline. The typical project phases for Wholesale or Large Business customers implementing a current MTG release will include:

- Initial Communications: During this phase, all activities to initiate a Customer’s implementation are discussed, and the Kickoff conference call is held to introduce specific team members.

- Electronic Implementation Services Manager (EISM): Responsible for facilitating meetings, coordinating the overall Project Timeline, and is the primary point of contact for the Customer during the entire implementation process.

- Business Analyst (BA): Responsible for providing assistance with the business rules that govern the Trouble Ticket process and are enforced by the Gateway

- Implementation Project Timeline and Test Plan Negotiation: During this phase, the Implementation Project Timeline and Test Plan is proposed, negotiated and approved.

- Requirements Review: The Requirements Review phase provides an opportunity for a Customer to review CenturyLink’s MTG Technical Specifications for trouble ticket transactions and ask any questions they may have regarding those requirements.

- Connectivity Testing: During this phase, Customer connectivity is established and tested. This phase includes the set up of the Customer configuration.

- Progression Testing: This phase affords the Customer the opportunity to validate their technical development efforts and to quantify Trouble Ticket processing results. CenturyLink provides an environment for Customers to test the MTG interface for connectivity and transaction processing.

- Testing Certification: The purpose of this test phase is to enable our Customers to conduct a series of required API test case scenarios against Maintenance Ticketing Gateway (MTG) application.  Upon completion, the partner will provide their results in the MTG Testing Certification document to the MTG Project Team for review ensuring that they meet CenturyLink’s expected results prior to deploying to production. Successful completion of these minimum tests, along with review and signoff by the MTG Project Team, is a requirement of all partners prior to CenturyLink granting access to it’s production systems.  Unless directed otherwise, all partner testing will be performed in CenturyLink’s MTG test environment.

- Production:  The Customer moves to production once testing is successfully completed. With new implementations, the EISM will support the customer for one week after production turn-up.

## Trouble Ticket Capabilities

Sending accurate and complete information is critical for the successful processing of Trouble Ticket transactions. CenturyLink strongly recommends that Customers using  MTG review the Technical Specifications Document in conjunction with implementing this service. The MTG Technical Specifications Document may be obtained from the CenturyLink Electronic Implementation Services Manager, or from: http://www.centurylink.com/wholesale/systems/mtg.html.

## Initial Communications Activities

Prior to the Kickoff call between CenturyLink and the Customer, it is recommended that the Customer review and answer the Customer Questionnaire provided as section three of this document. The answers to these questions will provide a basis for ongoing discussions as part of the implementation process.

The following activities will occur as part of the project initiation meeting (Kickoff call) between CenturyLink and the Customer:

- Provide an overview of the Maintenance Ticketing Gateway and the products supported by this interface.

- Discuss hardware/software requirements

- Provide overview of connectivity and transport type used by CenturyLink

- Determine if the customer will require a new Digital Certificate, or will reuse an existing one

- Introduce CenturyLink and Customer team members and identify roles and responsibilities

- Identify the objectives, scope of the products to be implemented and proposed timelines

- Review the Implementation Guidelines and the implementation processes

- Discuss the Testing/Production processes

- Review documentation resources and distribution

- Come to agreement that the Customer will move forward with an implementation.

## Initial Communications Phase Completion

The initial communications phase will be considered complete with an agreement to either move forward with an implementation or to suspend or halt progress due to limitations on the Customer side. This agreement and rationale will be documented in the meeting minutes by the EISM. Additional team meetings will be held as agreed upon.

## Project Timeline Negotiation

An Implementation Project Timeline represents the milestones and responsibilities of all parties throughout the planned MTG implementation process. These milestones will be mutually agreed upon. Regularly scheduled conference calls will be conducted as needed to review progress, answer questions, and identify and communicate resolution of issues.  The assigned project manager will be responsible for maintaining and monitoring progress within the Project Timeline. A mutual negotiation and approval process will be used to manage changes to schedules as recommended or required by either party. All parties will give sufficient advance notice to the other party to allow adequate analysis of the impact of any proposed schedule changes.

The inability of either party to meet any of the milestones contained in the Implementation Project Timeline on the date(s) identified may result in the need to renegotiate a revised Project Timeline/Test Plan.  All revised plans will be developed based on the availability of resources from within the respective organizations and may contain dates that are substantially different from those described in the original plan.

### Project Timeline Negotiation Activities

The following activities will occur during the Project Timeline development and approval process:

- CenturyLink EISM will provide Project Timeline for milestones that are required for a new implementation to MTG for the Customer’s review.

- The Customer will review the proposed Project Timeline and ask any questions about the content.

- The EISM will work with the Customer to incorporate changes to the Project Timeline and reissue, if necessary, for a final review and approval.

- The Customer will review Project Timelineand approve timeline when there is mutual agreement. This will be the final approved Project Timeline for the implementation/migration.

### Project Timeline Negotiation Phase Completion

This phase of the MTG Implementation will be considered complete with the creation of an agreed upon, approved Project Timeline.

### Requirements Review

A critical factor in a successful implementation is a thorough understanding by the Customer of MTG.  The requirements review phase of implementation will provide the Customer with an opportunity to develop a clear understanding of these requirements. This review is critical to the Customer who will:

- Develop and define the business processes and procedures necessary to support the use of their MTG interface for trouble ticket transactions.

- Develop the appropriate documentation (i.e., Methods and Procedures) necessary to support the use of the MTG interface by Customer personnel.

- Perform any necessary database gap analysis for the purpose of ensuring that all data fields that carry the trouble ticket information can be successfully populated.

- Identify appropriate data values.

### Requirements Review Activities

It is the Customer’s responsibility to perform a thorough review of all CenturyLink requirements and specifications.  CenturyLink will provide support to clarify issues and answer questions regarding MTG business rules, requirements, and the Implementation Process.  CenturyLink recommends the following process to ensure that the Customer has a thorough understanding of the answers to each question:

- The Customer reviews CenturyLink specifications as documented in the Technical Specifications Document, located at: http://www.centurylink.com/wholesale/systems/mtg.html

- Questions arising from the Customer’s review of MTG requirements should be logged on the question log and will be reviewed during the Implementation meetings.  The MTG Question Log is located at:  http://www.centurylink.com/wholesale/systems/mtg.html

- CenturyLink will either provide a response to the question or identify those questions requiring further investigation and research. CenturyLink will research these questions and will generally provide an initial response within 5 business days from the submittal.  Responses are typically communicated during the Implementation meetings but may be given via email or phone outside of the meeting.

### CenturyLink MTG Implementation Documentation Overview

The following documents provide additional information on the Implementation Process, or are designed to capture necessary business and configuration parameters. Distribution of these documents will occur as needed during the course of the implementation project.

Distributed prior to the kickoff call:

- Kickoff Agenda

- Contact List Template

- MTG Implementation Questionnaire

Additional information can be found on the Wholesale OSS website (http://www.centurylink.com/wholesale/systems/mtg.html) including:

- Technical Specifications Document

### Requirements Review Phase Completion

The Requirements Review phase of the implementation will be considered complete when the Customer determines that they have adequately reviewed CenturyLink’s specification documentation and have a thorough understanding of it. This understanding will be critical to the effective development of the customer’s interface with CenturyLink.

### Connectivity Testing

Customers must have a digital certificate issued by CenturyLink, and a NetworkID and UserId, for authentication/authorization of inbound customer requests in order to access MTG.  The specifics of connectivity testing will be defined during implementation meetings.

CenturyLink Digital Certificates are issued for each of your systems and are required for each system that will be used to access MTGweb services.  CenturyLink will provide a Digital Certificate ID and PIN and instructions for downloading the certificate from CenturyLink. The certificate must be downloaded within 30 days.  Certificates will expire every 5 years.

Customers will be assigned both a network ID and UserID during the MTG customer implementation process.

For additional information, please call your Implementation manager.

### Progression Testing

Progression Testing Phase:  This phase is accomplished using the MTG Testing environment.  Progression testing provides the Customer with the opportunity to validate technical development efforts and to quantify processing results during the MTG implementation process. Testing also verifies the Customer’s ability to send correct XML transactions through MTG.

The Testing environment relies on several back end systems.  Testing must be closely coordinated to ensure effective testing during your scheduled window.

## Production

Once testing has been completed according to the test plan, the Customer will be readied for production. There are some configuration settings that must be completed in the production environment before the customer can begin sending transactions in production.

Customer will be in Controlled Production for 2 days to closely monitor progress and ensure everything is working properly.  This will be defined and coordinated prior to your production date.  A call will be scheduled to monitor and track results for a set of predefined transactions to determine readiness to enter full Production.

As testing begins to wind down, the Customer and CenturyLink will reaffirm the production date from the Project Timeline and the EISM will direct any environment configuration that is necessary. On the agreed upon date for production, the Customer may begin sending in transactions to CenturyLink.

### Production Support Contacts

MTG support to Customers who have recently been placed into production will be provided as follows:

| Timeframe | Technical Support | Contact Information |
| --- | --- | --- |
| First Week after Implementation | Electronic Implementation Services Manager (EISM) | Provided by EISM |
| After First Week | Application AIP Support Team | CenturyLink Help Desk (Add TN information) |

### Change Management Process

CenturyLink facilitates a regularly-scheduled forum in which CenturyLink and the CLECs communicate about Operational Support System (OSS) interface changes, release lifecycles, release notifications, and communication intervals.  The CenturyLink CLEC Industry change management forum is referred to as the Change Management Process (CMP).

CenturyLink encourages CLECs implementing the MTG interface to participate in the CMP process.  Online registration can be found on the CMP website page. Release notifications, team meeting information, and change requests are also provided to all registered team members via e-mail.  For further CMP information, please refer to the following website:

http://www.CenturyLink.com/wholesale/cmp/index.html

During testing with CLECs, situations may occur that require CenturyLink to submit a Change Request internal to CenturyLink to fix an issue in CenturyLink's Test systems. When an issue is discovered that substantially impacts a CLEC's ability to use a transaction in MTG, notification will be distributed via e-mail within three (3) business-days.  Notification of any production issues will follow the CMP guidelines section 12.0.  Please refer to the following URL for more information:  http://www.CenturyLink.com/wholesale/cmp/whatiscmp.html

CenturyLink will notify all CLECs that have subscribed to the unplanned event notifications and Test environment notifications. It is the CLEC responsibility to subscribe to those notifications they wish to receive. The notification will include a description of the problem and, if known, a potential fix date.  If a fix date is not known, CenturyLink will update all impacted CLECs with the fix date when known. CLECs intending to implement new transactions will be informed of any known issues for that transaction during the Kickoff call.

### Hours of Availability for Maintenance Ticketing Gateway

http://www.centurylink.com/wholesale/cmp/ossHours.html

### Service Level Agreements

Wholesale customers may have specific contractual date and time frames for service delivery stated in their Service Level Agreement with CenturyLink. Those Agreements are negotiated separately from the services supported by MTG.

# Communication Protocol

The following diagram is an overview of the access topology into the CenturyLink XML Interface for electronic bonding trouble administration.

Figure 1 Connections Between customer and CenturyLink

Logical connectivity is offered as illustrated in Figure 1, “Connections between customer and CenturyLink.”

# Security

## CenturyLink/customer Responsibilities

Each company is responsible for ensuring that only authorized users have access to the host systems and gateways to the other company.

## Authentication

CenturyLink customers must have a Digital Certificate to make use of CenturyLink XML API.

MTG uses two-way Secure Socket Layer/Transport Layer Security (SSL/TLS) communication. The SOAP header is not used for transport security.

Please follow the X.509v3 standard.

For inbound transactions, the customer must send the CenturyLink-provided digital certificate.

For outbound transactions, CenturyLink will send the customer-provided digital certificate for client authentication.

CenturyLink has an additional option available to include partner provided username, password in plain text format under WSSE security header/ Usernametoken section inside SOAP header in the CenturyLink outbound request. With this option, the customer-provided digital certificate for client authentication is not required.

MTG’s current implementation (both as client and server) is compliant with RFC 5746 and allows secure renegotiations. However, on outbound communication from MTG to Partner, if the partner server doesn't support secure renegotiations, MTG client has an option to turn off session reuse upon partner’s request.

## Validation of Ownership (Authorization)

### Create Request

The CenturyLink MTG gateway validates that a serviceId (circuit/TN) entered belongs to the Manager (i.e., customer) via MCN or ACNA/RSID comparison.

### All Other Requests (After Successful Create Request)

The CenturyLink MTG gateway validates that a trouble report entered belongs to the Manager (i.e., customer).

# Business Functions

This section defines agreements, clarifications, or exceptions for business functions, attributes, and processes.

## Definition of Functions

This section defines the business transactions which are agreed will be supported via Electronic Bonding. For each of these transactions, CenturyLink will evaluate the request and determine if an error condition exists. If errors exist, CenturyLink will respond with the appropriate tML defined error message. If no error conditions exist, the response echoes back the header and TargetObjectName information, and returns other attributes applicable to the specific transaction.

See ‘MTG Supported Transactions – Trouble Administration’, and, ‘MTG Supported Transactions – POTS Service Test’ and ‘MTG Supported Transactions – Client Self Test’ at http://www.centurylink.com/wholesale/systems/mtg.html for more detail

### Create Trouble Report (RequestTroubleReportCreationRequest)

The request to create a trouble report originates from the customer. The customer issues a Create Trouble Report transaction to create the trouble report in the CenturyLink’s OSS. The customer is required to supply mandatory attributes in accordance with TRFD rules and defined XSD rules. CenturyLink is required to validate circuit ownership before transmitting the create response. The trouble report will then be routed to the appropriate group for resolution.

Auto-Test Rules:

POTS:

Auto-test is not applicable. Downstream systems determine if an MLT will be run.

Design:

It is advisable to perform CST (Client Self Test) before creating a ticket. AutoTest is determined by circuit type. If the circuit is not a candidate for AutoTest, this function will not be performed.

### Retrieve Trouble Report (RetrieveAttributesByTroubleReportIdRequest)

This transaction is used by the customer to obtain status and other information from CenturyLink about a previously entered trouble report. The customer issues a Retrieve Trouble Report transaction and CenturyLink will respond by returning the current values of all supported attributes.

### Add Trouble Information (AddTroubleInfoRequest)

A request to add trouble information to an existing trouble report originates from the customer. The customer issues an Add Trouble Information transaction. When CenturyLink receives the request, it updates the trouble information on the trouble report.  The customer also has the option to issue a Modify Attributes Request in order to add trouble information to an existing trouble report.

### Update Trouble Report (ModifyAttributesRequest)

A request to modify information on an existing trouble report originates from the customer. The customer issues an Update Trouble Report transaction only for modifiable attributes. When CenturyLink receives the request, it updates the information on the trouble report.

NOTE: A modification of the CommitmentTimeRequest attribute will not result in a change to the original Commitment Time established during the Trouble Report creation.

### Status/Log Notes Change Event Notification (AttributeValueChangeNotification (AVCN))

A status change notification (Event Notification) originates from CenturyLink. CenturyLink issues an Event Notification when the status of a trouble report changes to notify the customer of the status change. CenturyLink can also issue an Event Notification to send Log Notes (remarks) to the customer.

### POTS Closeout Process

POTS (LMOS) trouble report closure is a two step process (Cleared and Closed). Cleared information is contained in the first event notification, and detailed trouble report closure information is contained in the second event notification.

POTS Cleared Event Notification

CenturyLink first sends a notification (AVCN) containing Cleared state (3), or Cleared Customer Advised (CCA) status (25), the time the trouble ticket was restored (Trouble Report Status Time), and a message (Additional Trouble Status Info). The TR-Change-Denied rules will be applied after the Cleared event notification occurs (CCA) i.e., allowable actions on a cleared trouble report are limited.

POTS Closed Event Notification

CenturyLink sends the second notification (AVCN) to the customer when the trouble report is closed, and a response is not needed, expected, or waited for to continue processing. The closed notification contains: Closed state (4), status (27), status time, trouble found, maintenance service charge, outage duration, restored time and Close Out Narrative (explaining what CenturyLink found the trouble to be and what caused the trouble). CenturyLink sends the closed transaction as soon as the information is posted in its OSS, so there may be a time interval between the Cleared and Closed events.

Note: There may be a time interval between the Cleared event and the Closed event. If the customer requests status during this interval, the Cleared status information is returned. If the customer attempts to request to change the trouble report (e.g., Cancel) during this interval, the TR-Change-Denied rules will be applied.

Details of the closed notification attributes are:

| Attribute | Value | Description |
| --- | --- | --- |
| CloseOutNarr | Text | Contains the resolution and cause of the trouble resolved |
| MaintServiceCharge | Y/N | Y = based on disposition codes 1230, 1240, 1250, 1260 (See Appendix L for details) |
| OutageDuration | day, hour, min, sec, msec | restoredTime less receivedTime |
| RestoredTime | GMT | Cleared time |
| TroubleFound | Enumerated code value | An enumerated code value that identifies the problem resolved (See Appendix O for details.) |
| TroubleReportState | 4 | Closed |
| TroubleReportStatus | 27 | Closed Out |
| TroubleReportStatusTime | GMT | Closed Time |
| AdditionalTroubleStatusInfo | Text | Closed Message text |

### Design Service Closeout Process

Design Service (WFA) trouble report closure is a three step process. The first step is a CenturyLink-sent Cleared Awaiting Customer Verification Event notification (AVCN), which includes detailed trouble report closure information. The second step is the customer’s reply to CenturyLink’s request to close the Trouble report. (This reply is sent by the customer as a VerifyRepairCompletionRequest). Assuming the customer did not dispute or deny the request to close the trouble report, the third step is a CenturyLink-sent Closed Event Notification (AVCN).

#### Design Service Cleared/Cleared Awaiting Customer Verification Event

A Cleared Event Notification for a Design Service is an OSS request to close a Trouble Ticket. The same Attributes are returned as in the POTS ClosedOut Event, but the State and Status are returned with Cleared and ClearedAwaitingCustVerification values (3/26). Additionally, the Activity Duration attribute will be present, which contains all of the NoAccess periods (total) and the data structures for Dispatch and DelayedMaintenance. The Close Out Narrative is a text message from the CenturyLink repair technician. The Maintenance Service Charge indicates whether maintenance service charges will apply to the trouble report. The Outage Duration attribute indicates the amount of time between the Trouble Report clearing time and the Trouble Report received time, excluding any times for delayed maintenance or any times the service could not be accessed by the service provider for repair. The TroubleFound code identifies the resolved problem.

Details of the cleared transaction attributes (containing detailed closure information) are:

| Attribute | Value | Description |
| --- | --- | --- |
| Activity Duration | Activity Type, Duration (day, hour, min, sec, msec), Billable flag | May contain duration (day, hour, min, sec, msec) for activities NoAccess, Dispatch, and DelayedMaintenance, and whether billable. |
| CloseOutNarr | Text | Technician-entered close out summary. |
| MaintServiceCharge | Y/N | Indicates whether maintenance service charges will apply to the trouble report. |
| OutageDuration | day, hour, min, sec, msec | RestoredTime – ReceivedTime - NoAccessDuration – DelayedMaintDuration |
| RestoredTime | GMT | Technician-entered cleared time (Technician may back date). |
| TroubleFound | Enumerated code value | An enumerated code value that identifies the resolved problem (See Appendix O for details). |
| TroubleReportState | 3 | Cleared |
| TroubleReportStatus | 26 | ClearedAwaitingCustVerification |
| TroubleReportStatusTime | GMT | Cleared Time |
| AdditionalTroubleStatusInfo | Text | Cleared Message text |

Customer Reply (VerifyRepairCompletionRequest) to the Design Service Cleared Event Notification

The Cleared Event Notification from CenturyLink requires a customer reply. Once the Cleared Event Notification is sent to the customer, a 24 hour timer is started. If no response is received for the Cleared Event Notification, then the Trouble Ticket will be closed automatically. A customer-sent VerifyRepairCompletionRequest will verify or dispute the information (Activity Duration or Closeout Narrative) sent on the Cleared Event Notification, or deny that the trouble has been fixed:

A Verify reply will trigger the CenturyLink process to close the Trouble Ticket.

A Dispute reply triggers a Request for Manual Assistance in the CenturyLink Work Center, in order to resolve the dispute.

A Deny reply will expire the 24 hour timer and put the Trouble Ticket back into open/active status.

Design Service Closed Event Notification

A Closed Event Notification (AVCN) will be sent when the Trouble Ticket is Closed in the CenturyLink OSS. This Notification includes: TroubleReportState (4), TroubleReportStatus (27), TroubleReportStatusTime (Closed Time GMT), AdditionalTroubleStatusInfo (Closed message).

### Cancel Trouble Report

A request to cancel a trouble report originates from the customer. The customer issues a CancelTroubleReportRequest. When the cancel request is received, CenturyLink will screen the trouble report to determine the status of the trouble report. CenturyLink will either send the trouble report to a closeout process if no work is in progress, or will complete the work in progress on the trouble report, until it can be closed appropriately. In the latter case, billing charges may apply.

### Request MLT Test (POTS Service Test)

The CenturyLink gateway supports ATIS standard ATIS-0300002.2009 that allows Trading Partner to request an MLT test to be run on a 10 digit POTS telephone number.

A request for an MLT test originates from the customer. The customer issues a POTSUncontrolledTestRequest. CenturyLink is required to validate circuit ownership before transmitting the test request. CenturyLink has implemented the following types of POTS tests:

full (1),

quick (2),

centralOffice (3),

loop (4),

startTone (5)

NOTE: If the customer initiates a startTone (5), CenturyLink will automatically remove the tone from the line after 2 minutes.

See ‘MTG Supported Transactions – POTS Service Test’ at http://www.centurylink.com/wholesale/systems/mtg.html for details.

### Request CST (Design Service Test)

The CenturyLink gateway that allows Trading Partner to request a Client Self Test (CST) to be run on a Design Circuit ID.

A request for a CST test originates from the customer. The customer issues a ClientSelfTestRequest. CenturyLink is required to validate circuit ownership before transmitting the test request. CenturyLink has implemented the following types of Circuit tests: Refer to Appendix T -

Full Test (1)

Loop Back (2)

Supplemental Intrusive Test (3)

Non-Intrusive Test (4)

NOTE: If the customer initiates a Full Test (1), Loop Back (2) and Supplemental Intrusive Test (3), Centurylink will take the circuit out of service for the duration of the test. A warning message will be sent as part of the acknowledgment.

If the customer initiates Non-Intrusive Test (4), CenturyLink will verify the circuit is up and error free. This test will not include intrusive testing.

### Numbers of Tests Allowed

There are limits on the number of tests that can be run, within a given time, for each CEMR-MTG customer with valid CEMR-MTG credentials able to log into the Client Self Test tool.

- On a monthly basis, the customer will be limited to 4,000 tests.

- On a daily basis, there will be a limit of 200 test requests per customer.

- Each customer will be limited to kick off up to 25 test requests within a 10 minute time frame.

- A customer will not be allowed the ability to test a given circuit when any repair ticket currently exists for that circuit.

- If a customer reaches any of the limits, a pop-up message will be displayed notifying them that they reached their limits.

- A failed test request is still considered an attempt and will be counted as a test run.

See ‘MTG Supported Transactions – Client Self Test’ at http://www.centurylink.com/wholesale/systems/mtg.html for details.

## Attribute Implementation Definition

The definitions of attributes implemented in MTG, and the method for handling the attributes by CenturyLink are identified in Appendix A, ‘Attribute Definitions’.

See ‘MTG Supported Transactions – Trouble Administration’, and, ‘MTG Supported Transactions – POTS Service Test’ and ‘MTG Supported Transactions – Client Self Test’ at 
http://www.centurylink.com/wholesale/systems/mtg.html for more detail.

Although all the Attributes listed in Appendix A have been implemented, in some instances there is limited behavior or no behavior in the CenturyLink OSS due to OSS limitations.

## Implementation Exclusions

This section defines process exclusions that will not be supported via Electronic Bonding in CenturyLink’s OSS. Exclusions are due to the fact that attributes relating to these processes drive limited or no behavior in the current CenturyLink OSS.

### Manual Processes

The processes listed below are manual processes because the attributes relating to these processes are not fully supported in CenturyLink’s OSS via Electronic Bonding:

### Authorization

POTS trouble reporting does not support authorization requests electronically. The attribute AuthorizationList will be accepted on an electronic ticket creation request, and any values sent by the customer will be returned upon receipt of a ticket retrieval request from the customer. However, AuthorizationList will not be used within CenturyLink’s OSS, with the assumption that authorization to dispatch is granted. Access hour restrictions will require manual processing. See Section 5.3.4 “Scheduled Dispatch” (below) for further details.

For Design Service trouble reporting, AuthorizationList will be accepted on an electronic ticket creation request, and any values sent by the customer will be returned upon receipt of a ticket retrieval request from the customer. Additionally, AuthorizationList will be used within CenturyLink’s OSS and business processes. CenturyLink allows customers to provide or deny authorizations using the AuthorizationList attribute or as AdditionalTroubleInfo.  If additional authorizations are needed, CenturyLink will request those using AdditionalTroubleStatusInfo (rather than AuthorizationList attribute) in the AttributeValueChangeNotification.  Customers can then provide or deny those authorizations by modifying the AuthorizationList attribute or AdditionalTroubleInfo.

### Escalation

POTS trouble reporting does not support escalation requests electronically. The attribute EscalationList will be accepted on an electronic ticket creation request, and any values sent by the customer will be returned upon receipt of a ticket retrieval request from the customer. However, EscalationList will not be used within CenturyLink’s OSS, with the assumption that escalation requests must be made manually and are handled manually through the life of the trouble report.

For Design Service trouble reporting, EscalationList will be accepted on an electronic ticket creation request, and any values sent by the customer will be returned upon receipt of a ticket retrieval request from the customer. Additionally, EscalationList will be used within CenturyLink’s OSS and business processes. CenturyLink supports customer escalation requests as EscalationList attribute or as AdditionalTroubleInfo. CenturyLink will provide a reply to escalation request in the form of AdditionalTroubleStatusInfo rather than providing EscalationList attribute in the AttributeValueChangeNotification.

### Scheduled Dispatch

For POTS trouble reports, dispatches requiring coordination between the customer and CenturyLink will be handled manually, in accordance with CenturyLink business processes.

For Design Service trouble reports, dispatches requiring coordination between the customer and CenturyLink may be handled electronically. CenturyLink supports customer authorization requests as AuthorizationList attribute or as AdditionalTroubleInfo, although CenturyLink prefers use of the AdditionalTroubleInfo since more information can be exchanged using this method.  CenturyLink will provide a reply to authorization request in the form of AdditionalTroubleStatusInfo rather than providing AuthorizationList attribute in the AttributeValueChangeNotification.

### Modifications to Trouble Reports

For POTS trouble reports, modifications to attributes other than PerceivedTroubleSeverity and AdditionalTroubleInfoList will be accepted on an electronic trouble report update request, and any values sent by the customer will be returned upon receipt of a trouble report retrieval request from the customer. Modifications to attributes other than PerceivedTroubleSeverity and AdditionalTroubleInfoList will not be used within CenturyLink OSS.

For Design Service trouble reporting, modifications to attributes including PerceivedTroubleSeverity and AdditionalTroubleInfoList will be accepted on an electronic ticket update request, and any values sent by the customer will be returned upon receipt of a ticket retrieval request from the customer. Additionally, attributes including PerceivedTroubleSeverity and AdditionalTroubleInfoList may be used within CenturyLink’s OSS and business processes.

See ‘MTG Supported Transactions – Trouble Administration’, and ‘MTG Supported Transactions – Client Self Test’at http://www.centurylink.com/wholesale/systems/mtg.html for more detail.

### Missed Commitments

For POTS trouble reports, if a commitment is missed, the OSS needs a new commitment to create a subsequent report. As a result, trouble report update transaction will not be accepted in this case. CenturyLink handles this manually and negotiates a new commitment with the customer. If a commitment is missed and the customer has requested a trouble report update (e.g. modify, cancel) an error will be returned.

For Design Service trouble reports, no special rules exist.

## Critical Attributes for Flow-Through

The following table lists the critical Attributes for the business processes. It will be used to determine if the trouble report received achieves current flow-through:

Note: Please see MTG Interface Specification (Section 4.1) for specific rules regarding TRFD-based optionality for elements included used in creation of trouble reports.

Also see ‘MTG Supported Transactions – Trouble Administration’, and, ‘MTG Supported Transactions – POTS Service Test’, and, ‘MTG Supported Transactions – Client Self Test’, at http://www.centurylink.com/wholesale/systems/mtg.html for more detail.

| Attribute | Why Critical | Valid Data |
| --- | --- | --- |
| Account Name | POTS and Design Services: The Account Name is assigned by CenturyLink during onboarding. CenturyLink requires that this value be sent by the customer for authorization. | The exact value assigned by CenturyLink during onboarding. |
| Additional Trouble Info List | POTS and Design Services: CenturyLink requests a description of the problem and any additional information further defining the trouble to aid trouble resolution (current process). CenturyLink needs information explaining environmental or physical conditions, or special circumstances that may affect resolution of the trouble. POTS: In the case of a life threatening situation in Idaho, customer must send information describing the situation. In the case of a hunt group trouble, customer must describe the problem. Design Service: CenturyLink requests a description of the problem and any additional information further defining the trouble to aid trouble resolution (current process). CenturyLink needs information explaining environmental or physical conditions, or special circumstances that may affect resolution of the trouble. | Valid text giving a good description of the problem (in addition to the trouble type) and any important additional information that customer has gathered during their trouble isolation with the end-user of the service. For example, dangerous animal in yard, see neighbor next door, or hearing impaired customer. POTS: For a life threatening situation in Idaho, describe the situation, for example, line down in street, open pit in yard, or medical emergency. For series or multi-line hunting, add text describing the type of trouble and any important additional information. Due to CenturyLink OSS limitations, only the first 47 characters are guaranteed to be displayed in CenturyLink’s OSS (LMOS) for use by CenturyLink repair personnel. However, the customer may send in more characters without error. Design Service: Multiple occurrences of AdditionalTroubleInfoItem are allowed. AdditionalTroubleInfoItem limited to 400 characters. |
| A Location Access Address | POTS and Design Services: CenturyLink verifies the premises address to ensure correct dispatches. If customer does not send correct address information, incorrect dispatches and charges may result. | POTS and Design Services: Valid end-user premises street address. |
| A Location Access Hours | POTS: The Sunday element of the ALocationAccessHours weekmask can be used to specify a four hour appointment for a trouble report requiring dispatch. All other day settings will be ignored. Design Service: CenturyLink needs to know the hours that repair technicians can access the premise. Note: For UBL 2-Wire analog circuits, the Sunday element of the ALocationAccessHours weekmask can be used to specify a four hour appointment for a trouble report requiring dispatch. | POTS: Standard week mask syntax. Design Service: Send a single or multiple LocationAccessHoursItem for the days that have access hours. The DaysOfWeek section within the LocationAccessHoursItem should contain one or more days as “true” for which customer is providing access hours and “false” for the remaining days. MTG will use one interval per day. Only the current, previous, and next day will be stored in CenturyLink’s OSS (WFA), relative to the day the trouble report was created. NOTE: See MTG Interface Specification (Section 5.1) for XML example. |
| A Location Access Person | POTS: Currently, CenturyLink is not able to process this information in LMOS because the customer Contact Person is used instead. However, CenturyLink expects customer to send valid data. Design Service: CenturyLink repair personnel may use this information to contact the party associated with the premise. | POTS: Valid individual or center name and valid phone number. Only the first 10 characters of the phone number are used (no delimiters). Design Service: Valid individual or center name and valid phone number Only the first 10 characters of the phone number are used (no delimiters). |
| Managed Object Instance (Service Id component) | POTS: CenturyLink expects the line in trouble to be identified correctly to aid trouble resolution. Design Service: CenturyLink expects the circuit in trouble to be identified correctly to aid trouble resolution. | POTS: TN, for example, 3031234567 or TN plus TER, for example 3031234567TER12345 Design Service: See Appendix S, Managed Object Instance Formats for valid unbundled loop and unbundled switch circuit formats. |
| Manager Contact Person | POTS and Design Service: CenturyLink needs contact name and phone number to prevent further service delays when a telephone call must be made to customer. If customer does not send valid data, CenturyLink cannot respond appropriately and it may impact outage duration. | POTS and Design Service: Valid individual or center name and valid phone number. Only the first 10 characters of the phone number are used (no delimiters). |
| Network Id | CenturyLink assigns a Network Id during onboarding and requires that the assigned value be sent by the customer for authorization. | The exact value assigned by CenturyLink during onboarding. |
| Perceived Trouble Severity | POTS and Design Service: CenturyLink requests information about the trouble severity to understand the perceived impact of the trouble on the affected TN/Circuit. | POTS and Design Service: ATIS-defined values |
| Preferred Priority | POTS: CenturyLink receives “life threatening” value for Idaho lines and denotes this in the LMOS Narrative to identify to the flow-through process that immediate attention should be given to this trouble ticket. If customer does not send this value, CenturyLink cannot respond appropriately. In general , this attribute defines the urgency with which the manager/requestor requires resolution of the problem Design Service: In general , this attribute defines the urgency with which the manager/requestor requires resolution of the problem | POTS: ATIS-defined values Design Service: ATIS-defined values |
| Repeat Report | POTS: Indicates if there has been an activity on the Managed Object (TN) within the last 30 days. This information is used within CenturyLink’s trouble resolution processes. Design Service: N/A | POTS: ATIS-defined values Design Service: N/A |
| Trouble Clearance Person | POTS and Design Service: CenturyLink needs clearance name and phone number to identify who within customer’s organization has requested cancellation or is replying to CenturyLink’s request to close a trouble ticket. | POTS and Design Service: Valid individual or center name and valid phone number. Only the first 10 characters of the phone number are used (no delimiters). |
| Trouble Type | POTS and Design Service: CenturyLink uses this information is used within its trouble resolution processes. If customer sends a trouble Type that is inappropriate for the type of service, the create transaction will fail. This edit is based on the Customer Type. | POTS and Design Service: Standard values per the non-applicable (invalid) trouble type lists. See Appendix J, M, and P for details. POTS: For series or multi-line hunting when exact TN or TER in trouble is known, use the specific trouble type for the situation, if it can be identified. If the type of trouble cannot be identified, use 1118 for Hunting Not Working. For series or multi-line hunting when exact TN or TER in trouble is not known, always use 1118 for Hunting Not Working. |

## Error Conditions

### Customer Process for Error Conditions or No Response

If an activity returns an error response or no response, the customer may attempt to re-send the transaction. If the subsequent transaction also returns an error response, the customer may handle the activity manually. If an error response indicates a correctable activity, the customer will provide the correction and re-send. If a correction to the error is uncertain, the customer may contact the CenturyLink EB Single Point of Contact/Service Center for clarification of the error response.

See ‘MTG Supported Transactions – Trouble Administration’, and, ‘MTG Supported Transactions – POTS Service Test’, and ‘MTG Supported Transactions – Client Self Test’, at 
http://www.centurylink.com/wholesale/systems/mtg.html for details of possible error conditions.

# Production Availability

## CenturyLink Maintenance Ticket Gateway (MTG)

MTG hours of operation is listed on the Wholesale Systems Web site under Change Management Process (CMP) OSS Hours of Availability: http://www.centurylink.com/wholesale/cmp/ossHours.html

The following are the CenturyLink host ticketing system Hours of Operation. These are the hours that CenturyLink’s internal OSSs for trouble administration are available.

Note: If requests are received for a CenturyLink OSS during the scheduled downtime then an error response will be sent to the customer. You should wait until the downtime has expired before sending another transaction.

### LMOS

Central Region - AZ, CO, ID, MT, NM, UT, WY (Mountain Time)

00:15 to 01:15 (daily maintenance window)

Eastern Region - IA, NE, MN, ND, SD (Mountain Time)

23:15 to 00:15 (daily maintenance window)

Western Region - OR, WA (Mountain Time)

01:15 to 02:15 (daily maintenance window)

### WFA/C

Central Region - AZ, CO, ID, MT, NM, UT, WY  (Mountain Time)

22:00 Saturday through 06:00 Sunday

Eastern Region - IA, NE, MN, ND, SD (Central Time)

22:00 Saturday through 06:00 Sunday

Western Region - OR, WA (Pacific Time)

Maintenance Window: 2nd and 4th weekends 2200 to 0600

1st, 3rd and 5th weekends 2200 to 2300 Saturday

# Recovery Procedures

## Off-Nominal Status

### CenturyLink Process

Off-Nominal Status is an error state in which the software/hardware is capable of recovery on its own. Transaction errors may occur, but no intervention is required. The CenturyLink EB Single Point of Contact/Service Center will not contact the customer.

## Electronic Recovery and Late Bonding

### CenturyLink Process

It is to the advantage of both the customers and CenturyLink to maintain the electronic data flow for the life of an EB ticket. Minor errors (Off-Nominal Status) should be overcome, and data flow should continue as before without the need for any manual intervention or manual communication between the customers and CenturyLink. Each EB ticket shall remain electronically bonded.

A system failure could result in the permanent loss of data flow on existing EB tickets. Once the system is restored, communication between customers and CenturyLink may be needed to assess the need for manual intervention to fully recover to a Nominal Status.

### Manual to Electronic Recovery – Late Bonding

POTS: If a trouble report is created manually, it remains manual for the life of the trouble report.

Design Service: If trouble is detected on CenturyLink equipment, or if a customer calls in a trouble report (usually due to a Gateway disruption), a Work Center Technician may manually enter a trouble ticket into the appropriate OSS region.

If a customer submits a request to open a trouble ticket on CenturyLink equipment that has had a trouble ticket opened manually, the CenturyLink Gateway (MTG) will return an error stating that a trouble ticket already exists for that equipment (e.g. Circuit, TN).

The response returned on the Create request is a ‘TroubleReportAlreadyExists’ error, including the Trouble Report ID. (See ‘MTG Supported Transactions – Trouble Administration’ at http://www.centurylink.com/wholesale/systems/mtg.html for details).

### Customer Process – Late Bonding

Customer may send a Retrieve Trouble Report transaction on any manually created trouble reports that the customer wishes to electronically bond. CenturyLink will return the trouble ticket information, including a comment stating “THIS TROUBLE REPORT HAS BEEN CONVERTED TO AN ELECTRONIC TICKET!” The trouble ticket is now electronically bonded and it is expected that the normal Work Center EB processes will be followed from that point on (authorization/closeout requests and responses, text messages, Status Changes, Retrieve, Modify, etc.).

For manually created tickets that have been closed, no Late Bond ability exists. Close out details must be pursued manually.

## MTG Single Point of Contact

In order to manage technical contact between CenturyLink and the customer, a  single point of contact is needed.

CLEC/IXC customers should call the Wholesale Systems Help Desk (WSHD) 888-796-9102. The WSHD will assign out a ticket and assign it to the appropriate SME team.

Appendix A: Attribute Definitions

This section includes the Definition for POTS and Design Services for each attribute.

See documents at http://www.centurylink.com/wholesale/systems/mtg.html for details regarding whether the attribute is optional or mandatory.

A Location Access Address

Definition for POTS and Design Service: End-user premises street address. This is the address for which the A Location Access Hours attribute values apply.

A Location Access Hours

Definition for POTS: The A Location Access Hours attribute defines the specific hours for each day of the week during which access to the A location is available.

Within the ALocationAccessHours element, customer shall send one or more LocationAccessHoursItem for the days for which they are providing access hours. The DaysOfWeek section within the LocationAccessHoursItem should contain one or more days as “true” for which customer is providing access hours and “false” for the remaining days. MTG will use one interval per day.

Arranging premises access due to access restrictions is a manual process.

Definition for Design Service: CenturyLink OSS limitation of three days, one access interval per day. Time is specified in the customer’s (end user’s) local time based on the customer’s address.

Within the ALocationAccessHours element, customer shall send one or more LocationAccessHoursItem for the days for which they are providing access hours. The DaysOfWeek section within the LocationAccessHoursItem should contain one or more days as “true” for which customer is providing access hours and “false” for the remaining days. MTG will use one interval per day. Only the current, previous, and next day will be stored in CenturyLink’s OSS (WFA), relative to the day the trouble report was created.

A Location Access Person

Definition for POTS: The A Location Access Person attribute enables the manager to specify the details of the person at the A location. Not supported in CenturyLink OSS due to business process agreements and OSS limitations. The customer’s contact information will be used in the CenturyLink OSS as primary customer contact per agreement.

Definition for Design Service: The A Location Access Person attribute enables the manager to specify the details of the person at the A location. CenturyLink OSS supports Name (20 characters) and telephone number (10 digits).

Activity Duration

Definition for POTS: This Attribute is not applicable for POTS.

Definition for Design Service: This attribute is returned by CenturyLink when the trouble report is cleared.

The Activity Duration attribute indicates time spent on billable and nonbillable activities. It is possible to indicate the total billable or nonbillable time spent on a group of activities. May contain duration (day, hour, min, sec, msec) for activities NoAccess, DelayedMaintenance, and Dispatch, and whether billable.

Additional Trouble Information List

Definition for POTS: The Additional Trouble Information List attribute further describes the trouble being reported. The manager can only add information, but not remove it. Due to CenturyLink OSS limitations, only the first 47 characters are guaranteed to be displayed in CenturyLink’s OSS (LMOS) for use by CenturyLink repair personnel. However, the customer may send in more characters without error. CenturyLink uses the aLocationAccessAddress, managedObjectInstance, preferredPriority, repeatReport, troubleType, and tspPriority attributes to derive the information that is stored in its 55 characters. The information sent by the customer in this attribute should not repeat information derived by CenturyLink from these customer supplied attributes but further describe the trouble using CenturyLink’s standard abbreviations, where applicable. (See ‘MTG Supported Transactions – Trouble Administration’ at http://www.centurylink.com/wholesale/systems/mtg.html for details.) For Trouble Reports on Idaho lines, if the customer sends the attribute preferredPriority with a value of “life threatening,” then the customer is required to send further information about the situation in the Additional Trouble Information List attribute. If an add or modify is performed, the new customer information will overlay the old customer information. A joint Dispatch Out (DPO) field meet can be requested by populating the Additional Trouble Information List attribute with “DPO Joint Meet” and include date and time (e.g., DPO Joint Meet 07/21/04 3  p.m.). You may also request a joint Dispatch In (DPI) central office meet by populating the Additional Trouble Information List with “DPI Joint Meet” and include date and time (e.g., DPI Joint Meet 07/21/04 3  p.m.). To request a joint meet, you must submit your request no later than 3 p.m. local time the day before the joint meet.

A trouble ticket for IP CENTREX can be submitted by populating the Additional Trouble Information List attribute with “IPCTX” and the telephone number of the line(s) experiencing difficulty.

Definition for Design Service:

The Additional Trouble Information List attribute further describes the trouble being reported. The manager can only add information, but not remove it. Multiple occurrences of AdditionalTroubleInfoItem are allowed. AdditionalTroubleInfoItem limited to 400 characters.

Additional Trouble Status Information

Definition for POTS: For all status changes, a comment describing the status change is returned in this attribute. If the status change is due to the initial MLT test, a concise MLT result description may be returned. If CenturyLink needs to send comments to the customer at any time, then those comments are returned in this Attribute. (See ‘MTG Supported Transactions – Trouble Administration’ at http://www.centurylink.com/wholesale/systems/mtg.html for details.)

Definition for Design Service: For all status changes, a comment describing the status change is returned in this attribute. CenturyLink supports up to 256 characters.

Agent Contact Person

Definition for POTS and Design Service: The responsible CenturyLink Work Center name and phone number are returned when the trouble report is created, and when the trouble report is retrieved.

Authorization List

Definition for POTS: The Authorization List attribute identifies whether authorization is granted or denied by the manager. It also specifies the type of activities that are authorized, and optionally the authorizing person, and the time of authorization.

The customer shall send AuthorizationItem section(s) with one or more authorization Types that are being either granted or denied; with Types (being granted or denied) having a value of true, and the remaining Types having a value of false. (See MTG Interface Specification (Section 5) for example)

This attribute is not used within CenturyLink’s trouble resolution processes for POTS trouble.

Definition for Design Service: Used to indicate authorization for After Hours Repair, Test, Dispatch, No Access, and Delayed Maintenance for request, approve, and deny.

Called Number

Definition for POTS: The Called Number attribute specifies the number being called at the time of trouble detection.

Definition for Design Service: This attribute is not used within CenturyLink’s trouble resolution processes for Design Service trouble.

Cancel Requested By Manager

Definition for POTS and Design Service: The Cancel Requested By Manager attribute is a Boolean that indicates whether the manager has initiated the process to cancel a trouble report. When set to ‘true’, the manager has requested that the trouble report be cancelled.

Close Out Narrative

Definition for POTS: The Close Out Narrative attribute specifies additional information about the problem resolution. This field provides a place for the person who resolved the problem to document any additional information regarding the trouble report closure.

The disposition code (a number) and its associated text description, and the cause code (a number) and its associated text description entered when the trouble report is closed are returned.

Definition for Design Service: The Close Out Narrative attribute specifies additional information about the problem resolution. This field provides a place for the person who resolved the problem to document any additional information regarding the trouble report closure.

Commitment Time

Definition for POTS: The OSS generated commitment time returned by CenturyLink when the trouble report is created. CenturyLink provides a value when a trouble report is created, but may update the value later. The commitment time attribute is provided with each event notification.

Definition for Design Service: The OSS generated commitment time returned by CenturyLink when the trouble report is created. CenturyLink provides a value when a trouble report is created, but may update the value later.

Commitment Time Request

Definition for POTS and Design Service : The Commitment Time Request attribute indicates the trouble cleared time requested by the customer.

Customer Trouble Ticket Number

Definition for POTS Design Service: The Customer Trouble Ticket Number attribute contains the customer’s internal trouble ticket number.

Escalation List

Definition for POTS and Design Service: The Escalation List attribute indicates whether escalation is requested by the customer. It also specifies the person requesting the escalation, the escalation time, and optionally specifies the level of escalation.

Maintenance Service Charge

Definition for POTS: The Maintenance Service Charge attribute indicates whether the customer will be charged for repairs performed on the service. The disposition code entered when the trouble report is closed is used to set the Maintenance Service Charge, which is then returned. (See Appendix L for details.)

Definition for Design Service: The Maintenance Service Charge attribute indicates whether the customer will be charged for repairs performed on the service. The value is set to either Yes or No by the technician when the trouble report is cleared.

Managed Object Access Hours

Definition for POTS: The Managed Object Access Hours attribute defines the specific hours for each day of the week during which access to the managed object (TN) is available. This attribute is not applicable for POTS. CenturyLink believes this is not an issue because currently a technician monitors a line to see if the line is in use. Work is not performed until the line is not in use.

Definition for Design Service: The Managed Object Access Hours attribute defines the specific hours for each day of the week during which access to the managed object (circuit) is available. CenturyLink OSS limitation of three days, one access interval per day. Within the ManagedObjectAccessHours element, customer shall send one or more ManagedObjectAccessHoursItem for the days for which they are providing access hours. The DaysOfWeek section within the ManagedObjectAccessHoursItem should contain one or more days as “true” for which customer is providing access hours and “false” for the remaining days. MTG will use one interval per day. Only the current, previous, and next day will be stored in CenturyLink’s OSS (WFA), relative to the day the trouble report was created.

Managed Object Instance

Definition for POTS: This contains the telephone number, Network Id, and Account Name for the trouble being reported.

Definition for Design Service: This contains the Circuit Id, Network Id, and Account Name for the trouble being reported.

Manager Contact Person

Definition for POTS: The contact name and phone number for the primary customer contact.

Only the first 10 characters of the phone number are used (no delimiters).

Definition for Design Service: The contact name and phone number for the primary customer contact. CenturyLink supports Name (up to 20 characters) and telephone number (only the first 10 characters of the phone number are used (no delimiters)).

Outage Duration

Definition for POTS: This value is returned when the trouble report is closed, calculated as restoredTime less receivedTime.

Definition for Design Service: This value is returned when the trouble report is cleared, calculated as RestoredTime – ReceivedTime - NoAccessDuration – DelayedMaintDuration

Perceived Trouble Severity

Definition for POTS: This attribute allows the manager to indicate the effect of the trouble on the managed object being reported. If a modify is performed, the severity can only be changed to a more significant impairment. For example, if it was originally set to Service Impairment (2), then it can be modified to Out of Service (0). If it was originally set to Out of Service (0), then it cannot be modified.

Definition for Design Service: This attribute allows the manager to indicate the effect of the trouble on the circuit being reported.

Preferred Priority

Definition for POTS: The Preferred Priority attribute defines the urgency with which the manager requires resolution of the problem. The customer is required to send Preferred Priority (value = 4) to indicate a “life threatening” situation for Idaho lines.

Definition for Design Service: The Preferred Priority attribute defines the urgency with which the manager requires resolution of the problem.

Received Time

Definition for POTS and Design Service: The Received Time attribute indicates the date and time when a trouble report was entered. The CenturyLink system generates the value of this Attribute, which is returned when the trouble report is created.

Repeat Report

Definition for POTS: The Repeat Report attribute code value indicates whether there has been a provisioning/installation or a trouble activity on the managed object in the recent past (within the last 30 days).

Repeat Report is used to identify if there is recent service order and/or trouble report activity, defined as:

Unspecified (0)

Recent Installation (1) - Trouble is being reporting within 30 days of service Installation (based on service order activity).

Repeat (2) - Repeats are customer trouble reports received within 30 days of the last case of trouble closed on the same telephone number.

Recent Installation and Repeat (3) – Conditions for both Recent Installation and Repeat are met.

Chronic (4) - Three trouble reports received within a 30 day timeframe.

Recent Installation and Chronic (5) - Conditions for both Recent Installation and Chronic are met.

Definition for Design Service: Same as POTS. Stored in the OSS.

Restored Time

Definition for POTS: The Restored Time attribute indicates when the trouble was resolved. This value is returned when the trouble report is closed.

Definition for Design Service: The Restored Time attribute indicates when the trouble was resolved. This value is returned when the trouble report is cleared.

Target Object Name

Definition for POTS and Design Service: This contains the Trouble Report Id, Network Id, and Account Name for the trouble report.

Trouble Clearance Person

Definition for POTS: The customer person name and phone number that requested the cancellation of a trouble report. Only the first 10 characters of the phone number are used (no delimiters).

Definition for Design Service: The customer person name and phone number that either requested the cancellation of a trouble report, or replied to a CenturyLink request to close a trouble report. Only the first 10 characters of the phone number are used (no delimiters).

Trouble Found

Definition for POTS: The Trouble Found attribute specifies an enumerated code value (per the ATIS Trouble Administration standard), which identifies the problem resolved. Trouble Found is returned when the trouble report is closed. (See Appendix O for details.)

Definition for Design Service: The Trouble Found attribute specifies an enumerated code value (per the ATIS Trouble Administration standard), which identifies the problem resolved. Trouble Found is returned when the trouble report is cleared. (See Appendix O for details.)

Trouble Report Format Identifier

Definition for POTS and Design Service: Based on the type of service, indicates the attributes to be included on the trouble report. Supported values: 1, 2, or 3 (See MTG Interface Specification – Section 4.1).

Trouble Report Identifier

Definition for POTS: The CenturyLink Trouble Report Identifier that is generated by the host system is returned to the customer when the trouble report is created.

Format for POTS: nnnnnnn (e.g., 0123456)

Definition for Design Service: The CenturyLink Trouble Report Identifier that is generated by the host system is returned to the customer when the trouble report is created.

Format for Design Service: AAnnnnnn (e.g., SC123456)

Trouble Report State

Definition for POTS and Design Service: The Trouble Report State attribute specifies an enumerated code value (per the ATIS Trouble Administration standard), which indicates the current state of a trouble report. (See Appendix G.)

Trouble Report Status

Definition for POTS and Design Service: The Trouble Report Status attribute specifies an enumerated code value (per the ATIS Trouble Administration standard), which indicates the current status of a trouble report. (See Appendix H.)

Trouble Report Status Time

Definition for POTS and Design Service: The Trouble Report Status Time attribute identifies the last time at which the Trouble Report Status attribute was known to be changed.

Trouble Report Status Window

Definition for POTS and Design Service: The trouble Report StatusWindow attribute specifies an interval of time within which the customer wishes to be notified of the status of a trouble report (Treated as informational only).

Trouble Type

Definition for POTS: The Trouble Type attribute identifies the category of trouble that is being reported. CenturyLink has identified specific trouble types that are not applicable trouble types for (POTS). In this case, CenturyLink will not create an electronic trouble report for these trouble types and will return an Invalid Attribute Value error. (See Appendix M for details.)

Definition for Design Service: The Trouble Type attribute identifies the category of trouble that is being reported.  CenturyLink has identified specific trouble types that are not applicable trouble types for Design Service. In this case, CenturyLink will not create an electronic trouble report for these trouble types and will return an Invalid Attribute Value error. (See Appendix P for details.)

TSP Priority

Definition for POTS and Design Service: The Telecommunication Service Priority (TSP) Priority attribute conveys TSP codes if applicable between the manager and the agent. Comprised of a 2 character, pattern value="[E0-5][0-5]". Left character represents service provisioning priority and right character represents restoration priority for service.

Appendix B - MTG Supported Transactions – Trouble Administration

Detailed information about Trouble Administration transactions that are supported in Maintenance Ticketing Gateway (MTG) can be found in the ‘MTG Supported Transactions – Trouble Administration’ document located at http://www.centurylink.com/wholesale/systems/mtg.html

Appendix C - MTG Supported Transactions – POTS Service Test

Detailed information about POTS Service Test transactions that are supported in Maintenance Ticketing Gateway (MTG) can be found in the ‘MTG Supported Transactions – POTS Service Test’ document located at http://www.centurylink.com/wholesale/systems/mtg.html

Appendix D - Fallback Error Conditions

Fall Back Report Errors: This section lists the fall back errors as defined by ATIS. Note: There are no Fallback Errors for the POTS Service Test functions.

| Code | Error |
| --- | --- |
| 0 | Circuit/TN Mismatch - Circuit/TN not found or invalid Circuit/TN |
| 1 | Create in progress |
| 2 | Failed Circuit Ownership Validation |
| 3 | Invalid State Code |
| 4 | Invalid Segment |
| 5 | Leading Zeros |
| 6 | New Service Pending |
| 7 | Circuit Disconnected |
| 8 | Invalid Company Assigning Code |
| 9 | Invalid Circuit Format |

Appendix E - References to Other Documents

This document is intended to contain a list of all publications and release dates for all documents referenced in this Implementation Guideline document.

References

ATIS Standard “XML Schema Interface for Fault Management (Trouble Administration),” ATIS-0300003.2010, an industry standard for exchange of trouble ticket information

ATIS- 0300079 –tML Transport Profile: This document recommends a Transport Profile Specification to support the Telecommunications Markup Language (tML) Framework. The intent is to facilitate the interchange of XML formatted business transactions between service requestor and service provider. MTG does not implement every detail of the transport profile, but does use many of the asynchronous concepts described within the guidelines.

XML POTS Service Test ATIS-0300002.2009, “XML Schema Interface for POTS Service Test.” This standard provides an XML schema information model for POTS Service Test based on ATIS-0300262.2007 and an XML schema interface for POTS Service Test function specified in the same ANSI standard.

Additional reference documents can be found at http://www.centurylink.com/wholesale/systems/mtg.html including:

- MTG Interface Specification

- MTG Supported Transactions – Trouble Administration

- MTG Supported Transactions – POTS Service Test

Appendix F – Abbreviations for Problem Descriptions

Standard Abbreviations for Problem Descriptions

| ABBREVIATIONS | MEANING |
| --- | --- |
| AAB | ALL ACCESS BUSY |
| ACC | ACCESS |
| ADL | ADDITIONAL |
| ADV | ADVISED |
| ALCLS | ALL CALLS |
| ALIT | ALI (AUTOMATIC LINE TEST) |
| ALL ONES | GETTING ALL ONES |
| ALM | ALARM |
| ALPHS | ALL PHONES |
| ANA TST | ANALOG TEST LINE |
| ANI TMOUT | ANI TIMEOUT |
| APT | APARTMENT |
| ASAP | AS SOON AS POSSIBLE |
| ASW | AERIAL SERVICE WIRE |
| /T | AT TIMES OR INTERMITTANT |
| CLEC/IXCN | CLEC/IXCENTION |
| B4 | BEFORE |
| BAD BAL | BAD BALANCE |
| BAD ERL | BAD ERL |
| BAD FREQ | DOES NOT PASS FREQ RESPONSE |
| BAD LVLS | LEVELS OUT OF LIMITS |
| BDR | BELL DOESN’T RING |
| BDR EXT | BELL DOES NOT RING2 |
| BIPOL ERR | BIPOLAR VIOLATIONS |
| BO | BUSINESS OFFICE |
| BR | BELL RINGS |
| BRAA | BELL RINGS AFTER ANSWERED |
| BRCA | BELL RINGS CAN’T ANSWER |
| BRKN | BROKEN |
| BRWD | BELL RINGS WHILE DIALING |
| BSW | BURIED SERVICE WIRE |
| BUS | BUSINESS |
| BUSY | BUSY |
| BSY | ALWAYS BUSY/CANNOT BE CALLED BUSY |
| BSY TRIPS | RINGS THEN GOES BUSY |
| C/RUN CSU | CANNOT RUN TO CSU |
| C/RUN OSU | CANNOT RUN TO OSU |
| CALL RET | CALL RETURN NOT WORKING |
| CANCEL | CANCEL |
| CANT MEET | CANNOT MEET |
| CBC | CAN’T BE CALLED |
| CBDT | CAN’T BREAK DIAL TONE |
| CBDT | CAN’T BREAK DIAL TONE |
| CBH | CAN’T BE HEARD |
| CBR | CAN’T BE REACHED |
| CBS | CANNOT BE SIGNALLED |
| CC 700 | CANNOT CALL 700 |
| CC 800/888 | CANNOT CALL 800/888 |
| CC 900 | CANNOT CALL 900 |
| CC 911 | CANNOT CALL 911 |
| CC DA | CANNOT CALL DA |
| CC LD | CANNOT CALL LONG DISTANCE |
| CC LLD | CANNOT CALL INTERLATA TOLL |
| CC TRACE | CALL TRACE NOT WORKING |
| CCE | CUSTOMER CHECKED EQUIPMENT |
| CCF | CAN’T CALL FORWARD |
| CCO | CAN’T CALL OUT |
| CD | COMPLETION DATE |
| CF | CALL FORWARDING |
| CFBL | CALL FORWARDING BUSY LINE |
| CFDA | CALL FORWARDING DON’T ANSWER |
| CFWN | CALL FORWARDING WRONG NUMBER |
| CH | CAN’T HEAR |
| CHK | CHECK |
| CHNG | CHANGE |
| CID | CALLER ID |
| CKD | CIRCUIT DEAD/DEAD AT CIRCUIT |
| CKT DOWN | CIRCUIT DOWN |
| CKT FAIL | FAILING CIRCUIT |
| CKT SZD | SEIZURE ON CIRCUIT |
| CL BLK | CALL BLOCKING NOT WORKING |
| CL RET BLK | CALLER RETURN BLOCK NOT WORKING |
| CL XFER | CALL TRANSFER PROBLEM |
| CLB4 | CALL BEFORE |
| CLD | CALLED |
| CLICKING | CLICKING |
| CLIPPING | CLIPPING |
| CLR | CALLER |
| CNTX | CENTREX |
| COMM | COMMITMENT |
| CONV | CONVERSATION |
| CPH | CALLING PARTY HOLD |
| CPIW | CUSTOMER PROVIDED INSIDE WIRE |
| CPU | CALL PICK UP |
| CR | CALL REJECT |
| CRC | CAN’T RELEASE CIRCUIT |
| CRDA | CANNOT RECEIVE DATA |
| CRT | CATHODE RAY TUBE |
| CSDA | CANNOT SEND DATA |
| CSO | CANNOT SIGNAL |
| CUT CABLE | CUT CABLE |
| CUT OFF | CUT OFF |
| CW | CALL WAITING |
| CWD | CALL WAITING DELUXE |
| CXX | NEW OR ADDING INFORMATION |
| 2DY | TODAY |
| DAMAGE | DAMAGE |
| DATA EQUIP | DATA EQUIPMENT |
| DATA SET | DATA SET |
| DD | DUE DATE |
| DEAD PC | CANNOT ACTIVATE PC |
| DEL | DELAY |
| DIAL BLK | REPEAT DIAL BLOCK NOT WORKING |
| DIE | DISCONNECT IN ERROR |
| DIG TST | DIGITAL TEST LINE |
| DISC | DISCONNECT |
| DISP | DISPATCH |
| DISTANT | DISTANT |
| DL TMOUT | PARTIAL DIAL TIMEOUT |
| DMARC | DEMARCATION POINT |
| DROP OUTS | DROPOUTS |
| DT | DIAL TONE |
| DTAD | DIAL TONE AFTER DIALING |
| DTWT | DIAL TONE WHILE TALKING |
| ECO | ECHO |
| EQUIP | EQUIPMENT |
| ERR | ERRORS |
| EST | ESTIMATE |
| ETIR | EVERY TIME IT RAINS |
| EXT | EXTENSION |
| FAC ALM | FACILITY ALARM |
| FADE IN/OUT | FADES IN AND OUT |
| FADES | FADING |
| FEAT | FEATURES |
| FEAT BRK | CUSTOM CALL FEATURES DO NOT WORK |
| FLS PULSE | FALSE KEY PULSE |
| FRI | FRIDAY |
| FRM ERR | FRAME ERRORS |
| FRM ERR/H | FRAME ERRORS HICAP |
| FRM SLPS | FRAME SLIPS |
| FSR | FALSE RINGS |
| FST BSY | FAST BUSY |
| GBI | GETS BUSY IN |
| GCO | GETS CUT OFF |
| GRBL | GARBLED |
| GRBL DATA | GARBLED DATA |
| GRND | GROUND |
| GRND HUM | GROUND HUM |
| GWN | GETS WRONG NUMBER |
| HAE | HARMONIC DISTORTION |
| HAZARD | HAZARD |
| HI ROLL | HIGH END ROLLOFF |
| HI/DRY | HIGH AND DRY |
| HICAPDOWN | HICAP DOWN |
| HID | HIGH DISTORTION |
| HIL | HIGH LEVELS |
| HIS | HISTORICAL REPORTS |
| HITS | MULTIPLE SHORT DURATION HIT |
| HOL | HOLLOW |
| HOOL | HEARS OTHERS ON LINE |
| HOT LVL | HOT LEVELS |
| HTG | HUNTING |
| HUM ON LN | HUM ON LINE |
| HUNG UP | HUNG UP |
| IMP NSY | IMPULSE NOISE |
| IN FAIL | HIGH RATE INCOMPLETE INCOMING |
| IN LPBK | CIRCUIT IN LOOPBACK |
| IN OK | INCOMING OK |
| INF | INFORMATION |
| INFO | INFORMATION |
| INSP | INSPECT |
| INV DATA | INVALID DATA |
| IW | INSIDE WIRE |
| JITTER | PHASE JITTER |
| LBO | LIGHT BURNED OUT |
| LCR | LAST CALL RETURN |
| LD | LONG DISTANCE |
| LINE LOSS | LINE LOSS |
| LOC | LOCATION |
| LOL | LOW LEVELS |
| LONG LVL | LONG LEVELS |
| LOOSE JK | LOOSE JACK |
| LOUD | LOUD |
| LOW ROLL | LOW END ROLLOFF |
| LOW SF | LOW SF |
| LOW SIG | LOSS EPSCS OR SWITCHED |
| LTR | LOST TIME REPORT |
| LXD | LINE CROSSED |
| MEM | MEMORY |
| MIS PULSE | MISPLACED START PULSE |
| MISC | MISCELLANEOUS |
| MISS COMM | MISSED COMMITMENT |
| MKBSY | MAKE BUSY |
| MODEM | MODEM |
| MON | MONDAY |
| MONT CKT | MONITOR CIRCUIT |
| MSC | MAINTENANCE OF SERVICE CHARGE |
| MUT DIG | MUTILATED DIGIT GROUP |
| # | NUMBER |
| #CHG | NUMBER CHANGED |
| ND EQLZD | NEEDS EQUALIZED |
| NDT | NO DIAL TONE |
| NDT ORDER | NEW SERVICE NOT WORKING |
| NDT/T | NO DIAL TONE AT TIMES |
| NI | NETWORK INTERFACE |
| NO ANI | ANI FAILURE |
| NO ANSBK | NO ANSWER BACK |
| NO CONT | NO CONTINUITY |
| NO CXR | NO CARRIER |
| NO D CHNL | D CHANNEL DOWN |
| NO LPBK | NO LOOP BACK |
| NO NTWK | NETWORK FAILURE |
| NO POLL | NOT POLLING |
| NO PULSE | NO KEY PULSE |
| NO REG | NO REGISTER |
| NO RESP | NO RESPONSE |
| NO SF | NO SF |
| NO SYNC | LOSS OF SYNC |
| NRNA | NO RING NO ANSWER |
| NSY | NOISY |
| NSY EPS | NOISE EPSCS OR SWITCHED SERVICES |
| NSY/T | INTERMITTENT NOISE |
| NTR | CANNOT TRANSMIT CANNOT RECEIVE |
| NWNK | NO WINK START |
| OD | OUT OF ORDER |
| OG OK | OUTGOING OK |
| OHOP | ONLY HAS ONE PHONE |
| OO FRM | OUT OF FRAME |
| OO SPEC | OUT OF SPECIFICATION |
| OOS | OUT OF SERVICE |
| OPEN | OPEN |
| OPEN EPSC | OPEN EPSCS OR SWITCHED SERVICES |
| OPENDMARC | OPEN TO DEMARC |
| OUT FAIL | OUTGOING FAILURE AFTER WINK |
| OVERSEAS | CANNOT CALL OVERSEAS |
| PERM SIG | PERMANENT SIGNAL |
| PH | PHONE |
| PHYS | PHYSICAL |
| PLZ | PLEASE |
| PRC DEAD | PROCESSOR DEAD |
| PRN | HIGH SPEED PRINTER |
| PROT | PROTECTOR |
| PTY | PARTY |
| PTYLN | PARTY LINE |
| QTD | QUOTED |
| RCF | REMOTE CALL FORWARDING |
| REQ ASSIST | REQUEST TEST ASSIST |
| REQ DISP | REQUEST DISPATCH |
| RES | RESIDENCE |
| RLS | RELEASE |
| RLS CKTEC | RELEASE CKT REQUESTED BY EC |
| RLS CKTIC | RELEASE CKT REQUESTED BY IC |
| RLS FACEC | RELEASE FACILITY REQUESTED BY EC |
| RLS FACIC | RELEASE FACILITY REQUESTED BY IC |
| RMV | REMOVE |
| RNA | RING NO ANSWER |
| RNA CKL | CANNOT RAISE A CIRCUIT LOCATION |
| RNTRBL | OTHER RING TROUBLE |
| RO CKT | RECORDING ON CIRCUIT |
| ROH | RECEIVER OFF HOOK |
| ROL | RECORDING ON LINE OR INTERCEPT |
| ROUTINE | REQUEST FOR ROUTINE |
| RPR | REPAIR |
| RPT DIAL | REPEAT DIAL NOT WORKING |
| RPTD | REPORTED |
| RPTR | REPEATED REPORT |
| RTF | ROUTINE TEST FAILURE |
| RVY RPT | RECOVERY REPORT |
| SAT | SATURDAY |
| SC8/30 | SPEED CALLING 8 OR 30 |
| SFTWR ALM | SOFTWARE GROUP ALARM |
| SGD ERR | STATION GROUP DESIGNATION DIGIT FAILURE |
| SIG ERR | SIGNALING NETWORK FAILURE INCOMING |
| SLIP | SLIP |
| SLOW RESP | SLOW RESPONSE |
| SO | ORDER WORK |
| SOL | STATIC ON LINE |
| STAT | STATUS |
| STK SNDR | STUCK SENDER |
| STRMR | STREAMER |
| SUN | SUNDAY |
| SUP | SUPERVISION/IMPROPER SUPERVISION |
| SUPV | SUPERVISOR |
| SWITCH | SWITCH OR TRUNK RELATED |
| SYS | SYSTEM |
| T1 ERRS | DEGRADATION OF T1.5 |
| TAG LINE | LINES NEED TAGGING |
| TC | TRANSFER OF CALLS |
| THURS | THURSDAY |
| TIC | TROUBLE ISOLATION CHARGE |
| TKT | TICKET |
| TN | TELEPHONE NUMBER |
| TRACE BLK | CALL TRACE BLOCK NOT WORKING |
| TRAN | TRANSMISSION |
| TRBL | TROUBLE |
| TRK BLKD | TRUNK BLOCKED FAR END |
| TTY | TTY SET |
| VIDO EQUIP | VIDEO EQUIPMENT |
| VM | VOICE MESSAGE |
| VOIC EQUIP | VOICE EQUIPMENT |
| 3WC | THREE WAY CALLING |
| W/O | WITHOUT |
| WATS FSR | OUT WATS RINGING IN |
| WED | WEDNESDAY |
| WKG | WORKING |
| XFER | TRANSFER |
| XMD | CROSS MODULATION |
| XTLK | CROSS TALK |
| XTR DIGIT | EXTRA DIGIT |
| XTR PULSE | EXTRA PULSE |

APPENDIX G - TROUBLE STATE Mapping

| ATIS - Trouble State Description | ATIS Code |
| --- | --- |
| Queued | 0* |
| OpenActive | 1 |
| Deferred | 2 |
| Cleared | 3 |
| Closed | 4 |
| Disabled | 5* |

*Not supported in MTG

Queued: The Trouble Report (TR) is queued in the SP’s gateway until a trouble report is created in its OSS(s).

OpenActive: Repair and administrative activities (excluding screening) have been initiated.

Deferred: Corrective action on the TR has been suspended; the duration timer has been stopped by CenturyLink.

Cleared: Trouble has been corrected, awaiting closure; awaiting verification for closure from the Customer.

Closed: The TR had been closed and trouble history will be noted; no further action will be performed; the customer may or may not have authorized the closure.

Disabled: The gateway is inoperative/unavailable for traffic.

APPENDIX H - TROUBLE STATUS Mapping

| ATIS Definition | Enumerated Value from ATIS |
| --- | --- |
| screening | 1 |
| testing | 2 |
| dispatchedIn | 3 |
| dispatchedOut | 4 |
| preassignedOut | 5 |
| bulkDispatchedOut | 6 |
| startRepair | 7 |
| pendingTest | 8 |
| pendingDispatch | 9 |
| requestRepair | 10 |
| referMtceCenter | 11 |
| referVendor | 12 |
| noAccessOther | 13 |
| startNoAccess | 14 |
| stopNoAccess | 15 |
| startDelayedMtce | 16 |
| stopDelayedMtce | 17 |
| troubleEscalated | 18 |
| craftDispatched | 19 |
| temporaryOK | 20 |
| cableFailure | 21 |
| originatingEquipFailure | 22 |
| backOrder | 23 |
| clearedCustNotAdvised | 24 |
| clearedCustAdvised | 25 |
| clearedAwaltingCustVerification | 26 |
| closedOut | 27 |
| closedOutByCustReq | 28 |
| closedOutCustVerified | 29 |
| closedOutCustDenied | 30 |
| canceledPendingWorkInProgress | 31 |
| canceledPendingTestCompletion | 32 |
| canceledPendingDispatchCompl | 33 |
| techOnSite | 34 |
| techLeftSite | 35 |

APPENDIX I – Valid State/Status Combinations for POTS

| FunctionCode | Function Message | ASNI State | ANSI Status |
| --- | --- | --- | --- |
| BDO | Bulk Dispatched Out, Report one of several routed to a Technician | 1 | 6 |
| BKO | Back Order, Not completed because equipment is back ordered | 2 | 23 |
| CAF | Cable Failure | 1 | 21 |
| CCA | Cleared: Customer Advised, Service has been restored and customer advised | 3 | 25 |
| CLO | Closed, Report is closed in system and no longer electronically bonded | 4 | 27 |
| CNA | Cleared: Customer Advised, Service has been restored and customer advised | 3 | 25 |
| DPI | Dispatched In | 1 | 3 |
| DPO | Dispatched Out | 1 | 4 |
| HLD | Hold, Report is on hold pending further action | 2 | 16 |
| NAO | No Access Other, Technician had no access to TELCO equipment in order to restore service | 2 | 13 |
| NAS | No Access Subscriber, Outside tech had no access to customer premises | 2 | 14 |
| PAO | Preassigned Out | 1 | 5 |
| PD2 | Pending Dispatch | 1 | 9 |
| PD3 | Pending Dispatch | 1 | 9 |
| PD4 | Pending Dispatch | 1 | 9 |
| PD5 | Pending Dispatch | 1 | 9 |
| PDB | Pending Dispatch | 1 | 9 |
| PDC | Pending Dispatch | 1 | 9 |
| PDF | Pending Dispatch | 1 | 9 |
| PDG | Pending Dispatch | 1 | 9 |
| PDI | Pending Dispatch | 1 | 9 |
| PDM | Pending Dispatch | 1 | 9 |
| PDO | Pending Dispatch | 1 | 9 |
| PDS | Pending Dispatch | 1 | 9 |
| PDT | Pending Test, Report is pending test by a screener | 1 | 8 |
| PS | Pending Screen | 1 | 1 |
| PSH | Pending Screen | 1 | 1 |
| PSM | Pending Screen | 1 | 1 |
| PUT | Pending Screen | 1 | 1 |
| RBC | Referred to Business Center, SAB (Send Alternate Bureau) status cannot be used manually | 1 | 11 |
| RCC | Returned To Control Center, SAB (Send Alternate Bureau) status cannot be used manually | 1 | 11 |
| ROP | Referred to Alternate Bureau | 1 | 11 |
| RRC | Referred To Remote Maintenance Administration and Traffic System, SAB (Send Alternate Bureau) status cannot be used manually | 1 | 11 |
| RSC | Referred To Switching Control Center, SAB (Send Alternate Bureau) status cannot be used manually | 1 | 11 |
| RSS | Referred To Special Service Center, SAB (Send Alternate Bureau) status cannot be used manually | 1 | 11 |
| TMK | Temporary OK, Service is restored but is temporary | 3 | 20 |
| TSM | Tested, Report has been tested by a screener | 1 | 2 |
| TST | Tested, Report has been tested by a screener | 1 | 2 |

APPENDIX J - Trouble Types

| Trouble Type | TA Code |
| --- | --- |
| NoDialToneGroup | 0100 |
| NoDialTone | 0101 |
| SlowDialTone | 0102 |
| CircuitDead | 0103 |
| CanNotCallOutGroup | 0200 |
| CanNotCallOut | 0201 |
| CanNotBreakDialTone | 0203 |
| DialToneAfterDialing | 0204 |
| HighandDry | 0205 |
| CanNotRaise | 0206 |
| AllAccessBusy | 0207 |
| canNotCallOut2 | 0208 |
| CanNotCallLongDistance | 0209 |
| CanNotCallOverseas | 0210 |
| SpeedCall | 0211 |
| cannotCall911 | 0212 |
| cannotCall700 | 0213 |
| cannotCall800/888 | 0214 |
| cannotCall900 | 0215 |
| CannotCallDA | 0216 |
| CannotCallInterLATAToll | 0217 |
| CanNotBeCalledGroup | 0300 |
| CanNotBeCalled | 0301 |
| CanNotBeCalledBusy | 0302 |
| DoNotGetCalled | 0303 |
| CanNotTripRing | 0304 |
| FalseRings | 0305 |
| DoNotAnswer | 0306 |
| ReachRecording | 0307 |
| CanNotRaiseAStation | 0308 |
| CanNotRaiseAdrop | 0309 |
| CanNotRaiseACircuitLocation | 0310 |
| RingNoAnswer | 0311 |
| Reorder | 0312 |
| AlwaysBusy | 0313 |
| BellDoesNotRing | 0314 |
| bellDoesNotRing2 | 0315 |
| BellRingsCannotAnswer | 0316 |
| bellRingsAfterAnswer | 0317 |
| noRingNoAnswer | 0318 |
| otherRingTrouble | 0319 |
| receivesCallsForWrongNumber | 0320 |
| recordingOnLine | 0321 |
| ringsThenGoesBusy | 0322 |
| canNotBeHeardGroup | 0400 |
| canNotBeHeard | 0401 |
| canNotHear | 0402 |
| fading | 0403 |
| distant | 0404 |
| reachedWrongNumberGroup | 0500 |
| reachedWrongNumber | 0501 |
| circuitOperationGroup | 0600 |
| open | 0601 |
| falseDisconnect | 0602 |
| grounded | 0603 |
| canNotBeSignalled | 0604 |
| canNotSignal | 0605 |
| permanentSignal | 0606 |
| improperSupervision | 0607 |
| supervision | 0608 |
| canNotMeet | 0609 |
| canNotReleaseCircuit | 0610 |
| hungUp | 0611 |
| noWinkStart | 0612 |
| noSF | 0613 |
| lowSF | 0614 |
| noContinuity | 0615 |
| openToDEMARC | 0617 |
| noRingGenerator | 0618 |
| badERL | 0619 |
| echo | 0620 |
| hollow | 0621 |
| circuitDead | 0622 |
| circuitDown | 0623 |
| failingCircuit | 0624 |
| noSignal | 0625 |
| seizureOnCircuit | 0626 |
| lossEPSCSorSwitched | 0627 |
| monitorCircuit | 0628 |
| newServiceNotWorking | 0629 |
| openEPSCSorSwitchedServices | 0630 |
| otherVoiceDescribeAdditInfo | 0631 |
| trunkBlockedFarend | 0632 |
| badBalance | 0633 |
| highRateIncompleteIncoming | 0634 |
| outgoingFailureAfterWink | 0635 |
| cutOffsGroup | 0700 |
| cutOff | 0701 |
| noiseProblemGroup | 0800 |
| intermittentNoise | 0801 |
| noisy | 0802 |
| foreignTone | 0803 |
| clipping | 0804 |
| crossTalk | 0805 |
| staticOnLine | 0806 |
| groundHum | 0807 |
| hearsOtherOnLine | 0808 |
| humOnLine | 0809 |
| clicking | 0810 |
| noiseEPSCSorSwitchedServices | 0811 |
| levelTroublesGroup | 0900 |
| lowLevels | 0901 |
| highLevels | 0902 |
| longLevels | 0903 |
| hotLevels | 0904 |
| highEndRollOff | 0905 |
| lowEndRollOff | 0906 |
| needsEqualized | 0907 |
| lineLoss | 0908 |
| doesNotPassFreqResponse | 0909 |
| levelsOutOfLimits | 0910 |
| miscellaneousTroublesGroup | 1000 |
| carrierDown | 1002 |
| recordingOnCircuit | 1010 |
| outwatsRingingIn | 1012 |
| remoteAccess | 1013 |
| multipleShortDurationHit | 1016 |
| networkFailure | 1022 |
| memoryServiceProblemGroup | 1100 |
| picTrouble | 1101 |
| callTransferProblem | 1102 |
| callWaitingProblem | 1103 |
| customCallFeature | 1104 |
| threeWayCalling | 1105 |
| callTraceNotWorking | 1106 |
| callTraceBlockNotWorking | 1107 |
| repeatDialNotWorking | 1108 |
| repeatDialBlockNotWorking | 1109 |
| callReturnNotWorking | 1110 |
| calledReturnBlockNotWorking | 1111 |
| callerIdentificationNotWorking | 1112 |
| callBlockingNotWorking | 1113 |
| voiceMessagingServicesProblem | 1114 |
| callForwardingNotWorking | 1115 |
| callForwardingBusyLineNotWorking | 1116 |
| callForwardingNoAnswerNotWorking | 1117 |
| huntingNotWorking | 1118 |
| selectiveCallForwardingNotWorking | 1119 |
| cannotSetupUniqueRingID | 1120 |
| callerIDBlockNotWorkingPerLine | 1121 |
| callerIDBlockNotWorkingPerCall | 1122 |
| cannotRemoveBlockingOnASingleCall | 1123 |
| dataTroubleGroup | 1200 |
| canNotReceiveData | 1201 |
| canNotSendData | 1202 |
| canNotTransmitCanNotReceive | 1203 |
| noReceive | 1204 |
| noResponse | 1205 |
| delay | 1206 |
| noCarrier | 1212 |
| errors | 1224 |
| garbledData | 1225 |
| invalidData | 1226 |
| slowResponse | 1228 |
| otherDataDescribeAdditInfo | 1229 |
| wireBrokSetBrokePoleDown | 1415 |
| otherCaseGroup | 1500 |
| callTransferProblem | 1501 |
| callWaitingProblem | 1502 |
| customCallFeatureDoNotWork | 1503 |
| information | 1504 |
| threeWayCallingProblem | 1505 |
| orderWork | 1506 |
| recovery | 1600 |
| recoveryReport | 1601 |

APPENDIX K - POTS Disposition Code to Trouble Found

| Disposition Code | Definition | T1.227 Code | Trouble Found Definition |
| --- | --- | --- | --- |
| 01 | Public Segment - Applies To All Troubles Outside The Phone |  |  |
| 0110 | External Components not listed below | 24 | Public Service Coin Set |
| 0111 | Coin/Coinless Housing | 24 | Public Service Coin Set |
| 0112 | Rotary/TT Dial | 24 | Public Service Coin Set |
| 0114 | Loud button assembly | 24 | Public Service Coin Set |
| 0115 | Handset/Handset cord | 24 | Public Service Coin Set |
| 0117 | Switch-hook/Cradle/Intl Ckt | 24 | Public Service Coin Set |
| 0119 | Instruction Card/Number plate | 24 | Public Service Coin Set |
| 0150 | Enclosure misc. components | 24 | Public Service Coin Set |
| 0151 | Glass | 24 | Public Service Coin Set |
| 0152 | Lights | 24 | Public Service Coin Set |
| 0154 | Shelf | 24 | Public Service Coin Set |
| 0155 | Enclosure | 24 | Public Service Coin Set |
| 0156 | Power | 24 | Public Service Coin Set |
| 0158 | Directory | 24 | Public Service Coin Set |
| 0159 | Signage | 24 | Public Service Coin Set |
| 0160 | Miscellaneous Assemblies | 24 | Public Service Coin Set |
| 0168 | TDD Unit | 24 | Public Service Coin Set |
| 0170 | Clean Equipment | 24 | Public Service Coin Set |
| 0171 | Preventive Maintenance/Routine NTF | 24 | Public Service Coin Set |
| 02 | Public Segment - Applies To All Troubles Inside The Phone |  |  |
|  | Set Internal/Shelf/Book |  |  |
| 0210 | Set internal components not listed below | 24 | Public Service Coin Set |
| 0211 | Chassis | 24 | Public Service Coin Set |
| 0212 | Coin chute | 24 | Public Service Coin Set |
| 0213 | Escrow/Hopper/Relay Assembly | 24 | Public Service Coin Set |
| 0216 | Full Coin Box | 24 | Public Service Coin Set |
| 0217 | Signal Unit/Totalizer | 24 | Public Service Coin Set |
| 0219 | Validator | 24 | Public Service Coin Set |
| 0231 | Software/Reprogram | 24 | Public Service Coin Set |
| 0232 | Bcustomerery/Power/Transformer | 24 | Public Service Coin Set |
| 0233 | PCB (Printed Circuit Board) | 24 | Public Service Coin Set |
| 0234 | Card Reader Assembly | 24 | Public Service Coin Set |
| 0237 | LCD Display | 24 | Public Service Coin Set |
| 0240 | Coin Collection Misc. | 24 | Public Service Coin Set |
| 0246 | Prevent Full Box | 24 | Public Service Coin Set |
| 0247 | Tripped Box, Box not Seated | 24 | Public Service Coin Set |
|  | Miscellaneous |  |  |
| 0290 | Other Miscellaneous | 24 | Public Service Coin Set |
| 0291 | Foreign coin grabber | 24 | Public Service Coin Set |
| 0292 | Tel-Cart bcustomerery | 24 | Public Service Coin Set |
| 0293 | Lock or key | 24 | Public Service Coin Set |
| 0294 | Coin on ledge | 24 | Public Service Coin Set |
| 0295 | Box not open, not seated | 24 | Public Service Coin Set |
| 0296 | String cutter | 24 | Public Service Coin Set |
| 0297 | Telecart circuitry | 24 | Public Service Coin Set |
| 0298 | Board/Card - Inmate Service | 24 | Public Service Coin Set |
| 0299 | Conduit | 24 | Public Service Coin Set |
| 03 | Regulated Station Wiring |  |  |
| 0331 | Simple Network terminating Wire- for coin phone and/or wire between terminal and demarc | 19 | Station Wiring |
| 0341 | Network Interface, Registration Jack, NCTE | 16 | Station Product Terminal |
| 0371 | Protection | 30 | Protective Connecting Arrangement |
| 0381 | Drop or BSW bad, replaced or repaired | 44 | Outside Wire |
| 0382 | *Broadband drop replaced or repaired | 44 | Outside Wire |
| 0383 | Buried Service Wire bad, placed temp Drop on Grnd | 44 | Outside Wire |
| 0385 | Temp Drop On Grnd damaged; replaced or repaired | 44 | Outside Wire |
| 0387 | Temp Drop On Grnd, cut over to permanent BSW | 44 | Outside Wire |
| 04 | Outside Plant |  |  |
|  | Cable Not Repaired |  |  |
| 0401 | Pair Transferred/Cut to clear | 5 | Facility |
| 0402 | Bridge tap removed/Cut dead ahead | 5 | Facility |
| 0403 | Pair transposed | 5 | Facility |
|  | Copper Cable |  |  |
| 0410 | Intermittent/Came clear | 1 | Came Clear |
| 0411 | Fault in sheath, conductor or pair | 5 | Facility |
| 0421 | Splice case, closure | 5 | Facility |
| 0431 | Terminal, Cross Box, GAI | 5 | Facility |
| 0434 | Encap plant; unable to clear; laid temp drop | 5 | Facility |
| 0441 | Rural, Open or Urban wire | 5 | Facility |
| 0461 | Analog pair gain system | 46 | Outside Plant Equipment |
| 0471 | Digital pair gain system | 46 | Outside Plant Equipment |
|  | Associated Trouble |  |  |
| 0481 | All pole, guy, anchor, trench or other miscellaneous trouble | 46 | Outside Plant Equipment |
|  | Fiber Optic Cable |  |  |
| 0483 | Buried or aerial fiber optic cable | 47 | Outside Plant Fiber Optic |
|  | Broadband |  |  |
| 0492 | Hut, replacing broadband cards | 46 | Outside Plant Equipment |
| 0493 | ONU-COAX power associated trouble | 46 | Outside Plant Equipment |
| 0494 | ONU-Fiber | 47 | Outside Plant Fiber Optic |
| 0495 | ONU-Protection | 46 | Outside Plant Equipment |
| 05 | Central Office |  |  |
|  | Central Office Equipment |  |  |
| 0505 | Wireless port into to Wireline | 9 | Information |
| 0509 | Wireless port out to Wireless | 9 | Information |
| 0510 | Other/Came clear | 1 | Came Clear |
| 0511 | Common equipment processor | 2 | Central Office |
| 0512 | Common equipment peripheral | 2 | Central Office |
| 0513 | Line Equipment | 2 | Central Office |
| 0514 | Billing Equipment | 2 | Central Office |
| 0515 | Trunk, includes calling party hold | 6 | Central Office Facility |
| 0516 | Trunk, Customer/IEC | 6 | Central Office Facility |
| 0518 | Held by traffic | 2 | Central Office |
| 0519 | SS7 network failure | 35 | Service Node |
|  | Central Office Translations |  |  |
| 0520 | Other | 3 | Switch Trouble |
| 0521 | Software customer error | 3 | Switch Trouble |
| 0522 | Parameter error | 3 | Switch Trouble |
| 0523 | Translations Questionairres (TQs) and ASRs | 3 | Switch Trouble |
| 0524 | Routing | 3 | Switch Trouble |
| 0525 | Marketing Centrex forms | 3 | Switch Trouble |
| 0526 | Other marketing forms | 3 | Switch Trouble |
| 0527 | CenturyLink translations letters | 3 | Switch Trouble |
| 0528 | Trunking software | 3 | Switch Trouble |
| 0529 | Special Requests | 3 | Switch Trouble |
|  | Distributing Frames |  |  |
| 0530 | Other/Came Clear | 1 | Came Clear |
| 0531 | Cross-Connect missing | 50 | CO Equipment Frames |
| 0532 | Cross-Connect broken | 50 | CO Equipment Frames |
| 0533 | Cross-Connect work error | 50 | CO Equipment Frames |
| 0534 | Intercept work error (EM only) | 50 | CO Equipment Frames |
| 0535 | Protection/reversing device/coils | 50 | CO Equipment Frames |
| 0536 | Improper connection | 50 | CO Equipment Frames |
| 0537 | Cross-Connect document error | 50 | CO Equipment Frames |
| 0538 | Request for Assistance | 50 | CO Equipment Frames |
| 0539 | Customer change request/Not ready | 50 | CO Equipment Frames |
|  | Line Translations |  |  |
| 0540 | Other/Came clear | 1 | Came Clear |
| 0541 | RCMAC work error | 3 | Switch Trouble |
| 0542 | Flowthrough system error | 3 | Switch Trouble |
| 0543 | Inaccurate missing work document: HPS | 3 | Switch Trouble |
| 0544 | Inaccurate missing work document: SBS | 3 | Switch Trouble |
| 0545 | Inaccurate missing work document: BGS | 3 | Switch Trouble |
| 0546 | Inaccurate missing work document: Other MU | 3 | Switch Trouble |
| 0547 | Inaccurate missing work document: LPC/MPAC | 3 | Switch Trouble |
| 0548 | Inaccurate missing work document: CDAC/BDAC/BCSC | 3 | Switch Trouble |
| 0549 | Inaccurate missing work document: Network Tech | 3 | Switch Trouble |
|  | Power |  |  |
| 0550 | Other/Came clear | 1 | Came Clear |
| 0551 | DC Power Equipment | 2 | Central Office |
| 0552 | AC Power Equipment | 2 | Central Office |
| 0554 | Standby Emergency Power | 2 | Central Office |
|  | Miscellaneous |  |  |
| 0560 | Other/Came clear | 1 | Came Clear |
| 0561 | Subscriber line carrier | 46 | Outside Plant Equipment |
| 0562 | Line testing equipment | 51 | CO Concentrator |
| 0563 | Concentrator | 51 | CO Concentrator |
| 0564 | Range extender | 2 | Central Office |
| 0565 | Carrier system | 46 | Outside Plant Equipment |
|  | Special Services Equipment |  |  |
| 0570 | Other/Came clear | 1 | Came Clear |
| 0571 | Design | 2 | Central Office |
| 0573 | Carrier channel | 2 | Central Office |
| 0574 | Signaling | 35 | Service Node |
| 0575 | Repeater | 2 | Central Office |
|  | Radio System |  |  |
| 0580 | Other/Came Clear | 1 | Came Clear |
| 0581 | Maritime | 2 | Central Office |
| 0582 | Ship to Shore | 2 | Central Office |
| 0583 | G2 Control | 2 | Central Office |
| 0584 | Enhanced Mobile Telephone Service control | 2 | Central Office |
| 0585 | Enhanced Mobile Telephone Service/B | 2 | Central Office |
| 0586 | Telephone Mobile Radio Service manual | 2 | Central Office |
| 0587 | Telephone Mobile Radio Service aitp, atoc | 2 | Central Office |
| 0588 | Advanced Mobile Phone System | 2 | Central Office |
|  | Data Base for Driven Services |  |  |
| 0590 | Other/Came clear | 1 | Came Clear |
| 0591 | Calling Card Services (ABS-LIDB) | 3 | Switch Trouble |
| 0592 | Automatic Intercept System | 3 | Switch Trouble |
| 0593 | Expanded 911 Service | 3 | Switch Trouble |
| 0596 | 800 Data Base | 3 | Switch Trouble |
| 0597 | 700 Services | 3 | Switch Trouble |
| 0598 | Expanded 800 Service | 3 | Switch Trouble |
| 0599 | Dial it Services | 3 | Switch Trouble |
| 06 | Customer Action/Public Services/Customer Use Of Equipment |  |  |
| 0611 | Receiver Off Hook (ROH) | 25 | customer Operation Instructions |
| 0612 | Calling Party Hold (CPH) | 25 | customer Operation Instructions |
| 0613 | User Dialing Wrong | 25 | customer Operation Instructions |
| 0615 | Foreign or Bent Coins/Objects, Pennies | 25 | customer Operation Instructions |
| 0616 | Canadian | 25 | customer Operation Instructions |
| 0617 | Remove for Remodeling | 25 | customer Operation Instructions |
| 0618 | Can't Be Called (On Outgoing Only) | 25 | customer Operation Instructions |
| 0619 | Line Is In Use | 25 | customer Operation Instructions |
| 0690 | Service Order Activity | 9 | Information |
|  | Customer Action/All Classes Of Service/Non-Dispatched |  |  |
| 0620 | Service Order | 9 | Information |
| 0640 | Suspended or Disconnected | 9 | Information |
| 0650 | Cancel Report | 42 | Cancel Excluded |
| 0651 | Request to Cancel | 42 | Cancel Excluded |
| 0660 | Not Currently in Trouble | 9 | Information |
| 0661 | Customer Requests Information | 9 | Information |
| 07 | Test OK, Verify OK |  |  |
| 0701 | Verified OK with Customer | 26 | Tested OK, Verified OK |
| 0702 | Customer does not answer (DA) | 23 | Test OK |
| 0703 | Central Office Overload | 23 | Test OK |
| 0704 | *Broadband TOK | 23 | Test OK |
| 0710 | Operator report TOK | 23 | Test OK |
| 0720 | PRED report TOK non-dispatched | 23 | Test OK |
| 0747 | Test OK via front end close out | 23 | Test OK |
| 0751 | TOK, verified OK with Customer | 26 | Tested OK, Verified OK |
| 0752 | TOK, Customer does not answer | 23 | Test OK |
| 08 | Found OK In |  |  |
| 0810 | Test made - No Trouble Found | 27 | CO Facility Tested, Found OK |
|  | Data Base for Data Base Driven Services |  |  |
| 0880 | Other C. O. based services | 27 | CO Facility Tested, Found OK |
| 0891 | Calling Card Services | 27 | CO Facility Tested, Found OK |
| 0892 | Automatic Intercept Services | 27 | CO Facility Tested, Found OK |
| 0893 | Expanded 911 Service | 27 | CO Facility Tested, Found OK |
| 0897 | 700 Services | 27 | CO Facility Tested, Found OK |
| 0898 | Expanded 800 Service | 27 | CO Facility Tested, Found OK |
| 0899 | Dial It Service | 27 | CO Facility Tested, Found OK |
| 09 | Found OK Out |  |  |
| 0910 | Dispatched and Found OK | 13 | No Trouble Found |
| 0920 | *Broadband dispatched and found OK | 13 | No Trouble Found |
| 0950 | Unable to isolate trouble In or Out because of no access to demarc/protector | 13 | No Trouble Found |
| 0970 | Public Services Trouble reported and found OK | 13 | No Trouble Found |
| 10 | Referred Out |  |  |
| 1001 | CenturyLink Toll Cable Cut/Damaged | 29 | Referred Out to Other Department |
| 1002 | other outside CenturyLink | 29 | Referred Out to Other Department |
| 1005 | Move drop, deliver/place drop | 29 | Referred Out to Other Department |
| 1006 | Other non-network within CenturyLink | 29 | Referred Out to Other Department |
| 1015 | Fiber to Premise ( FTTP) | 29 | Referred Out to Other Department |
| 1016 | VOIP | 29 | Referred Out to Other Department |
| 11 | Non-Telco Plant |  |  |
|  | Non-CenturyLink, dispatched out |  |  |
| 1150 | Wires down, broken poles, etc., that are other than CenturyLink plant or equipment, and a dispatch was required to make this determination | 9 | Information |
|  | Non-CenturyLink, not dispatched |  |  |
| 1151 | Wires down, broken poles, etc., that are other than CenturyLink plant or equipment, and a dispatch was not required to make the determination | 9 | Information |
| 12 | Trouble Beyond The Network Interface |  |  |
| 1210 | Customer has a maintenance contract and CenturyLink does not bill | 31 | CPE customer Responsibility |
| 1211 | *Linebacker Coverage of non-standard inside wire | 31 | CPE customer Responsibility |
| 1220 | Customer has trouble beyond the NI and CenturyLink does not bill | 31 | CPE customer Responsibility |
| 1230 | Customer does not have a maintenance contract, or has only WMR, and we bill Trouble Isolation Charge (TIC). | 31 | CPE customer Responsibility |
| 1231 | Idaho non-complex customer and/or Iowa customer where CenturyLink does not bill | 31 | CPE customer Responsibility |
| 1240 | Customer does not have any maintenance contract and CenturyLink bills both TIC and Time & Materials | 31 | CPE customer Responsibility |
| 1250 | Customer does not have a maintenance contract and CenturyLink bills Trip Charge and Time & Materials | 31 | CPE customer Responsibility |
| 1260 | Carrier/End-user Trouble where CenturyLink bills TIC and possibly Time & Materials | 31 | CPE customer Responsibility |
| 13 | Miscellaneous Non-Dispatched Reports For Non-CenturyLink Trouble |  |  |
| 1310 | CPE Trouble | 31 | CPE customer Responsibility |
| 1320 | Reported by Other | 31 | CPE customer Responsibility |
| 1330 | Test Assist | 9 | Information |
| 1340 | Carrier Trouble | 8 | Interexchange Carrier |
| 1341 | Carrier/CenturyLink ISP Referral | 8 | Interexchange Carrier |
| 1350 | Carrier /ISP Trouble Report | 8 | Interexchange Carrier |
| 1370 | Customer Instructions | 25 | customer Operation Instructions |

APPENDIX L - Disposition Code to Maintenance Service Charge

| Disposition Code | Definition | MSC |
| --- | --- | --- |
| 1230 | Customer does not have a maintenance contract, or has only WMR, and CenturyLink bills Trouble Isolation Charge (TIC) | Y |
| 1240 | Customer does not have any maintenance contract and CenturyLink bills both TIC and Time & Materials | Y |
| 1250 | Customer does not have a maintenance contract and CenturyLink bills Trip Charge and Time & Materials | Y |
| 1260 | Carrier/End-user Trouble where CenturyLink bills TIC and possibly Time & Materials | Y |

APPENDIX M - Non-Applicable Trouble Types for POTS

| Trouble Type | TA Code | Extra Rules |
| --- | --- | --- |
| cutCable | 0616 |  |
| (miscellaneousTroublesGroup) |  |  |
| hiCapDown | 1001 |  |
| biPolarViolations | 1003 |  |
| frameErrorsHiCap | 1004 |  |
| outofFrame | 1005 |  |
| lossOfSync | 1006 |  |
| frameSlips | 1007 |  |
| noLoopBack | 1008 |  |
| canNotLoopbackDEMARC | 1009 |  |
| linesNeedTagging | 1011 |  |
| other | 1014 |  |
| alarm | 1015 |  |
| frameErrors | 1017 |  |
| facilityAlarm | 1018 |  |
| softwareGroupAlarm | 1019 |  |
| dChannelDown | 1020 |  |
| degadationOfT1.5 | 1021 |  |
| (dataTroubleGroup) |  |  |
| impulseNoise | 1207 |  |
| phaseJitter | 1208 |  |
| harmonicDistortion | 1209 |  |
| highDistortion | 1210 |  |
| noDataLoopback | 1211 |  |
| notPolling | 1213 |  |
| dataFramingErrors | 1214 |  |
| dropOuts | 1215 |  |
| hits | 1216 |  |
| noAnswerBack | 1217 |  |
| streamer | 1218 |  |
| outOfSpecification | 1219 |  |
| canNotRunToCSU | 1220 |  |
| canNotRunToOSU | 1221 |  |
| deadDataCircuit | 1222 |  |
| circuitInLoopback | 1223 |  |
| crossModulation | 1227 |  |
| gettingAllOnes | 1230 |  |
| slip | 1231 |  |
| stationTroubleGroup | 1300 |  |
| voiceEquipment | 1301 |  |
| dataEquipment | 1302 |  |
| videoEquipment | 1303 |  |
| otherEquipment | 1304 |  |
| stationWiring | 1305 | N/A for all states except Colorado, Minnesota, and Oregon. |
| physicalTroubleGroup | 1400 |  |
| lightBurnedOut | 1401 |  |
| dataset | 1402 |  |
| ttySet | 1403 |  |
| highSpeedPrinter | 1404 |  |
| ALI | 1406 |  |
| canNotActivatePC | 1407 |  |
| modem | 1408 |  |
| cathodeRayTube | 1409 |  |
| looseJack | 1410 | N/A for all states except Colorado, Minnesota, and Oregon. |
| OffHook | 1411 |  |
| processorDead | 1413 |  |
| NoRegister | 1416 |  |
| stuckSender | 1417 |  |
| otherStationTrouble | 1418 |  |
| (otherCaseGroup) |  |  |
| releaseCktRequestedByIC | 1507 |  |
| releaseCktRequestedByEC | 1508 |  |
| releaseFacilityRequestedByIC | 1509 |  |
| releaseFacilityRequestedByEC | 1510 |  |
| requestForRoutine | 1511 |  |
| release | 1512 |  |
| requestMonitorOfCircuit | 1514 |  |
| routineTestFailure | 1515 |  |
| lostTimeReport | 1516 |  |
| historicalReports | 1517 |  |
| switchOrTrunkRelated | 1518 |  |
| requestTestAssist | 1519 |  |
| analogTestLine | 1520 |  |
| digitalTestLine | 1521 |  |
| manualInterventionRequested | 1522 |  |
| switchedNetworkGroup | 1700 |  |
| aNITimeout | 1701 |  |
| extraDigit | 1702 |  |
| extraPulse | 1703 |  |
| falseKeyPulse | 1704 |  |
| misplacedStartPulse | 1705 |  |
| mutilatedDigitGroup | 1706 |  |
| noKeyPulse | 1707 |  |
| partialDialTimeout | 1708 |  |
| signalingNetworkFailureIncoming | 1709 |  |
| stationGroupDesignationDigitFailure | 1710 |  |
| aNI Problem | 1711 |  |
| oSPSEqualAccessSignaling | 1712 |  |
| missingANI | 1713 |  |
| vacantCodeAnnouncement | 1714 |  |
| invalidDigit | 1715 |  |
| highandWet | 1716 |  |
| payPhoneProblemsGroup | 1800 |  |
| noCoinReturn | 1801 |  |
| coinStuck | 1802 |  |
| cannotDepositCoin | 1803 |  |
| coinsFallThrough | 1804 |  |
| coinsDoNotRegister | 1805 |  |
| payPhoneDamage | 1806 |  |

APPENDIX N – Valid State/Status Combinations for Design Service

| FunctionCode | Function Message | ASNI State | ANSI Status |
| --- | --- | --- | --- |
| CAN | Cancel Trouble Ticket | 4 | 27 |
| CLD | Closed | 4 | 27 |
| CUS | Information to Customer | 1 | 34 |
| DMC | Delayed Maintenance Cancel | 1 | 17 |
| DME | Delayed Maintenance End | 1 | 17 |
| DMS | Delayed Maintenance Start | 2 | 16 |
| EBC | Electronic Bonding Confirmation | 4 | 27 |
| EBD | Electronic Bonding Deny | 2 | 16 |
| EBF | Electronic Bonding Failure | 1 | 30 |
| EBV | Electronic Bonding Verification | 3 | 26 |
| EBX | EBV timer request expired | 3 | 26 |
| HDC | Hand-off to Central Office | 1 | 3 |
| HDD | Hand-off to Dispatch | 1 | 4 |
| HDF | Hand-off to Facility | 1 | 11 |
| NAC | No Access Cancel | 1 | 15 |
| NAE | No Access Expired | 1 | 15 |
| NAS | No Access Start | 2 | 14 |
| RST | Restored | 4 | 27 |

APPENDIX O - Trouble Found Codes

| Trouble Found | ATIS 227 Code |
| --- | --- |
| pending | 0 |
| cameClear | 1 |
| centralOffice | 2 |
| switchTrouble | 3 |
| customerProvidedEquipment | 4 |
| facility | 5 |
| centralOfficeFacility | 6 |
| ICfacility | 7 |
| interexchangeCarrier | 8 |
| information | 9 |
| nonplanClassified | 10 |
| nonplanClassifiedIC | 11 |
| nonplanClassifiedEA | 12 |
| noTroubleFound | 13 |
| station | 14 |
| stationProductData | 15 |
| stationProductTerminal | 16 |
| stationProductVideo | 17 |
| stationProductVoice | 18 |
| stationWiring | 19 |
| otherStationEquipment | 20 |
| foundOKStation | 21 |
| servingBureau | 22 |
| testOK | 23 |
| publicServicesCoinSet | 24 |
| customerOperatingInstructions | 25 |
| testedOKVerifiedOK | 26 |
| coFacilityTestedFoundOK | 27 |
| outsideFacilityTestedFoundOK | 28 |
| referredOutToOtherDept | 29 |
| protectiveConnectiveArrang | 30 |
| cpeCustomerResponsibility | 31 |
| preService | 32 |
| preServiceIC | 33 |
| preServiceEA | 34 |
| serviceNode | 35 |
| data | 36 |
| customerReferredToVendor | 37 |
| exchangeAccess | 38 |
| international | 39 |
| otherProvidedAccess | 40 |
| existingReport | 41 |
| cancelExclude | 42 |

Appendix P - Non-Applicable Trouble Types for Design Service

| Trouble Type | TA Code |
| --- | --- |
| (stationTroubleGroup) |  |
| voiceEquipment | 1301 |
| dataEquipment | 1302 |
| videoEquipment | 1303 |
| otherEquipment | 1304 |
| (physicalTroubleGroup) |  |
| lightBurnedOut | 1401 |
| dataset | 1402 |
| ttySet | 1403 |
| highSpeedPrinter | 1404 |
| canNotActivatePC | 1407 |
| modem | 1408 |
| cathodeRayTube | 1409 |
| physicalProblem | 1412 |
| processorDead | 1413 |
| noRegister | 1416 |
| stuckSender | 1417 |
| otherStationTrouble | 1418 |
| (otherCaseGroup) |  |
| manualInterventionRequested | 1522 |
| recovery | 1600 |
| recoveryReport | 1601 |
| payPhoneProblemsGroup | 1800 |
| noCoinReturn | 1801 |
| coinStuck | 1802 |
| cannotDepositCoin | 1803 |
| coinsFallThrough | 1804 |
| coinsDoNotRegister | 1805 |
| payPhoneDamage | 1806 |

Appendix Q - Applicable Trouble Types for Local Number Portability (LNP)

| Trouble Type | TA Code |
| --- | --- |
| CanNotCallOut | 0201 |
| canNotCallOut2 | 0208 |
| CanNotBeCalled | 0301 |
| CanNotRaiseAStation | 0308 |
| receivesCallsForWrongNumber | 0320 |

Appendix R - Glossary/Acronyms

Acronyms either used in this document or useful for discussions about this document are listed below.

| Acronym | Definition |
| --- | --- |
| ACSE | Association Control Service Element |
| ANSI | American National Standards Institute |
| AVC | Attribute Value Change |
| BAS | Business Application Services |
| CLEC | Certified Local Exchange Carrier |
| CME | Conformant Management Entity |
| CST | Client Self Test |
| CTR | Customer Trouble Reporting |
| CUG | Closed User Group |
| DCS | Data Communications Services |
| DES CBC | Data Encryption Standard/Cipher Block Chain |
| DN | Distinguished Name |
| DTN | Digital Telephone Number |
| EB | Electronic Bonding |
| ECIC | Electronic Communications Implementation Committee |
| EFD | Event Forwarding Discriminator |
| FU | Functional Units |
| HTTP(S) | Hyper Text Transport Protocol (Secure Sockets) |
| IEC | International Electrotechnical Commission |
| ISO | International Organization for Standardization |
| ISP | International Standardized Profiles |
| LEC | Local Exchange Carrier |
| LMOS | Loop Maintenance Operations System |
| MAPDU | Management Application Protocol Data Unit |
| MLT | Mechanized Loop Test |
| MOCS | MTG Supported Transactions |
| MOI | Managed Object Instance |
| MORT | Managed Object Referring to Test |
| NM | Network Management |
| NSAP | Network Service Access Point |
| OBF | Ordering and Billing Forum |
| OID | Object Identifier |
| OIW | OSI Implementation Workshop |
| ORT | Operational Readiness Test |
| OSI | Open Systems Interconnection |
| OSS | Operations Support Systems |
| PDU | Protocol Data Unit |
| PICS | Protocol Implementation Conformance Statements |
| POI | Point of Interface |
| POP | Point of Presence |
| POTS | Plain Old Telephone Service |
| RDN | Relative Distinguished Name |
| RMA | Request for Manual Assistance |
| ROSE | Remote Operations Service Element |
| ROER | ROSE Error |
| RORJ | ROSE Error Reject |
| SAP | Service Access Point |
| SMFU | System Management Functional Unit |
| SOAP | Simple Object Access Protocol |
| SYAD | Systems Administration |
| TA | Trouble Administration |
| TACEN | Trouble Administration Configuration Event Notification |
| tML | telecommunications Markup Language |
| TMN | Telecommunications Management Network |
| TR | Telecommunications Local Trouble Report |
| TRFD | Trouble Report Format Definition |
| TSAP | Transport Service Access Point |
| TT | Trouble Ticket |
| TTR | Telecommunications Trouble Report |
| W3C | World Wide Web Consortium |
| WFA/C | Work Force Administration/Control |
| WSDL | Web Service Description Language |
| WS-I | Web Services Interoperability Organization |
| XML | Extensible Markup Language |

Appendix S - Managed Object Instance (Service ID component) formats

Sample POTS and Design Service (only unbundled loop and unbundled switch network elements) circuit formats are listed below.

POTS Formats

Telephone Number Format

3031234567

Telephone Number with Terminal Format

3031234567TER12345

Design Service Formats

Unbundled Loop Circuit Formats

24/LXFU/111111/MS (serial numbered)

24/UBFU/111111/MS

24/HCFU/111111/MS

Unbundled Switch Circuit Formats

29/SNNU/303/555/1111 (telephone numbered)

A02/T1/CLSPCOMADS0/CLSPCOMAHJ3 (carrier)

97/PH55IEKEYY/CLSPCOMAHJ3/77/CLSPCOMADS0 (message trunk)

Guide to Circuit ID Formats

The format of each type of circuit ID used in MTG is explained in the table below.

| Serial Number Format Prefix: 1-2 alphanumeric characters. This is an optional field. Service Code & Modifier: 2-4 alphabetic characters (usually 4). This is a required field. Serial Number: 1-6 digits. This is a required field. Suffix: 3 character suffix to the serial number may be required (rarely used). CO (Company) Code: 2-4 alphabetic characters (usually NW, MS, or PN). This is a required field. Segment: 1-3 alphanumeric characters. optional for non-multi-point circuits. multi-point segments map to Circuit End Location, e.g. CLK1 = A, CLK2 = B A Billing Telephone Number (BTN) cannot be used for opening a Trouble Report. The Serial Number Circuit Format must be used. | Telephone Number Format Prefix: alphanumeric characters. required if it exists (not all telephone number circuits have a prefix) Service Code & Modifier: 2-4 alphabetic characters (usually 4); This is a required field when specifying a non-DSL telephone numbered circuit. NPA: 3 digits. This is a required field. NXX: 3 digits. This is a required field. Line: 4 digits. This is a required field. Extension: 1-5 alphanumeric characters. This is an optional field. For states: AZ, CO, ID, MT, NM, UT, WY, alphas not accepted; convert D1 to 0001, D2 to 0002, etc. Segment: 1-3 alphanumeric characters. This is an optional field. rarely used |
| --- | --- |
| Carrier Facility Format Channel Group Number: 1-5 alphanumeric characters. This is a required field. Facility Type: 1-6 alphanumeric characters. This is a required field. Examples: T1, T1F, T1U, T1UZF, T1Z, T1ZF, T3 A CLLI Code: 8 or 11 alphanumeric characters. This is a required field. Z CLLI Code: 8 or 11 alphanumeric characters. This is a required field. All 4 of the above components are required | Message Trunk Format Trunk Number: 1-4 alphanumeric characters. This is a required field. Traffic Class: 1-2 alphanumeric characters. This is a required field. A hyphen may be allowed Office Class: 1-2 alphanumeric characters. This is a required field. A hyphen may be allowed A separator is not used between the Traffic Class and Office Class Traffic Use Code: 2 alphanumeric characters. This is a required field. A hyphen may be allowed. No separator between Office class and Traffic Use Code Traffic Modifier: 1-7 alphanumeric characters. This is an optional field. No separator between Traffic Use Code and Traffic Modifier A CLLI Code: 8 or 11 alphanumeric characters. This is a required field. Pulse & Direction: 2 alphanumeric characters. This is a required field. Z CLLI Code: 8 or 11 alphanumeric characters. This is a required field. |

Appendix T - Client Self Test (CST) Response codes

Detailed information about Client Self Test transactions response Summary Codes

## Full Test Responses

| Test Expert Results | Summary Code | Text Response |
| --- | --- | --- |
| No test access available | NTA | No test access available – Please open a ticket. |
| DS1 PM’s clean | CLN | DS1 PM’s Clean |
| Test OK | TOK | No trouble found on the circuit |
| Errors in CenturyLink Network (line) | ERL | Errors in the CenturyLink network – Please open a ticket |
| Errors Not Isolated (path) | ERP | Errors detected, not isolated – Please review before opening a ticket |
| HDSL errors detected | TQF | Trouble Found in CenturyLink network field – Please open a ticket. |
| Trouble to the office repeater | TQO | Trouble Found in CenturyLink network office - Please open a ticket |
| Inconclusive results | INC | Unspecified failure took place – Please open a ticket |
| Errors to NIU or Field devices | TQF | Trouble Found in CenturyLink network – NIU or Repeaters – Please open a ticket |
| CPE | CPE | Clean to NIU, taking errors to the CSU – Please contact your end user and isolate trouble further |
| Alarm Red | ALR | RED ALARM detected. No further trouble found. |
| Alarm Yellow | ALY | YELLOW ALARM detected. No further trouble found. |
| OOS, CenturyLink network TOK | QOK | Circuit is out of service or taking errors, CenturyLink network and equipment is test OK – Further isolation needed outside of CenturyLink |

## Loop Back Responses

| Test Expert Results | Summary Code | Text Response |
| --- | --- | --- |
| No test access available | NTA | No test access available - Please open a ticket. |
| Loop Up | CMP | Test completed successfully |
| Inconclusive results | INC | Unspecified failure took place – Please open a ticket |

## Supplemental Intrusive Responses

| Test Expert Results | Summary Code | Text Response |
| --- | --- | --- |
| No test access available | NTA | No test access available - Please open a ticket. |
| Test OK | TOK | No trouble found on the circuit |
| HDSL errors detected | TQF | Trouble Found in CenturyLink network field - Please open a ticket. |
| Trouble to the office repeater | TQO | Trouble Found in CenturyLink network office - Please open a ticket. |
| Inconclusive results | INC | Unspecified failure took place – Please open a ticket |
| Errors to NIU or Field devices | TQF | Trouble Found in CenturyLink network – NIU or Repeaters – Please open a ticket |
| CPE | CPE | Clean to NIU, taking errors to the CSU – Please contact your end user and isolate trouble further |

## Non-Intrusive Responses

| Test Expert Results | Summary Code | Text Response |
| --- | --- | --- |
| No test access available | NTA | No test access available - Please open a ticket. |
| DS1 PM’s clean | CLN | DS1 PM’s Clean |
| Errors in CenturyLink Network (line) | ERL | Errors in the CenturyLink network – Please open a ticket |
| Errors Not Isolated (path) | ERP | Errors detected, not isolated – Please review before opening a ticket |
| Inconclusive results | INC | Unspecified failure took place – Please open a ticket |
| Alarm Red | ALR | RED ALARM detected. No further trouble found. |
| Alarm Yellow | ALY | YELLOW ALARM detected. No further trouble found. |

Appendix U – MTG Supported Transactions – CST

Detailed information about Client Self Test transactions that are supported in Maintenance Ticketing Gateway (MTG) can be found in the ‘MTG Supported Transactions – Client Self Test’ document located at http://www.centurylink.com/wholesale/systems/mtg.html

# Text boxes

RequestTroubleReportCreationRequest

Receive and acknowledge request.

Submit Create Ticket request.

CenturyLink processing.

Receive Create Ticket notification.

Submit Create Ticket notification.

RequestTroubleReportCreationResponse

ACK/NACK (HTTP Response Message)

ACK/NACK (HTTP Response Message)

Receive and acknowledge request.

Submit Retrieve Ticket request.

CenturyLink processing.

Receive Retrieve Ticket notification.

Submit Retrieve Ticket notification.

RetrieveAttributesByTroubleReportIdResponse

ACK/NACK (HTTP Response Message)

RetrieveAttributesByTroubleReportIdRequest

ACK/NACK (HTTP Response Message)

Receive and acknowledge request.

Submit Update Ticket request.

CenturyLink processing.

Receive Update Ticket notification.

Submit Update Ticket notification.

ACK/NACK (HTTP Response Message)

ModifyAttributesResponse

ModifyAttributesRequest

ACK/NACK (HTTP Response Message)

Receive and acknowledge request.

Submit Update Ticket request.

CenturyLink processing.

Receive Update Ticket notification.

Submit Update Ticket notification.

ACK/NACK (HTTP Response Message)

ModifyAttributesResponse

ModifyAttributesRequest

ACK/NACK (HTTP Response Message)

Submit Update Ticket (status / log notes update) notification.

Receive Update Ticket (priority / log notes update) notification.

ACK/NACK (HTTP Response Message)

AttributeValueChangeNotification

Receive Cleared Ticket notification.

AttributeValueChangeNotification

Receive Closed Ticket notification.

Submit Closed Ticket notification.

AttributeValueChangeNotification

Cleared state (3), status (25), status time, additional trouble status info.

Closed state (4), status (27), status time, close out narrative, trouble found, maintenance service charge, outage duration, restored time.

Submit Cleared Ticket notification.

ACK/NACK (HTTP Response Message)

ACK/NACK (HTTP Response Message)

Receive Cleared Ticket notification.

Submit verification of issue resolution

AttributeValueChangeNotification

VerifyRepairCompletionRequest

Process request

Receive verification response

VerifyRepairCompletionResponse

Submit verification response

Receive Closed Ticket notification.

Submit Closed Ticket notification.

AttributeValueChangeNotification

After 24 hours of no response, no dispute, or immediately upon acceptance, the ticket may be closed.

Cleared state (3), status (26), status time, activity duration, close out narrative, trouble found, maintenance service charge, and outage duration, restored time.

Closed state (4), status (27), status time, additional trouble status info.

Submit Cleared Ticket notification.

ACK/NACK (HTTP Response Message)

ACK/NACK (HTTP Response Message)

ACK/NACK (HTTP Response Message)

ACK/NACK (HTTP Response Message)

CancelTroubleReportRequest

Receive and acknowledge request.

Submit Cancel Ticket request.

ACK/NACK (HTTP Response Message)

CenturyLink processing.

Receive Cancel Ticket notification.

Submit Cancel Ticket notification.

ACK/NACK (HTTP Response Message)

CancelTroubleReportResponse

Receive MLT Result.

Submit MLT request.

CenturyLink processing.

Receive MLT notification.

Submit MLT Test Request.

ACK/NACK (HTTP Response Message)

POTSUncontrolledTestResponse

POTSUncontrolledTestRequest

ACK/NACK (HTTP Response Message)

Submit CST request.

Receive CST notification.

Receive CST Result.

CenturyLink processing.

Submit CST Request.

ClientSelfTestRequest

ACK/NACK (HTTP Response Message)

ACK/NACK (HTTP Response) Message)

ClientSelfTestResponse