CONTENTS

Chapter and Section	Page

3.	Network Channel and Network Channel Interface Specifications	3-1

3.1	General	3-1

3.2	Network Channel (NC) Code Function	3-1

3.3	NC Code Components and Format	3-1

3.4	Unbundled Loop NC Codes	3-2

3.4.1	Unbundled Voiceband Loop NC Codes	3-2

3.4.2	Unbundled Digital Loop NC Codes	3-2

3.4.3	Unbundled xDSL Capable Loop NC Codes	3-4

3.5	Network Channel Interface (NCI) Code Function	3-6

3.6	NCI Code Components and Format	3-6

3.6.1	NCI Format	3-6

3.6.2	Example	3-9

3.7	Unbundled Loop Available NCI Codes	3-9

3.7.1	Available Voiceband Loop - NCI Codes	3-10

3.7.2	Available Digital Loop - Electrical NCI Codes	3-11

3.7.3	Available xDSL Capable and Advanced Digital Transport

Loop - NCI Codes	3-13

3.8	Compatible NC and NCI Code Combinations	3-14

3.8.1	Unbundled Voiceband Loop NC/NCI Codes	3-14

3.8.2	Unbundled Digital Loop NC/NCI Codes	3-15

3.8.3	Unbundled xDSL Capable Loop NC/NCI Codes	3-18

CONTENTS (Continued)

Tables	Page

3-1	Available CenturyLink Voiceband Loop NC Codes	3-2

3-2	Available CenturyLink Digital Loop NC Codes	3-4

3-3	Available CenturyLink Digital Data Service (DDS) Loop NC Codes

up to and including 64 kbit/s	3-5

3-4	Available CenturyLink Unbundled xDSL Capable Loop NC

Codes	3-6

3-5	NCI Impedance Values	3-8

3-6	Voiceband Loop NCI Protocol and Protocol Option Codes	3-10

3-7	Digital Loop Electrical NCI Protocol and Protocol Option Codes	3-11

3-8	CenturyLink xDSL and Advanced Digital Transport NCI Protocol and

Protocol Option Codes	3-13

3-9	CenturyLink Unbundled Voiceband Loop NC/NCI Code Combinations	3-15

3-10	CenturyLink Digital Channel Unbundled Loop NC/NCI Code

Combinations	3-16

3-11	Point-to-Point Digital Loop, DDS NC and NCI Code Combinations	3-18

3-12	CenturyLink Unbundled xDSL Capable Loop NC/NCI Code Combinations	3-19

Figures

3-1	Format Structure for NC Codes	3-1

3-2	Format Structure for NCI Codes	3-8

3-3	NCI Code Components	3-9

# 3.	Network Channel and Network Channel Interface Specifications

## 3.1	General

Network Channel (NC) codes describe, in standard format, the characteristics of the service transmission path.  Network Channel Interface (NCI) codes provide the means to define the physical and electrical characteristics at the handoff or termination of a channel . The ANSI standard document ATIS- 0300223.2009 describes these coding schemes. As technologies and industry standards change over time NC/NCI/SEC NCI may be added or revised and will be available to the CLEC.

## 3.2	Network Channel (NC) Code Function

Service considerations are encoded into NC codes.  The Carrier or End-User specifies the NC Code to advise CenturyLink of the required service connection of the transmission path and of any applicable Central Office (CO) functions.

## 3.3	NC Code Components and Format

An NC code is a four-character code with two data elements:

- Channel Code

- Optional Feature Code

Figure 3-1 illustrates NC code format.

| Network Channel Code |
| --- |
| Data Element | Channel Code | Optional Feature Code |
| Character Position | 1 | 2 | 3 | 4 |
| Character Key | X | X | X or - | X or - |
| X = Alphanumeric - = Hyphen |

Figure 3-1 Format Structure for NC Codes

The Channel Code (character positions 1 and 2) is a two character alpha or alphanumeric code that describes the channel service in an abbreviated form.  The channel code will frequently, but not always, be the service code of special service circuits or the transmission grade of message trunk circuits.  The NC channel code field is always filled.

The Optional Feature Code (character positions 3 and 4) is a two character alpha or alphanumeric or hyphen code that represents the option codes available for each channel code.  Varying combinations of this code will allow the customer to enhance the technical performance of the requested channel, or to further identify the type of service.  It can also specify options such as data conditioning, bridging, etc.  The NC optional code field is always filled.

## 3.4	Unbundled Loop NC Codes

### 3.4.1	Unbundled Voiceband Loop NC Codes

For Unbundled Voiceband Loops, the first two characters are LX.  The third and fourth characters are hyphens to denote no additional service features.

Table 3-1 contains the available CenturyLink NC codes for Unbundled Voiceband Loops.

Table 3-1 Available CenturyLink Voiceband Loop NC Codes

| Network Channel Code | Point-to-Point Analog Loop Description |
| --- | --- |
| Analog Loop |
| LX-- | Dedicated Facility (without equipment) |

The term “without equipment” indicates only that electronics for circuit conditioning or basic functionality are not normally required at either the Central Office or End User Interfaces as part of this service.  It does not eliminate the use of derived facilities such as subscriber loop carrier in providing this Unbundled Loop service.

### 3.4.2	Unbundled Digital Loop NC Codes

For Unbundled Digital Loops, the first two characters indicate the requested family of digital services.  The third and fourth characters provide further service features as needed.  For readability, there are two tables of NC Codes.  The first table lists those Digital Loops above the 64 kbit/s level.  The second table lists Digital Loops up to and including the 64 kbit/s level.

Table 3-2 contains the available NC codes for Unbundled Digital Loops 
of 160 kbit/s and above.

Table 3-2 Available CenturyLink Digital Loop NC Codes

| Network Channel Code | Point-to-Point Digital Loop Description |
| --- | --- |
| 160 kbit/s Digital Subscriber Line (DSL) |
| AD-- | Digital Subscriber Line (DSL), nominally 160 kbit/s (144 kbit/s, 2B+D channelized payload) per TR-NWT-000393 |
| ADU- | Digital Subscriber Line (DSL), nominally 160 kbit/s (144 kbit/s, un-channelized payload). Assured payload bit integrity, per TR-NWT-000397 |
| Digital Signal Level 1 (1.544 Mbit/s) |
| HC-- | SF Format PER TR-NPL-000342, AMI |
| HCD- | ANSI ESF, AMI |
| HCE- | ANSI ESF, B8ZS |
| HCF- | NON-ANSI ESF, AMI, |
| HCG- | NON-ANSI ESF, B8ZS |
| HCJ- | FREE FRAMING AND B8ZS |
| HCZ- | SF Format PER TR-NPL-000342, B8ZS |
| Digital Signal Level 3 (44.736 Mbit/s) |
| HF-- | DS3 M- frame structured signal. Unchannelized per ANSI T1.107-1995 |
| HFC- | DS3 M- frame structured signal and C-Bit Parity application. Unchannelized per ANSI T1.107-1995. |

Table 3-3 contains the available NC codes for Unbundled Digital Loops up to and including 64 kbit/s.

Table 3-3 Available CenturyLink NC Codes for Digital Data Service (DDS) Loop up to and including 64 kbit/s

| Network Channel Code | Point-to-Point Digital Data Service Transmission Path Description |
| --- | --- |
| Digital Data Service Transmission Path |
| LX-N | Digital Data Service Transmission Path SVC DA1, 2.4 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA1,with secondary channel, 2.4 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA2, 4.8 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA2,with secondary channel, 4.8 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA3, 9.6 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA3,with secondary channel, 9.6 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA5, 19.2 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA5,with secondary channel, 19.2 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA4, 56 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA4,with secondary channel, 56 kbit/s |
| LX-N | Digital Data Service Transmission Path SVC DA6, 64 kbit/s |

### 3.4.3	Unbundled xDSL Capable Loop NC Codes

For Unbundled xDSL Capable Loop the first two characters indicate the requested family of services.  The third and fourth characters provide further service features as needed.

The following table contains available CenturyLink NC codes for Unbundled xDSL Capable Loops.

Table 3-4 Available CenturyLink Unbundled xDSL Capable Loop NC Codes

| Network Channel Code | Point-to-Point xDSL Capable Description |
| --- | --- |
| xDSL Capable Loop |
| LX-N | Dedicated Facility (without equipment), Copper portion of facility contains no loading coils |
| LXR- | Dedicated Facility (without equipment), Copper portion of facility contains no loading coils and conforms to Revised Resistance Design (RRD) Engineering Rules. |

.   The customer specifies the NCI codes to communicate to CenturyLink the character of the signals the customer is connecting to the network at each end-point of the copper circuit.  CenturyLink will take into account the NC code and the NCI code when assigning, maintaining and repairing facilities for xDSL. The associated NC codes require that the service use copper facilities free of  load coils.  Those facilities shall be free of faults, such as opens, grounds, shorts and foreign volts.  The loops will also be conditioned when requested by the CLEC.  CenturyLink has responsibilities to provision the best available loop. 3.5	NCI Code Function

The NCI code is an encoded representation used to identify five interface elements located at a Point Of Termination (POT) at the CO or at the EU’s location.  The interface elements are physical conductors, protocol, impedance, protocol options and Transmission Level Points (TLPs).  Only the first four components are used for Unbundled Loop service.

## 3.6	NCI Code Components and Format

Technical specifications for an interface are encoded into NCI codes.  An NCI code tells a CenturyLink engineer and the circuit design system, of specific technical, customer requirements at a Network Interface.

This section gives a brief description of the NCI code format.  Specific technical information about the NCI codes may be found in the appropriate technical publication.  Some additional information may be found later in this document in the chapters describing the specific unbundled network element.

### 3.6.1	NCI Format

An NCI code is a maximum twelve-character code that consists of five (5) data elements:

Total Conductors
Protocol
Impedance
Protocol Options
Transmission Level Point(s) (TLP)

For xDSL Capable Loops, the first four data elements are required. For other Unbundled Loops, the first three data elements are required.  The last two are generally optional but may be required in certain situations.  Only the first four components are used for Unbundled Loops.  The format is illustrated in Figures 3-2 and 3-3.

Total Conductors (character positions 1 and 2) is a two-character numeric code that represents the total number of physical conductors (e.g., wires or fibers) required at the interface.

Protocol (character position 3 and 4) is a two-character alpha code that defines requirements for the interface regarding signaling/transmission.

Impedance (character position 5) is a one-character alpha or numeric code representing the nominal reference impedance, presented toward the network, that will terminate the transmission path for the purpose of evaluating transmission performance.  Values are listed in Table 3-6

| Network Channel Interface Code |
| --- |
| Total Conductors | Protocol | I | D | Protocol Options | D | TLP Level |
|  |  | m p e d a n c e | e l i m e t e r |  | e l i m i t e r | T r a n s m i t | R e c e i v e |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| N | N | A | A | X | • | X | X | X | • | X or - | X or - |
| A = Alpha N = Numeric X = Alphanumeric • = Delimiter (normally a period) - = Hyphen |

Figure 3-2  Format Structure for NCI Codes

Table 3-5  NCI Impedance Values

| Impedance in Ohms (Character Position 5) |
| --- |
| Data Value | Code | Data Value | Code |
| 110 | 0 | 124 | 7 |
| 150 | 1 | Variable | 8 |
| 600 | 2 | 100 | 9 |
| 900 | 3 * | Fiber | F |
| 1200 | 4 | Radio | Z |
| 135 | 5 | 50 Coaxial | C |
| 75 | 6 | Multi-Impedance | M |
| * Except for interface code 04DD3, the impedance character 3, when used with a 4-wire voice-frequency path at the POT, denotes a historical customer (Interexchange Carrier) provided transmission termination rather than a 900 ohm impedance. Such terminations were provided by customers in accordance with FCC Docket No. 20099 settlement Agreement and by Automatic Transmission Test and Control Circuit used in the previous provisioning process. |

Protocol Options (character positions 7, 8, and 9) is a one to three character alpha, numeric, or alphanumeric code that describes additional features (e.g., bit rate or bandwidth) on the Protocol to be used.  It is an conditional data element (based on the loop type) that is always left justified.

Transmission Level Point(s) (character positions 8 through 12) is assigned one or two-character alpha code corresponding to a value for Transmission Level Point(s) (TLPs) from either the Exchange Carrier/service provider or customer end.  This NCI function does not apply to Unbundled Loop transport.

### 3.6.2	Example

A compatible NCI code for the NC code LX-- is 02QC3.OOD.  The “02” indicates that there are two (2) conductors (copper wires in this case).  The “QC” describes the interface as "Manual Cross-Connect DS0/Voice Termination" (See reference publications for further information).  The impedance value of “3” indicates 900 ohms (Table 3-5).  The option codes “OOD” Loop Start, Loop Signaling, Open End.  Detailed description of the functions at the interface are as described in reference publications, particularly Telcordia's GR-334-CORE.

Figure 3-3  NCI Code Components

## Unbundled Loop Available NCI Codes

This Section provides the available CenturyLink NCI Codes to use when establishing an Unbundled Loop.

3.7.1	Available CenturyLink Voiceband Loop - NCI Codes

Table 3-6  CenturyLink Voiceband Loop NCI Protocol and Protocol Option Codes

| Protocol |  |
| --- | --- |
| Code | Option | Definition * |
| 3 4 | 7 8 9 |  |
| QC |  | Central Office Manual Cross-Connect DS0/Voice Termination |
|  | OOB | Ground Start Loop Signaling, open end |
|  | OOD | Loop Start Loop Signaling, open end |
|  | OOF | Transmission only, no signaling |
|  | RVO | Reverse Battery Originating: Loop closure provided by the Access Customer (AC) to the Access Provider (AP); Battery provided by AP to AC. * |
|  | RVT | Reverse Battery Terminating: Loop closure provided by the AP to the AC; Battery Provided by AC to AP. * |
| GO |  | Ground-start signaling -- open end (switch) function presented by Access Customer at interface to CenturyLink Access Service. |
| GS |  | Ground-start signaling -- closed end (station) function presented by Access Customer or End-user at interface to CenturyLink Access Service. |
| LO |  | Loop-start loop signaling -- open end (switch) function presented by customer at interface to CenturyLink Access Service. |
| LS |  | Loop-start signaling -- closed end (station) function presented by the customer at the interface to CenturyLink access service. |
| NO |  | Connects customer to an Access Service suitable for voice transmission with no signaling provided by CenturyLink |
| RV |  | Reverse battery (Trunk signaling) at interface |
|  | O | Loop closure provided by Access Customer to CenturyLink; Battery provided by CenturyLink to Access Customer |
|  | T | Loop closure provided by CenturyLink to End-User; Battery provided by End-User to CenturyLink |
| * The standard definitions defined in the reference documents should be modified to fit the Unbundled application. For example, the term “Interconnector” or "Alternate Exchange Carrier" should be substituted for “IC-POT” or “IC” in the standard definitions. The Access Provider (AP) is CenturyLink. The Access Customer (AC) is the carrier (or their customer). |

### 3.7.2 Available CenturyLink Digital Loop - Electrical NCI Codes

Table 3-7 CenturyLink Digital Loop Electrical NCI Protocol and Protocol Option Codes

| Protocol |  |
| --- | --- |
| Code | Option | Definition |
| 3 4 | 7 8 9 |  |
| QB |  | Central Office Manual Cross-Connect Termination with No Subrating Capability |
|  | 00 | MDF Cross-Connect |
|  | 11 | DS1 to DS1, This code may or may not meet DS1 Signal Levels as specified by ANSI T1.102-1999 |
|  | 33 | DS3 to DS3, This code may or may not meet DS3 Signal Levels as specified by ANSI T1.102-1999 |
|  | LL | Fiber Cross-Connect on Fiber Distribution Bay |
| QC |  | Central Office Manual Cross-Connect Termination DS0/Voice Termination |
|  | OOS | Basic Rate ISDN, LT Function Presented to Service Provider |
|  | OOV | Basic Rate ISDN, NT Function Presented to Service Provider |
| DS |  | Digital Hierarchy Interface |
|  | 44A | 44.736 Mbit/s, DS3 M-frame structured signal with C-bit Parity application. It is an unchannelized signal application, supporting a user payload of 44.210 Mbit/s per ANSI T1.107-1995. |
|  | 44R | 44.736 Mbit/s, DS3 M-frame structured signal. It is an unchannelized signal application, supporting a user payload of 44.210 Mbit/s per ANSI T1.107-1995. |
| DU |  | End User Digital Access Interface |
|  | 1KN | 1,544 Mbit/s, ANSI Extended Super Frame (ESF), Alternate Mark Inversion (AMI), without Line Power. |
|  | 1KX | 1,544 Mbit/s, ANSI Extended Super Frame (ESF), Alternate Mark Inversion (AMI), without Line Power, DSX-1 Interface. |
|  | 1SN | 1,544 Mbit/s, ANSI ESF, Binary 8-Zero Substitution (B8ZS), without Line Power |
|  | 1SX | 1,544 Mbit/s, ANSI ESF, Binary 8-Zero Substitution (B8ZS), without Line Power, DSX-1 Interface. |
|  | AN | 1,544 Mbit/s, Free Framing, B8ZS, without Line Power. |
|  | AX | 1,544 Mbit/s, Free Framing, B8ZS, without Line Power, DSX-1 Interface. |
|  | BN | 1,544 Mbit/s, Super Frame (SF) Format per GR-54-CORE, AMI, without Line Power. |
|  | BX | 1,544 Mbit/s, Super Frame (SF) Format per GR-54-CORE, AMI, without Line Power, DSX-1 Interface. |
|  | CN | 1,544 Mbit/s, Non-ANSI ESF, AMI, without Line Power. |
|  | CX | 1,544 Mbit/s, Non-ANSI ESF, AMI, without Line Power, DSX-1 Interface. |

Table 3-7 CenturyLink Digital Loop Electrical NCI Protocol and Protocol Option Codes (Continued)

| Protocol |  |
| --- | --- |
| Code | Option | Definition |
| 3 4 | 7 8 9 |  |
|  | DN | 1,544 Mbit/s, SF, B8ZS, without Line Power. |
|  | DX | 1,544 Mbit/s, SF, B8ZS, without Line Power, DSX-1 Interface. |
|  | SN | 1,544 Mbit/s, Non-ANSI ESF, B8ZS, without Line Power. |
|  | SX | 1,544 Mbit/s, Non-ANSI ESF, B8ZS, without Line Power, DSX-1 Interface. |
| IS |  | 2B1Q Signaling Format - U interface per ANSI T1.601, e.g., Basic Rate ISDN, Digital Subscriber Line (DSL) |
|  | L | Basic Rate ISDN, Customer Provides LT Function Presented to Service Provider |
|  | N | Basic Rate ISDN, Customer Provides NT Function Presented to Service Provider |

DS1 Capable Loops are provided to Carrier's and to End-User's (EU's) premises.  The Network Interface (NI) at a Carrier premises will be at the end of a DSX-1 jumper wire or cable with signal characteristics described in Technical Publication 77375.

The NI at an EU customer premises may be either a DSX-1 interface or a conventional interface. Signal characteristics, limitations, and the physical means of connection at the NI for each interface are described in Technical Publication 77375. Conventional interfaces use one of the Registration Jacks described by the three Universal Service Ordering Codes (USOC) RJ48C, RJ48M and RJ48H.  End-User, DSX-1 interfaces are available where the end user’s premises is served by an on-site, optic terminal.  In those situations, conventional interfaces are not available.

Additional information on the physical DS1 and DSX-1 NI configurations may be found in Technical Publication 77375.

### 3.7.3	Available CenturyLink xDSL Capable and Advanced Digital Transport Loop - NCI Codes

The CenturyLink xDSL and Advanced Digital Transport NCI codes listed below are available.

Table 3-8  Available CenturyLink xDSL and Advanced Digital Transport NCI Protocol and 
Protocol Option Codes

| Protocol |  |
| --- | --- |
| Code | Option | Definition |
| 3 4 | 7 8 9 |  |
| DU |  | Digital Access Interface |
|  | 00F | HDSL4, Technology Specific, Transmission System Per ANSI Standard T1.417 |
|  | 00G | G.shdsl, Technology Specific, Transmission System Per ANSI Standard T1.417 |
|  | 00S | 2B1Q SDSL, Technology Specific, Transmission System Per ANSI Standard T1.417 |
|  | 001 | Spectrum Management Class 1, Per ANSI Standard T1.417 |
|  | 002 | Spectrum Management Class 2, Per ANSI Standard T1.417 |
|  | 003 | Spectrum Management Class 3, Per ANSI Standard T1.417 |
|  | 004 | Spectrum Management Class 4, Per ANSI Standard T1.417 |
|  | 005 | Spectrum Management Class 5, Per ANSI Standard T1.417 |
|  | 006 | Spectrum Management Class 6, Per ANSI Standard T1.417 |
|  | 007 | Spectrum Management Class 7, Per ANSI Standard T1.417 |
|  | 008 | Spectrum Management Class 8, Per ANSI Standard T1.417 |
|  | 009 | Spectrum Management Class 9, Per ANSI Standard T1.417 |

Table 3-8  Available CenturyLink xDSL and Advanced Digital Transport NCI Protocol and 
Protocol Option Codes (Continued)

| Protocol |  |
| --- | --- |
| Code | Option | Definition |
| 3 4 | 7 8 9 |  |
| DU |  | Digital Access Interface |
|  | 00A | ADSL Using Discrete Multi-Tone (DMT) Format, per ANSI T1.413 |
|  | 01A | One POTS Transmission Path and ADSL Using Discrete Multi-Tone (DMT) Format, per ANSI T1.413 |
|  | 00C | ADSL Using Carrierless Amplitude Phase Modulation (CAP) Format, per ANSI T1.413 |
|  | 01C | One POTS Transmission Path and ADSL Using Carrierless Amplitude Phase Modulation (CAP) Format, per ANSI T1.413 |
|  | 00H | High-Bit-Rate Digital Subscriber Line (HDSL) per ANSI T1.E1 Report Number 28 |
| IS |  | 2B1Q Signaling Format - U interface per ANSI T1.601, e.g., Basic Rate ISDN, Digital Subscriber Line (DSL) |
|  | N | Basic Rate ISDN, Customer Provides NT Function Presented to Service Provider |
| QB |  | Central Office Manual Cross-Connect Termination with No Subrating Capability |
|  | 00F | HDSL4, Technology Specific, Transmission System Per ANSI Standard T1.417 |
|  | 00G | G.shdsl, Technology Specific, Transmission System Per ANSI Standard T1.417 |
|  | 00S | 2B1Q SDSL, Technology Specific, Transmission System Per ANSI Standard T1.417 |
|  | 001 | Spectrum Management Class 1, Per ANSI Standard T1.417 |
|  | 002 | Spectrum Management Class 2, Per ANSI Standard T1.417 |
|  | 003 | Spectrum Management Class 3, Per ANSI Standard T1.417 |
|  | 004 | Spectrum Management Class 4, Per ANSI Standard T1.417 |
|  | 005 | Spectrum Management Class 5, Per ANSI Standard T1.417 |
|  | 006 | Spectrum Management Class 6, Per ANSI Standard T1.417 |
|  | 007 | Spectrum Management Class 7, Per ANSI Standard T1.417 |
|  | 008 | Spectrum Management Class 8, Per ANSI Standard T1.417 |
|  | 009 | Spectrum Management Class 9, Per ANSI Standard T1.417 |
|  | 00A | ADSL Using Discrete Multi-Tone (DMT) Format, per ANSI T1.413 |
|  | 01A | One POTS Transmission Path and ADSL Using Discrete Multi-Tone (DMT) Format, per ANSI T1.413 |
|  | 00C | ADSL Using Carrierless Amplitude Phase Modulation (CAP) Format, per ANSI T1.413 |
|  | 01C | One POTS Transmission Path and ADSL Using Carrierless Amplitude Phase Modulation (CAP) Format, per ANSI T1.413 |
|  | 00H | High-Bit-Rate Digital Subscriber Line (HDSL) per ANSI T1.E1 Report Number 28 |
| QC |  | Central Office Manual Cross-Connect Termination DS0/Voice Termination |
|  | OOS | Basic Rate ISDN, LT Function Presented to Service Provider |

## 3.8	Compatible NC and NCI Code Combinations

This section provides CenturyLink code combinations used to order Unbundled Loop interfaces and services of the following types:

- Unbundled Voiceband Loops

- Unbundled Digital Loops

- Unbundled xDSL Capable Loops including Advanced Digital Transport Loops

### 3.8.1	Unbundled Voiceband Loop NC/NCI Codes

The following table shows the currently available NC/NCI code combinations for CenturyLink Unbundled Voiceband Loop.

Table 3-9  CenturyLink Unbundled Voiceband Loops NC/NCI Code Combinations

|  | NCI Code |  |
| --- | --- | --- |
| NC Code | CenturyLink CO-NI | End-User EU-NI | Description |
|  | Voiceband LOOPS |
| LX-- | 02QC3.OOD | 02LS2 | Loop Start (LS) Signaling: Open End (LO) at CO |
| LX-- | 02QC3.OOB | 02GS2 | Ground Start(GS) Signaling: Open End (GO) at CO |
| LX-- | 02QC3.RVT | 02RV2.O | Reverse Battery(RV): Loop closure provided by the End User |
| LX-- | 02QC3.RVO | 02RV2.T | Reverse Battery(RV): Reverse Battery provided by the End User |
| LX-- | 02QC2.OOF | 02NO2 | No Signaling: Transmission Only (NO) |
| LX-- | 04QC2.OOF | 04NO2 | No Signaling: Transmission Only (NO) |

### 3.8.2	Unbundled Digital Loop NC/NCI Codes

Table 3-10 lists CenturyLink NC/NCI Code combinations for Unbundled Digital Loops

Table 3-10 CenturyLink Unbundled Digital Loop NC/NCI Code Combinations

|  | NCI Code |  |
| --- | --- | --- |
| NC Code | CenturyLink CO-NI | End-User EU-NI | Description |
| ISDN BRI/xDSL-I 160 kbit/s Digital Subscriber Line (DSL) |
| AD-- | 02QC5.OOS | 02IS5.N | Digital subscriber Line with 2B1Q Signaling Format, NT function at EU |
| AD-- | 02QC5.OOV | 02IS5.L | Digital subscriber Line with 2B1Q Signaling Format, LT function at EU |
| ADU- | 02QC5.OOS | 02IS5.N | xDSL-I, 2B1Q Signaling Format, NT function at EU |
| ADU- | 02QC5.OOV | 02IS5.L | xDSL-I, 2B1Q Signaling Format, LT function at EU |
| Unbundled DS1 Capable loop (also see 77200 & 77375) |
| HC-- | 04QB9.11 | 04DU9.BN 04DU9.BX | SF Format PER TR-NPL-000342, AMI |
| HCD- | 04QB9.11 | 04DU9.1KN 04DU9.1KX | ANSI ESF, AMI |
| HCE- | 04QB9.11 | 04DU9.1SN 04DU9.1SX | ANSI ESF, B8ZS |
| HCF- | 04QB9.11 | 04DU9.CN 04DU9.CX | Non-ANSI ESF, AMI |
| HCG- | 04QB9.11 | 04DU9.SN 04DU9.SX | Non-ANSI ESF, B8ZS |
| HCJ- | 04QB9.11 | 04DU9.AN 04DU9.AX | Free Framing, B8ZS |
| HCZ- | 04QB9.11 | 04DU9.DN 04DU9.DX | SF, B8ZS |

Table 3-10 CenturyLink Digital Loop NC/NCI Code Combinations (Continued)

|  | NCI Code |  |
| --- | --- | --- |
| NC Code | CenturyLink CO-NI | End-User EU-NI | Description |
| unbundled DS3 capable loop (also see 77324) |
| HF-- | 04QB6.33 | 04DS6.44R | DS3 M-frame structured signal. It is an unchannelized signal application. |
| HFC- | 04QB6.33 | 04DS6.44A | DS3 M-frame structured signal with C-bit Parity application. It is an unchannelized signal application. |

The following table shows the currently available NC/NCI code combinations for Digital Data Service.

Table 3-11  CenturyLink Point-to-Point Digital Loop, DDS NC and NCI Code Combinations

|  | NCI Code |  |
| --- | --- | --- |
| NC Code | CenturyLink CO-NI | End-User EU-NI | Description: Application of CenturyLink’s Unbundled loop |
|  | Digital Data service transport |
| LX-N | 04QB5.00 | 04DU5.24 | 2.4 kbit/s, not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.24S | 2.4 kbit/s, with secondary chan., not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.48 | 4.8 kbit/s, not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.48S | 4.8 kbit/s, with secondary chan., not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.96 | 9.6 kbit/s, not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.96S | 9.6 kbit/s, with secondary chan., not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.19 | 19.2 kbit/s, not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.19S | 19.2 kbit/s, with secondary chan., not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.56 | 56.0 kbit/s, not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.56S | 56.0 kbit/s, with secondary chan., not DS0A Level signal |
| LX-N | 04QB5.00 | 04DU5.64 | 64.0 kbit/s, not DS0A Level signal |

### 3.8.3	Unbundled xDSL Capable and Advanced Digital Transport Loop NC/NCI Codes

Table 3-8 lists available CenturyLink NC/NCI code combinations for Unbundled xDSL Capable and Advanced Digital Transport Loops..   The customer specifies the NCIs to communicate to CenturyLink the character of the signals the customer is connecting to the network at each end-point of the copper circuit.  CenturyLink will take into account the NC code and the NCI code when assigning, maintaining and repairing facilities for xDSL.   The associated NC codes require that the service use copper facilities without load coils.  Those facilities shall be free of faults.  The customer has the option to inspect the character of the facilities, e.g. gauge, length, etc. The loops will also be conditioned when requested by the CLEC. CenturyLink has responsibilities to provision the best available loop.

Table 3-12  CenturyLink Unbundled xDSL Capable Loop NC/NCI Code Combinations

|  | NCI Code |  |
| --- | --- | --- |
| NC Code | CenturyLink CO-NI | End-User EU-NI | Description: Application of CenturyLink’s Unbundled loop |
| Advanced digital Transport – Spectrum Management Capable |
| LX-N | 02QB5.001 | 02DU5.001 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management Class 1 |
| LX-N | 02QB5.002 | 02DU5.002 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management Class 2 |
| LX-N | 02QB5.003 | 02DU5.003 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management Class 3 |
| LX-N | 04QB5.003 | 04DU5.003 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management Class 3 |
| LX-N | 02QB5.004 | 02DU5.004 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI T Standard, 1.417 Spectrum Management Class 4 |
| LX-N | 02QB9.005 | 02DU9.005 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard T1.417 Spectrum Management Class 5 |

|  | NCI Code |  |
| --- | --- | --- |
| NC Code | CenturyLink CO-NI | End-User EU-NI | Description: Application of CenturyLink’s Unbundled loop |
| LX-N | 02QB9.006 | 02DU9.006 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management Class 6 |
| LX-N | 02QB5.007 | 02DU5.007 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management Class 7 |
| LX-N | 02QB5.008 | 02DU5.008 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management Class 8 |
| LX-N | 02QB9.009 | 02DU9.009 | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management Class 9 |
| LX-N | 04QB5.00F | 04DU5.00F | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management HDSL4, Technology Specific, Transmission System Per ANSI Standard T1.417 |
| LX-N | 02QB5.00G | 02DU5.00G | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management G.shdsl, Technology Specific, Transmission System Per ANSI Standard T1.417 |
| LX-N | 04QB5.00G | 04DU5.00G | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management G.shdsl, Technology Specific, Transmission System Per ANSI Standard T1.417 |
| LX-N | 02QB5.00S | 02DU5.00S | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management 2B1Q SDSL, Technology Specific, Transmission System Per ANSI Standard T1.417 |
| LX-N | 04QB5.00S | 04DU5.00S | Advanced Digital Transport Loop, Signals at interfaces conform to ANSI Standard, T1.417 Spectrum Management 2B1Q SDSL, Technology Specific, Transmission System Per ANSI Standard T1.417 |

Table 3-13  CenturyLink Unbundled xDSL Loop NC/NCI Code Combinations (Continued)

|  | NCI Code |  |
| --- | --- | --- |
| NC Code | CenturyLink CO-NI | End-User EU-NI | Description: Application of CenturyLink’s Unbundled loop |
| digital SUBSCRIBER line (BASIC Rate ISDN -- DSL) Capable |
| LX-N | 02QC5.OOS | 02IS5.N | Digital subscriber Line with 2B1Q Signaling Format Capable Loop |
| High-bit-rate digital SUBSCRIBER line (HDSL) Capable |
| LX-N | 02QB9.00H | 02DU9.00H | HDSL Capable Loop, Copper Facility ONLY per ANSI T1E1 Technical Report Number 28 |
| LX-N | 04QB9.00H | 04DU9.00H | HDSL Capable Loop, Copper Facility ONLY per ANSI T1E1 Technical Report Number 28 |
| ASYMMETRIC digital SUBSCRIBER line (ADSL) Capable |
| LXR- | 02QB9.00A | 02DU9.00A | Revised Resistance Design (RRD)n Non-Loaded Loop with ANSI T1.413 DMT Signaling Format |
| LXR- | 02QB9.01A | 02DU9.01A | RRD, Non-Loaded Loop with ANSI T1.413 DMT Signaling Format and one POTS Channel |
| LXR- | 02QB9.00C | 02DU9.00C | RRD, Non-Loaded Loop with CAP Signaling Format |
| LXR- | 02QB9.01C | 02DU9.01C | RRD, Non-Loaded Loop with CAP Signaling Format and one POTS Channel |