EASE ASR 3.0 RELEASE CHANGE SUMMARY

# Introduction

This document contains changes to the 3.0 Custom Business Rules/Technical Specifications document as follows:

Drat Version - 7/17/17

- EQ914 – New soft edit to detect the ECCKT ID may be LSR and should not be used on an ASR unless the Project ID is UNETOPLT. The edit does not prevent the ASR from being submitted, but it may appear if there are other errors on the ASR.

- EQ915 – New hard edit for both Legacy Companies preventing the CFA and SCFA fields from containing the same exact value.

- EQ916 – New hard edit for LQ ICSC’s that requires the ASR:ADMIN:UNE field to be populated with Y when the ASR:ADMIN:SPEC field is populated with UNBALL. If the ASR:ADMIN:UNE field is blank, display error message "UNE field required with UNBALL SPEC".

- EQ917 – New hard edit for LQ ICSC’s that requires the ASR:ADMIN:PLU field to be populated with 100 when the ASR:ADMIN:SPEC field is populated with UNBALL. If the ASR:ADMIN:PLU field is not populated with 100, display error message "PLU field must be 100 with UNBALL SPEC".

- EQ918 – New hard edit for LQ ICSC’s that requires the ASR:ADMIN:CC field to be populated when the ASR:ADMIN:SPEC field is populated with UNBALL. If the ASR:ADMIN:CC field is not populated, display error message "CC Field Required with UNBALL SPEC".

Final Version – 8/4/17

- EQ920 – New soft edit for internal purposes to identify Coordinated Access requests. Customers will only see this edit if other errors exist on the PON. This edit does not prevent customers from submitting their order.

- EQ921 – New hard edit for both Legacy Companies preventing Ethernet ECCKTs on Non Ethernet Service Types. This edit requires customers to cancel and reissue with the correct service type.

| Error Code | ASOG Form | Section | Field | Error Message |
| --- | --- | --- | --- | --- |
| EQ914 | ASR | ADMIN | ECCKT | ECCKT field may contain LSR circuit. Validate circuit ID. |
| EQ915 | TRANS | CIR_DETAILS | CFA | CFA and SCFA field may not contain duplicate values. |
| EQ915 | TRANS | CIR_DETAILS | SCFA | CFA and SCFA field may not contain duplicate values. |
| EQ916 | ASR | ADMIN | UNE | UNE field required with UNBALL SPEC |
| EQ917 | ASR | ADMIN | PLU | PLU field must be 100 with UNBALL SPEC |
| EQ918 | ASR | ADMIN | CC | CC field required with UNBALL SPEC |
| EQ920 | ASR | BILL | ACNA | ACNA equals ZZZ. Verify if order is Coordinated Access. |
| EQ921 | ASR | ADMIN | ECCKT | Invalid Service Type for Ethernet services - Cancel and Reissue with correct Service Type |