EASE ASR 4.1 RELEASE Business Rules CHANGE SUMMARY

# Introduction

This document contains changes to the 4.1 Custom Business Rules/Technical Specifications document as follows:

BRMS Business Rules

- EQ62 – New hard edit in EASE that covers both LC and LQ orders and prevents duplicate values in the Location Designator fields on the SALI form.

- Error Code EQ585 – – Deleted this invalid edit from the document as the edit was never implemented.

- Error Code EQ529 – Deleted this invalid edit from the document as the edit was never implemented.

JMS Rules

New JMS Edits:

- CTLV0221 – New hard edit in EASE for LQ only to prevent mismatch of jurisdiction between the PIU field and all RUID IDs on the ASR.

- CTLV0222 – New hard edit in EASE for both LC and LQ to prevent a change of the LTP field on a SUP 3 or SUP 4.

- CTLV0073 – New hard edit in EASE for LQ only to prevent cross LATA ordering on an ASR with EVC and/or SES forms.

- CTLV0223 – New soft edit in EASE for LQ only to coincide with CTLV0203 edits where further investigation is required by the CenturyLink Service Center.  This error does not require any action on the part of customers.

Changed JMS Edits:

- CTLV0073 – Changed Trunk SECLOC and TRUNK MUXLOC edits to cover both LQ and LC; previously was LQ only edit.

- CTLV0140 – Changed edit to apply only on the EVC form for both LQ and LC adding SUP 4 to the edit; previously edit was for SUP 3 LQ only on multiple forms.

- CTLV0203 – Changed edit to apply on Multi-EC and non-Multi-EC ASRs for both LC and LQ and add additional forms to the edit; previously applied only on Multi-EC ASRs.  Also updated Error Message text and Explanation or Solution text.

- CTLV0203 – LC Standalone EVC, LQ Switched Ethernet and LQ End User Switched Ethernet requests have unique Error Messages for the ACTL, EVCSP and PRILOC fields as LQ does not have Multi-EC arrangements for these types of ASRs.

Deleted JMS Edits (deleted as other JMS Edits cover this functionality):

- CTLV0015 – LC only edit on the EVC S-VLAN field.

- CTLV0029 – LQ only edit on the EVC LOSACT field.

- CTLV0043 – LC only edit on the TRUNK CIC field.

- CTLV0044 – LC only edit on the TRUNK ACIC field.

- CTLV0057 – LC only edit on the ASR TQ field.

- CTLV0113 – LC only edit on the TRUNK NC1 field.

- CTLV0141 – LQ only edit on the TRUNK NC1 field.

- CTLV0143 – LQ only edit on the ASR QTY field.

- CTLV0146 – LQ only edit on the SR field on multiple forms.

- CTLV0203 – LQ only edit on cross LATA check for ACTL to SECLOC for TRUNK and TRANSPORT forms.

- CTLV0218 – LC and LQ edit on the NC field on multiple forms.

Documentation only Changes:

- Changed all Form references from WATS to WAL to match ASOG Form description.

BRMS Business Rules

| Error Code | ASOG Form | Section | Field | Error Message | Explanation or solution | Legacy Company |
| --- | --- | --- | --- | --- | --- | --- |
| EQ62 | SALI | ADDR_DETAIL | LD1 | LD values on SALI form cannot be duplicated | When an ASR contains a SALI section, LD1, LD2, and LD3 field values cannot be duplicated. | B |
| EQ62 | SALI | ADDR_DETAIL | LD2 | LD values on SALI form cannot be duplicated | When an ASR contains a SALI section, LD1, LD2, and LD3 field values cannot be duplicated. | B |
| EQ62 | SALI | ADDR_DETAIL | LD3 | LD values on SALI form cannot be duplicated | When an ASR contains a SALI section, LD1, LD2, and LD3 field values cannot be duplicated. | B |

JMS Rules

| Error Code | ASOG Form | Section | Field | Error Message | Explanation or solution | Legacy Company |
| --- | --- | --- | --- | --- | --- | --- |
| CTLV0221 | EVC | UNIMAPPING | RUID | JURISDICTION MISMATCH BETWEEN RUIDS | The PIU data on the ASR indicates a different jurisdiction than indicated by the RUID ID. Please correct the PIU or RUID ID to indicate either interstate or intrastate service. | Q |
| CTLV0222 | ASR | ADMIN | LTP | IF REQUESTED LTP CHANGE IS VALID, PLEASE CANCEL AND REISSUE ASR. | The previous accepted version of the ASR contains a different value in the LTP field. Please alter the current version to match the previous version, or cancel the ASR and resubmit with the new value. | B |
| CTLV0073 | EVC | UNIMAPPING | RUID | RUIDS CANNOT CROSS LATA BOUNDARIES | All RUIDs on the ASR are not in the same LATA. Please correct the incorrect RUID IDs or cancel the ASR. | Q |
| CTLV0073 | EVC | UNIMAPPING | RUID | ADDRESS AND/OR RUIDS CANNOT CROSS LATA BOUNDARIES | All RUIDs and the end user address on the ASR are not in the same LATA. Please correct the incorrect end user address, the incorrect RUID IDs or cancel the ASR. | Q |
| CTLV0073 | TRUNK | SVC_DETAILS | SECLOC | WHEN THERE IS A CFA, ROUTE FROM MUXLOC TO SECLOC CANNOT CROSS LATA BOUNDARIES | The SECLOC provided on the ASR is not in the same LATA as the MUXLOC. Please confirm the LATA associated with the CLLI code or contact the CenturyLink service center to have the CLLI code added/checked in the ordering tables. | B |
| CTLV0073 | TRUNK | SVC_DETAILS | MUXLOC | WHEN THERE IS A CFA, ROUTE FROM MUXLOC TO SECLOC CANNOT CROSS LATA BOUNDARIES | The SECLOC provided on the ASR is not in the same LATA as the MUXLOC. Please confirm the LATA associated with the CLLI code or contact the CenturyLink service center to have the CLLI code added/checked in the ordering tables. | B |
| CTLV0140 | EVC | EVC_DETAIL | NC | NC IS NOT ALLOWED TO BE CHANGED ON A SUP | The previous confirmed version of the ASR contains a different value in NC field. Please alter the current version to match the previous version, or cancel the ASR and resubmit with the new value. | B |
| CTLV0203 | ASR | ADMIN | ACTL | ACTL location ICSC does not match ICSC or OEC ICSC | The ACTL CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the ACTL or contact the CenturyLink service center for assistance. | B |
| CTLV0203 | ASR | ADMIN | ACTL | ICSC Incorrect for ACTL | The ACTL CLLI ICSC must match the ASR ICSC. Please correct the ACTL or contact the CenturyLink service center for assistance. | Q |
| CTLV0203 | EUSA | EUSA | PRILOC | PRILOC location ICSC does not match ICSC or OEC ICSC | The PRILOC ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the PRILOC or contact the CenturyLink service center for assistance. | B |
| CTLV0203 | SES | SALI |  | ICSC Incorrect for Address | The PRILOC SWC ICSC must match the ASR ICSC. Please correct the PRILOC or contact the CenturyLink service center for assistance. | Q |
| CTLV0203 | EUSA | EUSA | SECLOC | SECLOC location ICSC does not match ICSC or OEC ICSC | The SECLOC ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SECLOC or contact the CenturyLink service center for assistance. | B |
| CTLV0203 | EVC | UNIMAPPING | EVCSP | EVCSP location ICSC does not match ICSC or OEC ICSC | The EVCSP ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the EVCSP or contact the CenturyLink service center for assistance. | C |
| CTLV0203 | TRANS | CIR_DETAILS | SECLOC | SECLOC location ICSC does not match ICSC or OEC ICSC | The SECLOC ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SECLOC or contact the CenturyLink service center for assistance. | B |
| CTLV0203 | TRANS | CIR_DETAILS | MUXLOC | MUXLOC location ICSC does not match ICSC or OEC ICSC | The MUXLOC CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the MUXLOC or contact the CenturyLink service center for assistance. | B |
| CTLV0203 | TRANS | CIR_DETAILS | SMUXLOC | SMUXLOC location ICSC does not match ICSC or OEC ICSC | The SMUXLOC CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SMUXLOC or contact the CenturyLink service center for assistance. | B |
| CTLV0203 | TRUNK | SVC_DETAILS | FACTL | FACTL location ICSC does not match ICSC or OEC ICSC | The FACTL CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the FACTL or contact the CenturyLink service center for assistance. | B |
| CTLV0203 | TRUNK | SVC_DETAILS | SECLOC | SECLOC location ICSC does not match ICSC or OEC ICSC | The SECLOC ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SECLOC or contact the CenturyLink service center for assistance. | B |
| CTLV0203 | TRUNK | SVC_DETAILS | MUXLOC | MUXLOC location ICSC does not match ICSC or OEC ICSC | The MUXLOC CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the MUXLOC or contact the CenturyLink service center for assistance. | B |
| CTLV0203 | TRUNK | SVC_DETAILS | SMUXLOC | SMUXLOC location ICSC does not match ICSC or OEC ICSC | The SMUXLOC CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SMUXLOC or contact the CenturyLink service center for assistance. | B |
| CTLV0223 | ASR | ADMIN | ACTL | ACTL location ICSC does not match ICSC or OEC ICSC | The ACTL CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the ACTL or contact the CenturyLink service center for assistance. | Q |
| CTLV0223 | EUSA | EUSA | PRILOC | PRILOC location ICSC does not match ICSC or OEC ICSC | The PRILOC ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the PRILOC or contact the CenturyLink service center for assistance. | Q |
| CTLV0223 | EUSA | EUSA | SECLOC | SECLOC location ICSC does not match ICSC or OEC ICSC | The SECLOC ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SECLOC or contact the CenturyLink service center for assistance. | Q |
| CTLV0223 | TRANS | CIR_DETAILS | SECLOC | SECLOC location ICSC does not match ICSC or OEC ICSC | The SECLOC ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SECLOC or contact the CenturyLink service center for assistance. | Q |
| CTLV0223 | TRANS | CIR_DETAILS | MUXLOC | MUXLOC location ICSC does not match ICSC or OEC ICSC | The MUXLOC CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the MUXLOC or contact the CenturyLink service center for assistance. | Q |
| CTLV0223 | TRANS | CIR_DETAILS | SMUXLOC | SMUXLOC location ICSC does not match ICSC or OEC ICSC | The SMUXLOC CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SMUXLOC or contact the CenturyLink service center for assistance. | Q |
| CTLV0223 | TRUNK | SVC_DETAILS | FACTL | FACTL location ICSC does not match ICSC or OEC ICSC | The FACTL CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the FACTL or contact the CenturyLink service center for assistance. | Q |
| CTLV0223 | TRUNK | SVC_DETAILS | SECLOC | SECLOC location ICSC does not match ICSC or OEC ICSC | The SECLOC ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SECLOC or contact the CenturyLink service center for assistance. | Q |
| CTLV0223 | TRUNK | SVC_DETAILS | MUXLOC | MUXLOC location ICSC does not match ICSC or OEC ICSC | The MUXLOC CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the MUXLOC or contact the CenturyLink service center for assistance. | Q |
| CTLV0223 | TRUNK | SVC_DETAILS | SMUXLOC | SMUXLOC location ICSC does not match ICSC or OEC ICSC | The SMUXLOC CLLI ICSC must match the ASR ICSC or an OEC ICSC code. Please correct the SMUXLOC or contact the CenturyLink service center for assistance. | Q |